## Slide 1: WF on NR MIMO OTA
vivo, CAICT
3GPP TSG-RAN WG4 Meeting #98-e R4-2103913
Electronic Meeting, Jan. 25-Feb. 5, 2021
Agenda item: 11.1.1
Document for: Approval

## Slide 2: Test Method
System implementation of FR2 3D-MPAC system
  Keep the probe locations the same among system implementations at this time, but enhanced implementation or solution can be considered by RAN4 in future
  Further study the MU evaluation to address the FR2 blocking issue
Conclude the agreed 36 test points for FR2 MIMO OTA testing
Usage of gNB beams for FR1 MIMO OTA testing
  Beam1_H, Beam1_v, Beam2_H, Beam2_v are mapped to CE input ports 1, 2, 3 and 4 in 4x4 case and Beam1_H, Beam1_v are mapped to CE input ports 1 and 2 in 2x2 case.
  The beams are not combined in the actual test. The gNB emulator ports are connected to each CE input port, where each port corresponds a channel model realization with one beam.

## Slide 3: System validation
Channel model validation
  For spatial correlation validation, only Vertical validation is required.
  gNB Beams Usage Criteria for FR1 MIMO OTA Channel Model Validation
    Option 1: Beam specific: The two strongest beams are measured separately.
    Option 2: Combined beams: The two strongest beams are combined at the input of the channel emulator for validation of spatial correlation. The PDP validation is done separately for each beam in this case.
    Clarification is needed
  For FR1 and FR2 channel model validation, adopt 40dB threshold for cluster power
  conclude the existing PSP validation procedure with 5cm radius as baseline
  Channel model validation limit
    FR1 PDP: Power [±0.8 dB], delay [±11ns]
    FR1 and FR2 Cross-polarization: V/H [±0.9 dB]
    FR1 and FR2 Temporal correlation:
      Option 1: 0.5λ, [NonPolarized value +/- 0.1 capped at 1];1 λ, [NonPolarized value +/- 0.2]; 1.5λ, [NonPolarized value +/- 0.25]; 2λ, [NonPolarized value +/- 0.2]; 2.5λ and greater, [Below 0.35] (Spirent)
      Option 2: 0.25λ, [NonPolarized value +/- 0.05]; 0.5λ, [NonPolarized value +/- 0.05]; 1 λ, [NonPolarized value +/- 0.075]l; 1.5λ, [NonPolarized value +/- 0.1]; 2λ, [NonPolarized value +/- 0.1]; 2.5λ and greater, [NonPolarized value +/- 0.2] (Keysight)

## Slide 4: Test Parameters for requirements
Test Parameters for FR1 requirements
  RAN4 confirms that the CDL-C UMa channel model is adopted to define FR1 4x4 MIMO OTA requirements
  For FR1 2x2 MIMO OTA requirements, the channel model is FFS. Candidate options are: CDL-A UMi, CDL-C UMa, CDL-C UMi. Other options are not precluded (vivo, OPPO, Samsung, Huawei, Qualcomm, CAICT)
  PRS-EPRE-MAX for band frequency <3GHz, 40MHz bandwidth
    Option 1: -83dBm/30kHz
    Option 2: -80dBm/15kHz (-77dBm/30kHz)
    Option 3: [-80dBm/30kHz], power validation results from test labs are encouraged
  PRS-EPRE-MAX for band frequency >3GHz, 10MHz and 40MHz bandwidth needs further study
    When define the maximum downlink power, the path loss induced by different channel models need to be considered
  Minimum number of subframe for FR1 MIMO OTA testing
    Option 1: 10k FR1; further check the impacts on bands below 1GHz (CAICT,vivo,OPPO,Samsung,Xiaomi,Huawei, [QC])
    Option 2: 10k for bands >1GHz, [20k] for bands <1GHz ([KS]?)

## Slide 5: NR MIMO OTA requirements
Figure of Merit for NR MIMO OTA requirements
  For FR1 MIMO OTA performance requirements:
    Restriction of Pmode at 70%TP for 40MHz CHBW.
      For 40MHz CHBW, the 11 of total 12 PMODE should reach 70%TP as a starting point
    Additional restriction of Pmode for 10MHz and 40MHz CHBW.
      Adopt Pmode at 90%TP as an additional restriction
        Option 1: 70% TP: all 12; 90% TP: 11 of 12 (QC)
        Option 2: 70% TP: 11 of 12 (agreed); 90% TP [TBD] of 12;
  For FR2 MIMO OTA performance requirements:
    How to treat the orientations that cannot reach 70% TP
      the missing points can not reach 70%TP, should not be considered into the CCDF curve for FR1 MASC calculation
      additional criterion on how to treat the number of failing points should be further studied

## Slide 6: Next steps
  Further study the proper Channel model for FR1 2x2 MIMO OTA requirements
  Discuss the pass/fail limit and reference figure of channel model validation
  Further discuss testing parameters for requirements (e.g. Maximum downlink power for bands>3GHz)
  Further discuss the Figure of Merit for FR1 and FR2
  Measurement results of FR1 or FR2 UEs are encouraged for discussion
  Channel model validation results for FR2 channel models are encourages
  Analysis on MU evaluation of FR2 blocking issue
  FR2 simulation results of UE performance are encouraged