## Slide 1: WF on NR MIMO OTA
vivo, CAICT
3GPP TSG-RAN WG4 Meeting #98-e R4-2103913
Electronic Meeting, Jan. 25-Feb. 5, 2021
Agenda item: 11.1.1
Document for: Approval

## Slide 2: Test Method
System implementation of FR2 3D-MPAC system
  Keep the probe locations the same among system implementations at this time, but enhanced implementation or solution can be considered by RAN4 in future
  Further study the MU evaluation how to address the FR2 blocking issue for UE which not use repositioning approach
Conclude the agreed 36 test points for FR2 MIMO OTA testing
Usage of gNB beams for FR1 MIMO OTA testing :
  Beam1_H, Beam1_v, Beam2_H, Beam2_v are mapped to CE input ports 1, 2, 3 and 4 in 4x4 case and Beam1_H, Beam1_v are mapped to CE input ports 1 and 2 in 2x2 case. -> further update
  The beams are not combined in the actual test. The gNB emulator ports are connected to each CE input port, where each port corresponds a channel model realization with one polarization of one beam.
Notes: Keysight: We believe no MU evaluation needed, the blocking issue belong to QoQz.
Vivo: we think it’s a new issue specific for FR2 OTA test, we would like to study further for this issue.
Oppo: Similar view as vivo. We would like to further study the impact on the implementation.
Samsung: Similar view as vivo. Unlike SISO, we have multiple probes and worth to further study.
Qualcomm: Similar view as Samsung, the evaluation only needed for UE which not use repositioning approach.
Huawei: For 2X2 cases, only 1 beam used ? In TR, we specify two strongest beams applied.
vivo: This is coming from one TE vendor, can be treated as a example, not sure other TE vendors feedback ? Same question as Huawei.
Keysight: For NR FR1 MIMO OTA, 2 strongest transmitted beams from v and H polarization during test .
CAICT: combined beams used for spatial correlation validation only , or also applied for XPR as well?
Oppo: We support option 2.
Huawei: 2 beams selected for 4X4 and 1 strongest selected for 2X2.
Keysight: in our paper we present the curves, we are checking which approach used, these beams could be separate.
Sprient: Our preference to have single set assumption for all factors of validation including XPR, PDP, spatial correlation. We prefer have simple generic assumption for used.
MVG: Share similar view as Spirent, we need to align the assumption, since throughput is key metric. Channel model validation assumption should be one single assumption.
Keysight: We can do individual beam validation, meanwhile combine beams approach can save time for spatial correlation validation.

## Slide 3: System validation
Channel model validation
  For spatial correlation validation, only Vertical validation is required.
  gNB Beams Usage Criteria for FR1 MIMO OTA Channel Model Validation
    Option 1: Beam specific: The two strongest beams are measured separately applied for all channel model validation factors (baseline)
    Option 2: Combined beams: The two strongest beams are combined at the input of the channel emulator for validation of spatial correlation. The PDP validation is done separately for each beam in this case.
    Option 3: Combined beams for all channel model validation including PDP, spatial correlation, XPR , Doppler
    Clarification is needed
  For FR1 and FR2 channel model validation, adopt 40dB threshold for cluster power
    Further study the impact on UE throughput performance with CDLA channel model for FR2
  Conclude the existing PSP validation procedure with 5cm radius as baseline
  Channel model validation limit
    Further discuss and define the reference before RAN4 specify the actual values
    FR1 PDP: Power [±0.8 dB], delay [±11ns]
    FR1 and FR2 Cross-polarization: V/H [±0.9 dB]
    FR1 and FR2 Temporal correlation:
      Option 1: 0.5λ, [NonPolarized value +/- 0.1 capped at 1];1 λ, [NonPolarized value +/- 0.2]; 1.5λ, [NonPolarized value +/- 0.25]; 2λ, [NonPolarized value +/- 0.2]; 2.5λ and greater, [Below 0.35] (Spirent)
      Option 2: 0.25λ, [NonPolarized value +/- 0.05]; 0.5λ, [NonPolarized value +/- 0.05]; 1 λ, [NonPolarized value +/- 0.075]l; 1.5λ, [NonPolarized value +/- 0.1]; 2λ, [NonPolarized value +/- 0.1]; 2.5λ and greater, [NonPolarized value +/- 0.2] (Keysight)

## Slide 4: Test Parameters for requirements
Test Parameters for FR1 requirements
  RAN4 confirms that the CDL-C UMa channel model is adopted to define FR1 4x4 MIMO OTA requirements
  For FR1 2x2 MIMO OTA requirements, the channel model is FFS. Candidate options are: CDL-A UMi, CDL-C UMa, CDL-C UMi. Other options are not precluded (vivo, OPPO, Samsung, Huawei, Qualcomm, CAICT)
  PRS-EPRE-MAX for band frequency <3GHz, 40MHz bandwidth
    Option 1: -83dBm/30kHz
    Option 2: -80dBm/15kHz (- [-77dBm/30kHz] (starting point)
    Option 3: -80dBm/30kHz, power validation results from test labs are encouraged
    The value is pending on further verification and confirmation from TE vendors/Test labs for the feasibility
    Further discuss and revise the value not excluded
  PRS-EPRE-MAX for band frequency >3GHz, 10MHz and 40MHz bandwidth needs further study
    When define the maximum downlink power, the path loss induced by different channel models need to be considered
  Minimum number of slots for FR1 MIMO OTA testing
    Option 1: 10k FR1; further check the impacts on bands below 1GHz (CAICT,vivo,OPPO,Samsung,Xiaomi,Huawei)
    Option 2: 20k for 30kHz SCS/10k for 15kHz SCS for bands >1GHz, [20k] for 15kHz SCS for bands <1GHz (KS,QC,MVG) (This is the recommendation for both test lab alignments and UE performance requirements introduction)
    Test labs are encouraged to bring more analysis/measurement results with different number of slots for comparison purpose
Notes: Samsung/Huawei: We should maintain the same PSD for 10MHz and 40MHz CHBW.
Oppo: TE vendors feedback encouraged
vivo: I can understand the concern from TE, Test lab maybe have some concern for the feasibility.
MVG/QC/Keysight: We need to check with more results for multi UEs and for multi bands.
vivo: 10k already used in CCSA and means 20k slots for 30kHz. This is the tradeoff for saving test time.

## Slide 5: NR MIMO OTA requirements
Figure of Merit for NR MIMO OTA requirements
  For FR1 MIMO OTA performance requirements:
    Restriction of Pmode at 70%TP for 40MHz CHBW.
      For 40MHz CHBW, the 11 of total 12 PMODE should reach 70%TP as a starting point based on the current assumption of PRS-EPRE-MAX value
    Additional restriction of Pmode for 10MHz and 40MHz CHBW.
      Adopt Pmode at 90%TP as an additional restriction
        Option 1: 70% TP: all 12; 90% TP: 11 of 12 (QC)
        Option 2: 70% TP: 11 of 12 (agreed); 90% TP [TBD] of 12 as starting point
        Companies are encourage to bring more analysis and measurement data.
  For FR2 MIMO OTA performance requirements:
    How to treat the orientations that cannot reach 70% TP
      the missing points can not reach 70%TP, should not be considered into the CCDF curve for FR1 MASC calculation
      additional criterion on how to treat the number of failing points should be further studied
Notes: QC: We would like to align with LTE as same.
Vivo: The situation in NR is different compared for LTE for performance aspect.

## Slide 6: Next steps
  Further study the proper Channel model for FR1 2x2 MIMO OTA requirements
  Discuss the pass/fail limit and reference figure of channel model validation
  Further discuss testing parameters for requirements (e.g. Maximum downlink power for bands>3GHz)
  Further discuss the Figure of Merit for FR1 and FR2
  Measurement results of FR1 or FR2 UEs are encouraged for discussion
  Channel model validation results for FR2 channel models are encourages
  Analysis on MU evaluation of FR2 blocking issue
  FR2 simulation results of UE performance are encouraged