## Slide 1: WF on NR-U RRM Core Requirements all agreements in RAN4#98-e in email thread: [98e][205] NR_unlic_RRM_1
Ericsson
3GPP TSG-RAN WG4 Meeting #98-e R4-210xxxx
Electronic Meeting, Jan. 25 - Feb. 5, 2021
Agenda Items: 7.1.5

## Slide 2
Agreements from the 1st GTW session
Agreements from the 1st round
Agreements from the 2nd round

## Slide 3: General
Further NR-U terminology clarification
  General principles to address the impact of DRX, MGRP, CSSF, etc. on the availability definition:
    When configured with measurements in measurement cycles: the UE is not required to determine the availability of SMTC occasions more frequent than once per measurement cycle.
    For measurements in gaps: The UE is not required to determine the availability of SMTC occasions more frequent than once during MGRP.
    For measurement requirements with DRX: the UE is not required to determine the availability of SMTC occasions more frequent than once per DRX cycle.
    For RLM/CBD: The UE is not required to determine the availability of SSB occasions more frequent than once per DRX cycle length, when configured with DRX.
    FFS: how to account CSSF impact
      Option 1: For measurement requirements with CSSF: The UE is not required to determine the availability of SMTC occasions more frequent than what is required by CSSF
    A common approach (but applicable for the relevant issues among DRX, MGRP, etc.) shall be used for all measurements
  FFS: how to capture the above in 38.133 and the level of details

## Slide 4: Random Access - General
Supplementary UL
  Do not define RRM requirements for random access in supplementary uplink
    Note: The respective requirements can be discussed in the future when the corresponding RF band combinations including NR-U and SUL are introduced and also subject to the outcome of RAN1 discussion
Specification structure for RA requirements in 38.133
  The specification structure for clause 6.2.2A shall follow the structure of clause 6.2.2, but unnecessary sections can be omitted (do not use void for this purpose)

## Slide 5: Random Access – 2-step RA
Define requirements for 2-step RA in Rel-16 NR-U
Specification structure
  Create section 6.2.2A.3 for 2-step RA in NR-U
    6.2.2A.3 Requirements for 2-step RA type
      6.2.2A.3.1 Contention based random access
        6.2.2A.3.1.1 Correct behaviour when transmitting MsgA
        6.2.2A.3.1.2 Correct behaviour when receiving MsgB
        6.2.2A.3.1.3 Correct behaviour when not receiving MsgB
      6.2.2A.3.2 Non-contention based random access
        6.2.2A.3.2.1 Correct behaviour when transmitting MsgA
        6.2.2A.3.2.2 Correct behaviour when receiving MsgB
        6.2.2A.3.2.3 Correct behaviour when not receiving MsgB

## Slide 6: Random Access – 2-step RA (cont.)
UE behaviour with respect to lbt-FailureRecoveryConfig:
  When lbt-FailureRecoveryConfig is configured and is capable of ul-LBT-FailureDetectionRecovery [2]:
    The UE shall perform LBT failure detection and recovery procedure as outlined in Clause 5.21.2 of TS 38.321.
    For 2-step RA, if UL LBT failure is indicated by the lower layers for a Random-Access Preamble transmission, the UE shall:
      Cancel the transmission of the msgA payload on the associated PUSCH resource
      Perform the Random-Access Selection procedure and as specified in Clause 5.1.2a of TS 38.321 for 2-step RA.
  When lbt-FailureRecoveryConfig is not configured or is not capable of ul-LBT-FailureDetectionRecovery [2]:
    For 2-step RA, if UL LBT failure is indicated by the lower layers, the UE shall
      Cancel the transmission of the msgA payload on the associated PUSCH resource
      Increment the PREAMBLE_TRANSMISSION_COUNTER by 1
      The UE shall again perform the Random Access Resource selection procedure if PREAMBLE_TRANSMISSION_COUNTER < preambleTransMax + 1, as specified in clause 5.1.3a in TS38.321.
      If the Random Access Procedure is not complete and the UE is configured with msgA-TransMax then, as specified in clause 5.1.3a in TS 38.321 [7], the UE shall perform the Random Access Resource selection procedure with 4-step RA type provided that PREAMBLE_TRANSMISSION_COUNTER = msgA-TransMax + 1

## Slide 7: Random Access – 4-step RA
Specification structure
  6.2.2A.1 Introduction
  6.2.2A.2 Requirements for 4-step RA type
    6.2.2A.2.1 Contention based random access
      6.2.2A.2.1.1 Correct behaviour when transmitting Random Access Preamble
      6.2.2A.2.1.2 Correct behaviour when receiving Random Access Response
      6.2.2A.2.1.3 Correct behaviour when not receiving Random Access Response
      6.2.2A.2.1.4 Correct behaviour when receiving an UL grant for msg3 retransmission
      6.2.2A.2.1.5 Correct behaviour when receiving a message over Temporary C-RNTI
      6.2.2A.2.1.6 Correct behaviour when contention Resolution timer expires
    6.2.2A.2.2 Non-contention based random access
      6.2.2A.2.2.1 Correct behaviour when transmitting Random Access Preamble
      6.2.2A.2.2.2 Correct behaviour when receiving Random Access Response
      6.2.2A.2.2.3 Correct behaviour when not receiving Random Access Response

## Slide 8: Random Access – 4-step RA (cont.)
UE behaviour with respect to lbt-FailureRecoveryConfig:
  When lbt-FailureRecoveryConfig is configured and is capable of ul-LBT-FailureDetectionRecovery [2]:
    The UE shall perform LBT failure detection and recovery procedure as outlined in Clause 5.21.2 of TS 38.321.
    For 4-step RA, if UL LBT failure is indicated by the lower layers for a Random-Access Preamble transmission, the UE shall:
      Perform the Random-Access Selection procedure again as specified in Clause 5.1.2 of TS 38.321 for 4-step RA
  When lbt-FailureRecoveryConfig is not configured or is not capable of ul-LBT-FailureDetectionRecovery [2]:
    For 4-step RA, if UL LBT failure is indicated by the lower layers, the UE shall
      Increment the PREAMBLE_TRANSMISSION_COUNTER by 1 and perform the procedure as outlined in Clause 5.1.3 in TS 38.321

## Slide 9: Random Access: Applicability rules for RA in other RRM requirements
Update the applicability rules for 2-step RA and 4-step RA in 36.133 and 38.133 such that:
  2-step RA and 4-step RA without CCA apply to RRM requirements where the RA is sent to a target cell NOT subject to CCA and
  2-step RA and 4-step RA with CCA apply to RRM requirements where the RA is sent to a target cell subject to CCA
The list of impacted RRM requirements in TS 36.133:
No. | Clause | RRM requirements involving RA to NR target cell NOT subject to CCA
1 | 5.3.4 | E-UTRAN - NR FR1 handover requirements
2 | 5.3.5 | E-UTRAN - NR FR2 handover requirements
3 | 6.3.4 | RRC connection release with redirection to NR requirements
4 | 7.31.2 | PSCell addition delay requirements
 |  | RRM requirements involving RA to NR target cell subject to CCA
5 | 5.3.4A | E-UTRAN - NR FR1 handover requirements
6 | 6.3.2.5 | RRC connection release with redirection to NR requirements
7 | 7.31A.2 | PSCell addition delay requirements

## Slide 10: Random Access: Applicability rules for RA in other RRM requirements (cont.)
The list of impacted RRM requirements in TS 38.133:
No. | Clause | RRM requirements involving RA to NR target cell NOT subject to CCA
1 | 6.1 | Handover requirements except for clauses 6.1.2 and 6.1B
2 | 6.2.1 | RRC connection re-establishment requirements
3 | 6.2.3.2.1 | RRC connection release with redirection to NR requirements
4 | 7.1 | UE transmit timing requirements
5 | 8.9.2 | PSCell addition delay requirements
6 | 8.11 | PSCell change requirements
7 | 8.11B | Conditional PSCell change requirements
 |  | RRM requirements involving RA to NR target cell subject to CCA
8 | 6.1B | Handover requirements
9 | 6.2.1A | RRC connection re-establishment requirements
10 | 6.2.3.2.3 | RRC connection release with redirection to NR requirements
11 | 7.1 | UE transmit timing requirements

## Slide 11: SI reading with LBT in RRC release with redirection, RRC re-establishment, and paging interruption
FFS: defining a requirement on the minimum number of available samples for SI reading during the RRC release with redirection, RRC re-establishment, and paging interruption at a low operation point, e.g., at -3 dB
For NR-U RRM test cases, TSI,CCA is set as follows, considering the agreed limited set of values for PCCA_DL:
  TSI,CCA(PCCA_DL = 0.25) = X1*TDBT
  TSI,CCA(PCCA_DL = 0.5) = X2*TDBT
  TSI,CCA(PCCA_DL = 0.75) = X3*TDBT
  X1=[35], X2=[17], X3=[10]
  No other margins are needed

## Slide 12: SCell Activation: Interruptions
General
  Further discuss the following 2 types of interruptions
    Interruptions on any active cell in the same band with the SCell being activated
    Interruptions on any active cell outside the band with the SCell being activated
Interruptions for inter-band CA
  For any active cell in the same band with the SCell being activated, the interruption requirements (i.e. number of interruptions and starting point of an interruption) for intra-band CA apply
  For any active cell outside the band with the SCell being activated, the interruption requirements are FFS
  For the known target SCell:
    FFS: a single interruption applies, regardless of whether the victim cell is on an intra-band or inter-band CC
  For unknown target SCell:
    Scenario with victims on inter-band CCs only (no intra-band victim serving cells): single interruption
    Scenario with victims on inter-band CCs and intra-band CCs: FFS

## Slide 13: SCell Activation: sCellDeactivationTimer is NOT configured
Applicability of SCell activation requirements when sCellDeactivationTimer is NOT configured
    Option 1 (E///, QC, Apple, Huawei/HiSilicon):
      The SCell activation requirements for NR-U do not apply when the sCellDeactivationTimer is not configured, when the SCell activation delay exceeds some pre-defined time (e.g., equivalent or comparable to the longest possible value of sCellDeactivationTimer).
    Option 2 (Nokia, ZTE, MTK):
      SCell activation delay requirements are applicable in Scenario A (CA with NR PCell and NR SCell) with any LBT type and in Scenario B and C (E-UTRAN-NR-U DC/SA NR-U) with LBT type 2C. Requirements are also applicable in all scenarios, if the UE does not experience any UL LBT failures during SCell activation/deactivation.
      SCell activation delay requirements are applicable when sCellDeactivationTimer is not configured also in Scenarios B and C (EN-DC and SA) LBT types other than 2C.
    Option 3 (possible compromise solution):
      SCell activation delay requirements are applicable in Scenario A (CA with NR PCell and NR SCell) with any LBT type and in Scenario B and C (E-UTRAN-NR-U DC/SA NR-U) with LBT type 2C. Requirements are also applicable in all scenarios, if the UE does not experience any UL LBT failures during SCell activation/deactivation.
      For all other scenarios the SCell activation requirements for NR-U do not apply when the sCellDeactivationTimer is not configured, when the SCell activation delay exceeds some pre-defined time (e.g., equivalent or comparable to the longest possible value of sCellDeactivationTimer).

## Slide 14: RLM
The RLM requirements under CCA in clause 8.1A apply regardless of whether CO-DurationPerCell is configured or not [TS 38.213]
  No need to explicitly capture this in TS 38.133

## Slide 15: Beam Management: Link Recovery
The link recovery requirements under CCA in clause 8.5A apply regardless of whether CO-DurationPerCell is configured or not [TS 38.213]
  No need to explicitly capture this in TS 38.133

## Slide 16: Measurement Requirements: L1-RSRP
Semi-persistent L1-RSRP measurement reporting
  Capture the following sentence in TS38.133 9.5A.3.2:
    When CCA is used on target frequency, the UE shall stop semi-persistent L1-RSRP measurement reports on PUCCH, when the UE cannot transmit a PUCCH with HARQ-ACK information in slot n corresponding to the PDSCH carrying the deactivation command
The L1-RSRP requirements under CCA in clause 9.5A apply regardless of whether CO-DurationPerCell is configured or not [TS 38.213]
  No need to explicitly capture this in TS 38.133

## Slide 17: Measurement Requirements: SFTD
NR-U bands in SFTD accuracy requirements in TS 36.133:
  Add NR unlicensed bands to SFTD accuracy requirements in TS 36.133 clause 9.1.27

## Slide 18: Measurement Requirements: CSSF
CSSF outside measurement gaps for carrier frequency with CCA
  CSSF outside gaps (CSSFoutside_gap,i ) should increase by one if one MO configured both RMTC (for RSSI measurement) and SMTC (for SSB-based measurement)
CSSF within measurement gaps for carrier frequency with CCA
  CSSF within measurement gaps (CSSFwithin_gap,i ) needs also to be adapted to account for inter-frequency RSSI/CO measurements and intra-frequency RSSI/CO measurements with gaps
  Regarding the CSSF within measurement gaps (CSSFwithin_gap,i ), a MO should be counted twice, if the MO is configured with both RMTC and SMTC which are candidates to be measured in gap j where the measurement object i is also a candidate

## Slide 19: Other
PL-RS switching for Rel-16 NR-U
  Do not include RRM requirements for PL-RS switching in Rel-16 NR-U
Rel-16 CGI reading for Rel-16 NR-U
  Do not include RRM requirements for the Rel-16 CGI reading feature in Rel-16 NR-U