## Slide 1: WF on UE co-existence between n40 and n41
Agenda item: 7.19.3
Source: Huawei, HiSilicon, CMCC…
3GPP TSG-RAN WG4 Meeting # 98-e R4-2103157
Electronic Meeting, 25th January– 5th Febuary, 2021

## Slide 2: Background
This WF[1] which focus on single carrier band operation was approved to provide some assumptions.
Based on the WF, companies provided some results and analysis [2][3][4]. The results and analysis is based on the n41 full frequency range.
FFS for for n41 intra-band UL CA.
For n40->n41, it seems more discussions in 2nd round are needed especially the filter rejection assumption, whether 20dB or 30dB is a good baseline;
For n41->n40, it seems there is possibility of agreeing on the emission requirement, i.e. [-40dBm/MHz];

## Slide 3: WF
  It’s proposed that spurious emissions for UE-to-UE co-existence for single carrier between band n40 and n41 will be specified since Rel-16 as below.
    To introduce [-40 to -50] dBm/MHz spurious emission requirements for band n41 frequency range when band n40 transmitting power.
    To introduce [-40] dBm/MHz spurious emission requirements for band n40 frequency range when band n41 transmitting power.

## Slide 4: Reference
[1] R4-2016831, WF on unsynchronized NW between n40 and n41, Huawei
[2] R4-2101175, n40-n41 Coexistence, Qualcomm Incorporated
[3] R4-2101806, Discussion on spurious emission about UE co-existence between band n40 and n41, Huawei, HiSilicon, CMCC
[4] R4-2102929, UE-UE Coexistence for Asynchronous n40 n41 Networks, Skyworks Solutions Inc