## Slide 1: WF on Non-default RX-TX frequency separation
Qualcomm, ...
3GPP TSG-RAN WG4#98-e Meeting R4-2103158
Electronic Meeting, 25th Jan – 5th Feb, 2021

## Slide 2: Background
For frequency bands using a single duplexer the TX-RX separation can have a wide range of values as each TX and RX band has continuous coverage over the entire frequency range
Bands where the frequency gap between TX and RX bands is very narrow it is not always possible to implement duplex filters over the full frequency band [1]
A solution is to use several narrow duplex filters to cover the entire frequency range. Fig 1 illustrates a 2 filter implementation where either filter set a or b is selected depending on the channel in use.
The split duplexer block diagram (fig 2) illustrates that only one of the filters A or B is connected to the antenna at a given time. Therefore there is a functional limitation on the TX-RX spacing that can be used
The default TX-RX separations defined in 5.4.4-1 are commonly accepted values which can be modified if desired. The SIBs FrequencyInfoUL and FrequencyInfoDL can set the UL and DL frequencies independently. Hence the TX-RX duplexer spacing can be changed from the values given in 5.4.4-1.
In split band implementations not all TX-RX spacings can be supported. The TX-RX spacing must be chosen carefully so as to keep the transmission/receiver bands within the UL/DL frequency ranges of the individual narrow BW duplexers
Figure 1 Implementation using two narrow band duplex filters
Figure 2 Split duplexer block diagram

## Slide 3: WF on Non-default RX-TX frequency separation
For n28 and n74 we propose adding the following notes in table 5.4.4-1:
  Limit the applicable TX-RX spacing for n28 to 55 MHz plus any frequency deviation of ΔFTX-RX due to UL/DL BW asymmetry that may be introduced in the future.
  Limit the applicable TX-RX spacing for n74 to 48 MHz plus any frequency deviation of ΔFTX-RX due to UL/DL BW asymmetry that may be introduced in the future.

## Slide 4: References
# | TDoc | Title | Source | Type | Agenda item
1 | R4-21002904 | Non-default RX-TX Frequency Separation Values and split band duplexers | Qualcomm | other | 7.19.3