## Slide 1: WF on the introduction of band n67
Ericsson
R4-2103218
3GPP TSG-RAN WG4 Meeting # 98-e
Electronic Meeting, 25 Jan - 5 Feb., 2021

## Slide 2: Band n67 - System parameters agreement
Band definition
Supported channel BWs
Channel arrangement
NR operating band | Uplink (UL) operating band BS receive / UE transmit FUL,low – FUL,high | Downlink (DL) operating band BS transmit / UE receive FDL,low – FDL,high | Duplex mode
n67 | N/A | 738-758MHz | SDL
NR band / SCS / BS channel bandwidth |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NR Band | SCS kHz | 5 MHz | 10 MHz | 15 MHz | 20 MHz | 25 MHz | 30 MHz | 40 MHz | 50 MHz | 60 MHz | 70 MHz | 80 MHz | 90 MHz | 100 MHz
 | 15 | Yes | Yes | Yes | Yes |  |  |  |  |  |  |  |  | 
n67 | 30 |  | Yes | Yes | Yes |  |  |  |  |  |  |  |  | 
 | 60 |  |  |  |  |  |  |  |  |  |  |  |  | 
NR operating band | ΔFRaster (kHz) | Uplink Range of NREF (First – <Step size> – Last) | Downlink Range of NREF (First – <Step size> – Last)
n67 | 100 | - | 147600– <20> – 151600
NR operating band | SS Block SCS | SS Block pattern1 | Range of GSCN (First – <Step size> – Last)
n67 | 15 kHz | Case A | 1850 – <1> – 1888

## Slide 3: Band n67 – BS Tx requirements agreement
OBUE
  n67 shall be added to the list of bands for Wide Area cat B option 1 limits for bands below 1GHz, in clause 6.6.4.2.2
Spurious
  Spurious: Band n67 shall be added to the coexistence spurious emissions limits, table 6.6.5.2.3-1.
System type for NR to co-exist with | Frequency range for co-existence requirement | Basic limits | Measurement bandwidth | Note
E-UTRA Band 28 or NR Band n28 | 758 – 803 MHz | -52 dBm | 1 MHz | This requirement does not apply to BS operating in band n20, n67 or n28.
 | 703 – 748 MHz | -49 dBm | 1 MHz | This requirement does not apply to BS operating in band n28, since it is already covered by the requirement in clause 6.6.5.2.2. For BS operating in band n67, it applies for 703 MHz to 736 MHz.
E-UTRA Band 67 or NR band n67 | 738 – 758 MHz | -52 dBm | 1 MHz | This requirement does not apply to BS operating in Band n28 or n67.
NR Band n83 | 703 – 748 MHz | -49 dBm | 1 MHz | This requirement does not apply to BS operating in band n28, since it is already covered by the requirement in clause 6.6.5.2.2. For BS operating in Band n67, it applies for 703 MHz to 736 MHz.

## Slide 4: Band n67 – BS Rx requirements agreement
No impact on Rx requirements when introducing band n67.

## Slide 5: Band n67 – UE Tx requirements agreement
No impact on Tx requirements when introducing band n67.

## Slide 6: Band n67 – UE Rx requirements agreement
REFSENS
Operating band / SCS / Channel bandwidth / Duplex-mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NR Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | 50 MHz (dBm) | 60 MHz (dBm) | 70 MHz (dBm) | 80 MHz (dBm) | 90 MHz (dBm) | 100 MHz (dBm) | Duplex Mode
n67 | 15 | -100.0 | -96.8 | -95.0 | -93.8 |  |  |  |  |  |  |  |  |  | SDL
 | 30 |  | -97.1 | -95.1 | -94.0 |  |  |  |  |  |  |  |  |  | 
Operating band / SCS / Channel bandwidth / Duplex-mode |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
NR Band | SCS kHz | 5 MHz (dBm) | 10 MHz (dBm) | 15 MHz (dBm) | 20 MHz (dBm) | 25 MHz (dBm) | 30 MHz (dBm) | 40 MHz (dBm) | 50 MHz (dBm) | 60 MHz (dBm) | 70 MHz (dBm) | 80 MHz (dBm) | 90 MHz (dBm) | 100 MHz (dBm) | Duplex Mode
n67 | 15 | 15 | 25 | 251 | 251 |  |  |  |  |  |  |  |  |  | SDL
 | 30 | 30 |  | 101 | 101 |  |  |  |  |  |  |  |  |  |