## Slide 1: WF on introduction of lower 6GHz NR unlicensed operation for Europe
RAN4
Nokia, Qualcomm, Charter Communications Inc, …

## Slide 2: General - Band plan
Unlicensed operation in the range 5945-6425 MHz can be introduced by:
  Option 1: Re-using already defined band n96
    FFS if additional notes and/or clarifications are needed. Regional specific requirements to be included in relevant specifications.
  Option 2: Defining a new band n[xx]
    On top of specific requirements provided by ECC, the new band shall reuse requirements already defined for n96, where possible.
NR-ARFCN and GSCN already defined for n96 should be re-used in the frequency range applicable to 6GHz NR unlicensed operation in Europe. This is independent if n96 is reused or a new band is defined.

## Slide 3: General - LPI and VLP deployment
LPI devices to be supported by 3GPP Specifications
VLP devices can be supported by the 3GPP specification, VLP deployments and devices are subject to further checking of regulations
0 dBi antenna gain is assumed for the purpose of deriving 3GPP specifications on MOP, PSD, and ASE for LPI deployments and, if introduced, also VLP deployments.
VLP deployment and device types are subject to further checking of regulations

## Slide 4: UE RF - A-MPR assumptions
A-MPR evaluation shall be performed with the following assumptions:
  A-MPR for PC5 is assessed using band n96 PC5 definitions for VLP and LPI device A-MPR.
  No filter rejection is assumed <5935 MHz and >6425MHz for spurious emissions
  Same PA model and calibration setpoint from Band n96 is to be used.
  A-MPR for other power classes are to be added at a later stage.
  A-MPR studies for PC5 are to be compared and, if possible, decided at next RAN4 meeting.

## Slide 5: UE RF - NS definition
NS shall be defined corresponding to LPI deployments and if introduced also VLP deployments.
The currently, by ECC, defined OOB limit at -45 dBm/MHz for VLP shall be used. If/when a new limit is introduced by ECC the NS(s) will be revised accordingly.

## Slide 6: BS RF -
FFS if ΔfOBUE/ ΔfOOBB should follow n46 or n96
FFS if there is impact to BS maximum output power clause or the current statement that it shall conform to regional regulations is sufficient.
FFS if there is impact to REFSENS requirement