## Slide 1: WF on RF architecture and requirements for PC2 intra-band UL contiguous CA
Huawei, HiSilicon, []
R4-2103231
3GPP TSG-RAN WG4 #98-e
Jan 25 – Feb 05, 2021
Electronic meeting

## Slide 2: WF1: Baseline RF architecture
Agreement :
A single TX PC2 PA (200MHz 1LO) is the baseline to develop MPR and A-MPR requirement
In parallel, also assess the two other cases: 1) 2 100MHz PC2 PA; 2) 2 200MHz PC3 PA
It is preferred to define 1 set of MPR and A-MPR requirements. Final decisions are FFS

## Slide 3
WF2: RF requirement
Agreement:
For PC2 intra-band UL contiguous CA with 2PA architecture, the emission requirement is defined as the sum from both UE transmit antenna connectors.