## Slide 1: WF on RF requirements for Rel-17 Tx switching enhancements
3GPP TSG-RAN WG4 Meeting #98e
Electronic Meeting, 25 Jan - 5 Feb, 2021
Agenda: 12.2.2.2, 12.2.2.3
R4-2103235
China Telecom

## Slide 2: Background
  Two topics in Rel-17 FR1 WI are covered in the WF
  Topic #1: 2Tx-2Tx switching between carrier 1 and carrier 2 for SUL and UL CA
  Topic #2: 1Tx-2Tx and 2Tx-2Tx switching between band A (1 carrier) and band B (carrier 2+3) for SUL and UL CA
  Note: latest WID in RP-202799.
  WF approved in previous meeting
  RAN4 #97e, R4-2017815

## Slide 3: WF on applicability of DL interruption
There is no need to differentiate the DL interruption applicability between Rel-16 1Tx-2Tx switching and Rel-17 Tx switching scenarios, which means that “DL interruption allowed” specified in existing TS 38.101-1 should also be applied to the Rel-17 Tx switching scenarios including:
  2Tx-2Tx switching between carrier 1 and carrier 2
  1Tx-2Tx and 2Tx-2Tx switching between band A (carrier 1) and band B (carrier 2+3)

## Slide 4: Clarification on understanding of the transmission power in case 3
It is common understanding that for 23+26dBm CA PC2 UE, in case 3, the max transmission power for carrier 1 in band A is 23dBm; and there is no difference between normal inter band UL CA and Tx switching.
Reference: Definition of per BC power class in TS 38.306
 | Number of Tx chains in WID (band A + band B)
Case 1 | 1T+1T
Case 2 | 0T+2T
Case 3 | 2T+0T
powerClass, powerClass-v1610 Indicates power class the UE supports when operating according to this band combination. If the field is absent, the UE supports the default power class. If this power class is higher than the power class that the UE supports on the individual bands of this band combination (ue-PowerClass in BandNR), the latter determines maximum TX power available in each band. The UE sets the power class parameter only in band combinations that are applicable as specified in TS 38.101-1 [2] and TS 38.101-3 [4]. | BC | No | N/A | FR1 only

## Slide 5: WF on 1Tx-2Tx and 2Tx-2Tx switching between band A (carrier 1) and band B (carrier 2+3)
Clarification on the location of switching period
  For 1Tx-2Tx and 2Tx-2Tx switching between band A and band B, clarify that the location of switching period is semi-statically configured on one of the two uplink bands.
2-layer MIMO support
  Mandate 2-layer PUSCH transmission in all the carriers supporting 2Tx, including the two carriers on band B in 1Tx-2Tx switching scenario and the three carriers on band A+B for 2Tx-2Tx switching scenario.
    Clarify that the case with 1T on CC2@Band B and 1T on CC3@Band B is not considered in the WI discussion.
    Mandate 2-layer PUSCH transmission is only under the precondition that 2T is supported already on the carrier.
    The Tx switching feature itself is optional.

## Slide 6
Thanks!