## Slide 1: Way Forward on BCS reporting and support to intra-band EN-DC band combinations
Bell Mobility

## Slide 2
Background information | RAN2 IE description from 38.306
New IE “supportedBandwidthCombinationSetIntraENDC” was added into 38/306/38.331 version 15.9.0 As per the IE description, this IE is introduced to report the bandwidth combinations for the intra-band EN-DC component for intra-band EN-DC with additional inter-band CA component(s) of LTE and/or NR. It also says that this IE is mandatory if the band combination is an intra-band EN-DC combination with additional inter-band NR/LTE CA component The CR was approved as being BC under the assumption that no devices implemented intra-band EN-DC combination with additional inter-band NR/LTE CA component. This assumption is right or wrong depending on the interpretation of what defines an intra-band EN-DC component for intra-band EN-DC with additional inter-band CA component(s) of LTE and/or NR If intra-band EN-DC component for intra-band EN-DC with additional inter-band CA component(s) of LTE and/or NR is defined considering DL and UL support, RAN2 assumption is right and there is no BC issue with the CR If intra-band EN-DC component for intra-band EN-DC with additional inter-band CA component(s) of LTE and/or NR is defined considering DL or UL support, RAN2 assumption is wrong and there is a BC issue with the CR since there are devices on the field that supports combinations such as DC_2A-7A-7A-66A_n66A where only DL intra-band is supported This is the reason why Plenary sent LS to RAN4 to clarify questions in next page | supportedBandwidthCombinationSetIntraENDC Defines the supported bandwidth combination for the band combination set as defined in the TS 38.101-3 [4]. For intra-band EN-DC with additional inter-band CA component(s) of LTE and/or NR, the field defines the bandwidth combinations for the intra-band EN-DC component. Field encoded as a bit map, where bit N is set to "1" if UE support Bandwidth Combination Set N for this band combination as defined in the TS 38.101-3 [4]. The leading / leftmost bit (bit 0) corresponds to the Bandwidth Combination Set 0, the next bit corresponds to the Bandwidth Combination Set 1 and so on. It is mandatory if the band combination is an intra-band EN-DC combination with additional inter-band NR/LTE CA component. supportedBandwidthCombinationSet Defines the supported bandwidth combination for the band combination set as defined in the TS 38.101-1 [2], TS 38.101-2 [3] and TS 38.101-3 [4]. For NR SA CA, NR-DC, inter-band EN-DC without intra-band EN-DC component and intra-band EN-DC with additional inter-band NR CA component, the field defines the bandwidth combinations for the NR part of the band combination. For intra-band EN-DC without additional inter-band NR and LTE CA component, the field indicates the supported bandwidth combination set applicable to the NR and LTE band combinations. Field encoded as a bit map, where bit N is set to "1" if UE support Bandwidth Combination Set N for this band combination as defined in the TS 38.101-1 [2], TS 38.101-2 [3] and TS 38.101-3 [4]. The leading / leftmost bit (bit 0) corresponds to the Bandwidth Combination Set 0, the next bit corresponds to the Bandwidth Combination Set 1 and so on. It is mandatory if the band combination has more than one NR carrier (at least one SCell in an NR cell group) or is an intra-band EN-DC combination or both.

## Slide 3
Questions | Possible Answers |  | Proposed way forward Compromised answers to Plenary questions
B) Resolve the general question of classification of intra-band EN-DC band combinations according to UL support. If the UE doesn't support UL on intra-band EN-DC part of a band combination, is band combination classified as "intra-band EN-DC band combination"? | YES All signalling defined for intra-band EN-DC is applied | NO This case can only happen with a higher order combination and the combination would be classified as inter-band EN-DC | In RAN4 understanding, there are three categories of EN-DC combinations in RAN2 signalling support, i.e. inter-band EN-DC, intra-band EN-DC, and intra-band EN-DC with additional inter-band LTE/NR CA components. However, in RAN4 we have the following understanding: If the UE does not support UL on intra-band EN-DC part of a band combination, then the combination is not an intra-band EN-DC combination but it has an intra-band EN-DC component, but the UE is allowed to optionally report BCS as answered in Question A. If the UE does not support UL on the intra-band EN-DC part of a band combination, then the combination is downlink inter-band and intra-band EN-DC with uplink inter-band EN-DC. But the UE is allowed to optionally report intra-band EN-DC BCS as answered in Question A. This may not fit into the current RAN2 signaling framework, therefore we would like RAN2 to consider it and feed back RAN2 views. The combinations described in the , Why it is a compromise? Because by answering NO it will mean that no BCS will be ever possible to be reported. Answering Yes with the proposed answer to second question, the BCS can optionally be signalled using the already defined mechanism by RAN2
A1) Clarify if higher order (i.e. those band combinations which the UE indicates support for explicitly in UE capability signalling) EN-DC band combinations with a common band on the LTE and NR side such as DC_2A-7A-7A-66A-n66A and DC_2A-71A_n71A need to report a BCS for intra-band EN-DC (as defined in 38.101-3, section 5.3B.1), even if the UE doesn’t support the intra-band UL configurations DC_66A_n66A or DC_71A_n71A respectively? | YES Pros: BCS may be needed to be reported due to HW limitations Cons: RAN2 CR becomes NBC and an assumption for devices in field must be done | NO Pros: RAN2 CR is 100% BC and no default assumption is needed. If UL is not required to be supported the combination will follow under Inter-Band EN-DC and the mechanism in place to treat inter-band EN-DC takes place (use of LTE/NR BCS and LTE/NR supported BW) Cons: Some companies believe BCS need to be reported to report some HW limitations | No but UE shall be allowed to optionally report intra-band EN-DC BCS. If BCS is reported it must be taken into consideration by network Why it is a compromise? Devices with any limitation can still report BCS and NW must take reported BCS into consideration. Making the report optional addresses both “camps”. If the BCS is not reported the combination is treated as inter-band EN-DC (like it was prior to the CR). This would be similar to answer NO to first question. This will address the legacy devices issue (since devices are allowed not to report BCS). An exception will be needed to address devices supporting DC_n71(AA) Note: This should be a small change into RAN2 spec. One option is by making supportedBandwidthCombinationSetIntraENDC mandatory for DL and UL intra-band EN-DC combination with additional inter-band NR/LTE CA component and optional for DL intra-band EN-DC combination with additional inter-band NR/LTE CA component Devices with any limitation can still report BCS and NW must take into consideration so it address the concern raised by some companies that wants the BCS to be reported It is of course up to RAN2 to define how to address RAN4 clarifications
A2) If the UE does not report the EN-DC BCS for such a combination, what can the network assume about the configuration limitations for the common bands (e.g. LTE band 71 and NR band n71) in the combination? | Default BCS Combination should be treated as inter-band EN-DC | No assumption needed except for n71 | If an UE supports a combination that has an intra-band EN-DC component and the UE does not report an intra-band EN-DC BCS, Either 1) default bandwidth combination capabilities defined in 38.101-3 clause 4.2 shall be assumed Or 2) Single default BCS can be assumed (RAN4 can document it in 101-3, or it is conveyed by RAN2 signalling). RAN4 will look at both options and inform RAN2 once a decision is made With the proposed compromise a default is only needed for n71 devices. For DC_n71(AA) combinations BCS=0 may be assumed as default if not reported RAN4 CR is needed