## Slide 1: WF on transient period
Moderator (CMCC)
3GPP TSG-RAN WG4 #98-e
25 Jan. – 5 Feb. 2021
Electronic meeting
R4-2103361

## Slide 2
Issue 1-1-1 :CR on introduction of shorter Transient Period Capability
Agreements:
  Type 1 transient period placement in 2684 is agreed
  EVM measurement exclusion period needs to be agreed with type 1 placement as a package
Proposals for EVM measurement exclusion period：
WF:
  SCS option 1 is agreed, under the condition that in IoDT testing, the UE indicates it can’t support 30kHz SCS for a band.
  Tpstart are put in brackets. Tpstart only applies to the case where the transient period is placed over two consecutive symbols
Reported transient capability (us) | EVM definition | tpstart (µs) | SCS (option1) | SCS (option2) | SCS (option3)
2 |  | -0.5 | 30kHz is default unless it is not supported and in this case 15kHz | 30kHz | 30kHz
4 |  | -1 | 15kHz | 15kHz | 30kHz
7 |  | -2 | 15kHz | 15kHz | 15kHz
NOTE 1: ,,and are defined in Annex F NOTE 2: is the EVM for a symbol right after a transition; is the EVM for a symbol right before a transition NOTE 3: tpstart denotes the start position of the EVM exclusion window as shown in Annex F.4 |  |  |  |  | 
Table 1

## Slide 3
Issue 1-2-6 EVM budget for symbol where the transient occurs
Proposals
  256QAM: [5%], or [8%],
  64QAM: [15%], or [10%],
WF
  64QAM: [10%]
  256QAM: [8%]
Parameter | Unit | Average EVM Level
64 QAM | % | [10]
256 QAM | % | [5-8]

## Slide 4
Issue 1-2-2: Whether 20dB power change can represent the maximum power change in the network, if not, whether TE can provide the test condition for the maximum power change
Proposals
  Option 1: 20 dB power step is reasonable for on-on power change.
  Option 2: 55dB Large power change range case cannot be ignored.
WF
  Option 1.
  At the same time, one company presented real network data showing 55dB power change was observed in some cases. Option 1 is agreed considering the limitation of TE capability.