## Slide 1: WF on Intra-band EN-DC support
Nokia
3GPP TSG-RAN WG4 #99-e
R4-2107751

## Slide 2: Issue 5-1-1: intraBandENDC-Support definition
Options discussed in RAN4#99e
  Option 1: For intra-band EN-DC, contiguous or non-contiguous is determined by the configuration between the primary cells from each cell group. (Apple, OPPO, [MTK])
  Option 2: The entire LTE and NR spectrum are contiguous, i.e., all carriers are contiguously spaced for contiguous EN-DC. (Qualcomm, Nokia)
    Option 2a: If separate UL/DL signaling is not available, then the lowest capability between UL and DL should be reported where the lowest capability is regarded as C-only. Some scenarios will not be able to be configured by the network. (Qualcomm)
    Option 2b: Not allowed only signaling non-contiguous for more than two carriers. Both must be signaled for all possible mixed configurations (Nokia)
  Option 3: If UE supports the case where one of LTE carriers is contiguous with one of NR carriers, UE needs to indicate contiguous EN-DC capability. If UE supports the case where one of LTE carriers is non-contiguous with one of NR carriers, UE needs to indicate non-contiguous EN-DC capability. If UE supports above both cases, UE needs to indicate both contiguous and non-contiguous EN-DC capability. The interpretation should be applied to both UL and DL. (NTT Docomo, Verizon, [Ericsson])
  Option 4: IntraBandENDC-Support IE should be indicated in UL and DL separately per band combination. (Huawei, Qualcomm, Google)
  Option 5: Redefine DC_(n)48CA with UL DC_48A_n48A non-contiguous, DC_48A_(n)48AA with UL DC_(n)48AA contiguous not to violate fallback operation (Google, Apple)
  Option 6: CR R4-2109968 (Ericsson); the contiguous EN-DC sub-block consist of one E-UTRA and one NR sub-block of the EN-DC band class as specified in Table5.3B.0-1. Then intraBandENDC-Support is absent. For combinations of C and NC EN-DC (e.g. DC_48A-(n)48AA) there can be at most two NC EN-DC sub-blocks one of which is to the type in Table 5.3B.0-1, the other either an E-UTRA or an NR sub-block. For these the UE lists three sub-blocks with intraBandENDC-Support = “both”. This can also be indicated for two sub-blocks, e.g. DC_(n)48AA and DC_48A-n48. For NC combinations of E-UTRA and NR sub-blocks, there can be an arbitrary number of sub-blocks (each either E-UTRA or NR) when intraBandENDC-Support = “non-contiguous”.
Way-forward for 5-1-1.
    See next page.

## Slide 3: Issue 5-1-2: Impact to UE capability signaling
Options discussed in RAN4#99e
  Option 1: Ask RAN2 to introduce or modify UE capability signaling. (Huawei, Qualcomm, [OPPO])
    Option 1a: Change needed from Rel-15. (Huawei)
    Option 1b: Keep Rel-15 signaling. Introduce enhancement from Rel-16. ([MTK])
  Option 2: No new signaling is needed (Apple, Google, OPPO, DOCOMO, [MTK], [Nokia])
    Option 2a: Some clarification of existing signaling may be needed in RAN2. (Verizon, Google)
    Option 2b: No change at all to RAN2 is needed. (Ericsson)
Way-forward on 5-1-1 and 5-1-2
  Further study the following options.
    Apple CR (R4-2110155/R4-2110156) without changing UE capability signaling
    Ericsson CR (Revision of R4-2109968) without changing UE capability signaling
    Nokia CR (R4-2109782) without changing UE capability signaling
    Huawei proposal (R4-2111353) without changing RAN4 spec. Ask RAN2 to introduce a UE capability to indicate contiguous/non-contiguous EN-DC separately for UL from DL.

## Slide 4: Issue 5-1-3: Fallback from C to NC and NC to C.
Options discussed in RAN4#99e
  Option 1: Fallback from C to NC is not required but NC to C is required. (Qualcomm, Apple, OPPO)
  Option 2: None of cross C-NC fallbacks is required. (Verizon)
  Option 3: It depends on UE capability.
    Option 3a: UE capable of both C and NC can support the fallback from C to NC, as well as from NC to C.
    Option 3b: others
  Option 4: Removing RAN2 38.306 fall back restriction might be needed. ([OPPO])
  Option 5: No need to make any change to 38.306 (Ericsson, MTK, Huawei, [Nokia])
Way-Forward on 5-1-3
  FFS

## Slide 5: Issue 5-1-4: UE RF requirement update
Options discussed in RAN4#99e
  Option 1: The UE RF requirements for intra-band contiguous and non-contiguous EN-DC should be updated to reflect the possibility of intra-band contiguous or non-contiguous CA within the E-UTRA and/or NR cell group. (Qualcomm, Apple)
  Option 2: UE RF requirement change is not required.
Way-Forward on 5-1-4
  The proponents are encouraged to provide the spec impacts (i.e., in a form of a CR) for further review.

## Slide 6: Issue 5-1-5: BCS issue
Proposals
  Option 1: The same BCS shall be applied between contiguous and non-contiguous EN-DC. (Nokia)
  Option 2: Others
Way-Forward on 5-1-5
  No action. Already solved in RAN2 (R4-2107617)