## Slide 1: WF on introduction of power limits for serving cells of UL CA
Ericsson
3GPP TSG-RAN WG4 Meeting #99-e
Electronic meeting, 19 – 27 May 2021
R4-2107762

## Slide 2: Background
The background for introducing power limits for serving cells
a problem first reported in conformance testing that Rel-15 FR2 UEs stop transmitting UL signals of NR SCC when it is set to transmit UL signals at maximum power [1]
problems in the field with SCells significantly reduced in power or dropped depending on the radio conditions with impact on UL throughput
RAN4 has sent an LS informed RAN5 on the conformance test problem regarding two options listed [2]
  Option 1: Equal PSD between CCs
  Option 2: Measure the UE as is even SCC output may be scaled down under CA mode
The problem in the field remains (both for FR1 and FR2), a solution for operations in the field would also resolve the conformance-test problem

## Slide 3: Proposed solution by RAN4
Introduce UE-specific power limits for serving cells of UL CA configuration
  for SCell power reductions, limit the maximum power for the PCell to reserve power for SCell transmissions
  in the general case any one of the UL serving cells to reserve power for other cells
  limits configured by RRC e.g. in uplinkConfig (UE-specific)
The limits disabled/enabled by MAC-CE (avoiding DCI limitations) for fast adaptation to changing radio conditions
  limits possibly only applicable for concurrent transmissions (e.g. not if only one cell is scheduled during a slot)
  at least for particular transmissions (e.g. PUSCH)
Existing power prioritization in 38.213 clause 7 applies
  not affected if the limits are not configured or disabled

## Slide 4: Some more details
The UE-specific limits applicable for both FR1 and FR2
A limit on a serving cell c is relative to the actual configured power PCMAX,f,c. An absolute limit not feasible for two reasons:
  for FR2 the PCMAX governing the power prioritization for CA is specified in a plane of reference that is implementation specific
  an absolute limit would have no effect if the applied power reduction (MPR) on the total signal (same as the MPR on each serving cell) is larger
Notwithstanding, both absolute and relative limits on UL serving cells can be accommodated by the same signaling structure
Many more details can be found in R4-2109979 [3]

## Slide 5: WF
The CRs introducing the power limits in Rel-16 postponed:
  R4-2109957 for FR1 [4] , R4-2109960 for FR2 [5]
Verify that the provisions in these CRs imply the intended behaviour until RAN4#100-bis
Inform RAN5 that RAN4 is considering a solution of the Scell dropping problem for operations in the field, and thus also for conformance tests when RAN4 reach consensus of introducing the solution
Inform RAN1 and RAN2 when RAN4 reach consensus of introducing the solution
  RAN2 for introduction of signaling needed for the power limits
  RAN1 for any unforeseen impact on the RAN1 specifications

## Slide 6: References
R4-2009656, “NR SCC UL power drop behaviour with EN-DC UE in FR2”, Anritsu
R4-2011695, “WF on NR SCC UL power drop behavior in FR2”, Antritsu
R4-2109979, “Power reduction for contigous (and non-contiguous) UL CA with HPUE: MPR and power prioritization”, Ericsson
R4-2109957, “Introduction of power limits for serving cells of UL CA”, Ericsson
R4-2109960, “Introduction of power limits for serving cells of UL CA”, Ericsson