## Slide 1: WF on Rx Requirements for Type 2 UE
Qualcomm Inc., …
R4-2107784
3GPP TSG-RAN WG4 Meeting #99-e
Electronic meeting, 19 – 27 May 2021

## Slide 2: Background:
Problem to solve as stated in [3] [4]
    Scenario for which the current intra-band EN-DC requirements do not ensure RF performance
    RAN4 to consider requirements to ensure performance with larger received PSD differences (than 6 dB for Type 1) between intra-band (or inter-band with shared DL spectrum) cell groups.
Proposal in [2]:
    a provision that the minimum requirements apply for an input power of the anchor signal up to [30 dB] greater than the input power of the wanted NR except for the minimum requirement on the maximum input power (consistent with ACS requirements)
Issue with [2]:
    UE filters have no selectivity for other DL carriers that are largely imbalanced
    UE cannot meet RX requirements due to lack of selectivity of DL carrier from another CELL group.
Proposal in [1] in response to [2] for equal DL carrier BWs:
    REFSENS relaxation is a function of DL carrier imbalance with inadequate filter selectivity.
    REFSENS must be relaxed by [0.5-1]dB for 19dB DL carrier power imbalance
    REFSENS must be relaxed by [14]dB for 30dB DL carrier power imbalance

## Slide 3: WF:
Choices so far for DL carrier power imbalance
    Agree on REFSENS requirement for 19dB DL carrier power imbalance at the worst-case frequency offset.
      Option 1: [0]dB
      Option 2: [0.5-1]dB
      Option 3: Other values are not precluded.
    Further study for impact on RX requirements for a larger range [19-30]dB DL carrier power imbalance
      Further refine the DL carrier power imbalance test point.
      Study impact on REFSENS
        Up to 14dB relaxation for 30dB DL carrier power imbalance from [1] at the worst-case frequency offset
        Study relaxation for 25dB DL carrier power imbalance from [4]
        Study relaxation Vs frequency offset of other CG for larger DL carrier power imbalance.
      [FFS] impact on other RX requirements.

## Slide 4: References:
[1] R4-2111461 Imbalance Requirement for Type 2 UE RX, Qualcomm Incorporated, R4#99-e
[2] R4-2109964 Requirements Type 2 UEs supporting inter-band MRDC with overlapping DL, Ericsson., R4#99-e
[3] R4-2103166 WF on requirements for Type 2 UEs supporting inter-band MRDC with overlapping DL, Ericsson, R4#98bis-e
[4] R4-2000953 Further discussion on power imbalance requirement for intra-band EN-DC/NR CA , NTT DOCOMO, INC., R4#94-e