## Slide 1: WF on n262 UE EIRP/EIS requirement
Nokia
3GPP TSG-RAN WG4 #99-e
R4-2107790

## Slide 2: GTW agreement (May 20th)
Min peak EIRP
  Agreement in GTW May 20th:
    For PC2, 22.9dBm
    For PC4, 28.3dBm
REFSENS
  Agreement in GTW May 20th
    PC2: -86.8dBm
    PC4: -91.0dBm
Gain drop
  Agreement in GTW May 20th
    PC2: 11.9dBm
    PC4: 12.1dBm

## Slide 3: Wayforward on PC1 Min peak EIRP
 |  |  |  |  |  |  |  |  | Option 1 | Option 2 | Option 3 | Option 4
power class | Qualcomm | Vivo | Sony | Ericsson | Nokia | Intel | MediaTek | OPPO | Average made over mW [dBm] | Average made over dBm [dBm] | Average made over mW [dBm] excluding extremes (i.e., 41.9dBm) | Average made over dBm [dBm] excluding extremes (i.e., 41.9dBm)
 | R4-2108813 | R4-2109669 | R4-2109007 | R4-2111163 | R4-2109789 | R4-2111063 | R4-2109547 | R4-2110839 |  |  |  | 
PC1 | 35.9 | 33.6 | 35.5 | 35.5 | 34 | 29.5 | 33.4 | 33.6 | 34.9 | 34.2 | 34.2 | 33.9
Agreement:
PC1 Minimum peak EIRP
    For PC1, 34.2 dBm

## Slide 4: Wayforward on PC1 REFSENS
 |  |  |  |  |  |  |  |  | Option 1 | Option 2 | Option 3 | Option 4
power class | Qualcomm | Vivo | Sony | Ericsson | Nokia | Intel | MediaTek | OPPO | Average made over mW [dBm] | Average made over dBm [dBm] | Average made over mW [dBm] excluding extremes (i.e. -98.5 dBm) | Average made over dBm [dBm] excluding extremes (i.e. -98.5 dBm)
 | R4-2108813 | R4-2109670 | R4-2109008 | R4-2111164 | R4-2109791 | R4-2111064 | R4-2109557 | R4-2110840 |  |  |  | 
PC1 | -95.5 | -92 | -94.5 | -94.5 | -91.5 | -90.7 | -91.6 | -92 | -92.6 | -93.0 | -92.5 | -92.8
Agreement:
PC1 REFSENS for 50MHz CBW
    For PC1, -92.5 dBm

## Slide 5: Wayforward on PC1 Gain drop
 |  |  |  |  |  |  |  |  | Option 1 | Option 2 | Option 3 | Option 4
power class | Qualcomm | Vivo | Sony | Ericsson | Nokia | Intel | MediaTek | OPPO | Average (linear) | Average over dBm | Average (linear) excluding extremes | Average made over dB excluding extremes
 | R4-2108813 | R4-2109669 | R4-2109007 | R4-2111163 | R4-2109789 | R4-2111063 | R4-2109547 | R4-2110839 |  |  |  | 
PC1 | 8 | 8.5 | 8 | 8 | 8 |  | 8.5 | 10.2 | 8.5 | 8.5 | 8.2 | 8.2
Agreement:
PC1 Gain drop from peak EIRP/REFSENS to spherical EIRP/EIS
    For PC1, 8.2 dB