## Slide 1: Way forward on MSD due to IMD of intra-band UL CA UL configurations
Skyworks Solutions Inc., Qualcomm Inc…
R4-2107802
3GPP TSG-RAN WG4 Meeting #99-e
Electronic meeting, 19 – 27 Apr. 2021

## Slide 2: WF: intra-band cases
MSD with ULCA IMDs
  CA_n5B MSD related to IMD3 of ULCA need to be specified.
    Large MSD is expected, similar to DC_(n)71AA
  CA_n66(2A) and CA_n66B do not need MSD study for IMD (high IMD order)
Protection level of band n40 by band n41 with UL CA needs to be studied:
  Band n40 is subject to IMD3
  With contiguous intra-band UL the -13dBm/MHz SEM part overlaps with band n40 thus with only MPR applied
  Requires at least 37dB rejection from the filter to meet -50dBm/MHz band protection level
  If filter rejection is not available, RAN4 needs to study for regions where band 40 and band 41 are not synchronized:
    Change of protection level in band 40 to higher level than -50dBm/MHz
    Allocation restriction or A-MPR

## Slide 3: WF: Converging input on IMD related MSD for inter-band
Band / Channel bandwidth / NRB / Duplex mode |  |  |  |  |  |  |  | Source of IMD
NR CA band combination | NR band | UL Fc | UL/DL | UL LCRB | DL Fc | MSD (dB) | Duplex mode | 
 |  | (MHz) | BW (MHz) | SKW / QCOM | (MHz) |  |  | 
CA_n2A-n77(2A) | n2 | N/A | 5 | same | 1988 | 2 / 3.4 => avg 2.7 | FDD | IMD7
 | n77 | 3455 | 10 | same | 3455 |  | TDD | N/A
 |  | 3945 | 10 | same | 3945 |  |  | 
CA_n2A-n66(2A) | n2 | N/A | 5 | same | 1933 | 0.6 / 0 => avg 0.3 => 0 | FDD | IMD7
 | n66 | 1722.5 | 5 | same | 1723 |  | TDD | N/A
 |  | 1777.5 | 5 | same | 1778 |  |  | 
CA_n3A-n77(2A) | n3 | N/A | 5 | same | 1878 | 1.7 / 2.7 => avg 2.2 | FDD | IMD7
 | n77 | 3455 | 10 | same | 3455 |  | TDD | N/A
 |  | 3945 | 10 | same | 3945 |  |  | 
CA_n25A-n41C | n25 | N/A | 5 | same | 1988 | 9.6 / 7.3 => avg 8.5 | FDD | IMD7
 | n41 | 2545 | 90 | same | 2545 |  | TDD | N/A
 |  | 2460 | 100 | 1 (RBstart=225) / 1 (RBstart=229) | 2460 |  |  | 
CA_n30A-n77(2A) | n30 | N/A | 5 | same | 2353 | 2.3 / 4 => avg 3.2 | FDD | IMD7
 | n77 | 3455 | 10 | same | 3455 |  | TDD | N/A
 |  | 3825 | 10 | same | 3825 |  |  | 
CA_n41C-n66A | n41 | 2545 | 90 | same | 2545 |  | TDD | N/A
 |  | 2640 | 100 | same | 2640 |  |  | 
 | n66 | N/A | 5 | same | 2198 | 22 / [33.5]1 | FDD | IMD5
CA_n41C-n77A | n41 | 2545 | 60 | same | 2545 |  | TDD | N/A
 |  | 2640 | 100 | same | 2640 |  |  | 
 | n77 | N/A | 5 | same | 3305 | 1.1 / 4.2 => avg 2.7 | FDD | IMD9
CA_n66A-n77(2A) | n66 | N/A | 5 | same | 2198 | 2.3 / 4.4 => avg 3.4 | FDD | IMD7
 | n77 | 3455 | 10 | same | 3455 |  | TDD | N/A
 |  | 3875 | 10 | same | 3875 |  |  | 
DC_3A_n41C | 3 | N/A | 5 | / N/A | 1878 | 0 / 3.3 => avg 1.7 | FDD | IMD9
 | n41 | 2545 | 90 | / 1 (RBstart=0) | 2545 |  | TDD | N/A
 |  | 2460 | 100 | / 1 (RBstart=190) | 2460 |  |  | 
Given this is the first evaluation of such issues, the input from the two companies are very close
When difference is les than 3dB average is taken (see table on the left)
For CA_n25A-n41C: check the small difference allocation
For CA_n41C-n77A need to crosscheck assumptions (Note that proponent of higher value had to verify)
For CA_n3A-n78(2A) has no MSD for IMD but needs to be crosschecked for triple beat
CA_n2(2A)-n66, CA_n66 and CA_n66(2A) can be introduced or confirmed in the specification with draft CRs without MSD related to IMD.

## Slide 4: WF: Cases needing convergence: CA_n25A-n41C test point
RBstart=225, IMD falls at 1988MHz, 0.5MHz offset from DL channel center at 1887.5MHz (After small correction and using exactly the UL channel frequencies in the test point RBstart=226 should have been used to be better centered)
RBstart=229, IMD falls at 1987.5MHz but uses contiguous UL CA channel spacing equations vs exact test points frequencies
Misalignment only exists for contiguous UL CA cases
Both approaches are mathematically valid thus we must decide on which chanel spacing to use for the test points.
Does not influence the MSD value
WF: Channel spacing to be used for contiguous UL CA needs to be decided at next meeting between UL CA channel spacing or exact frequency on test point with simplicity in mind but unambiguous for RAN5 testing
In the meantime RBstart=226 and frequencies for CA_n25A-n41C test points based on R4-2111016 (no exact value for the other case available) are put in brackets for verification at next meeting

## Slide 5: WF: Cases needing convergence: CA_n41C-n66A MSDA_n41C-n66A
MSD = 22dB: n-plexing of n66 and n41 on the same antenna
  IMD5=-25dBm/MHz (based on NS04 A-MPR and IMD3 -25dBm/MHz met with band 41 filter help)
  45dB filter rejection based on triplexer arrangement (n-plexer for higher order)
  Interference -68.2dBm/MHz with correction factor. MSD calculated with MRC and 10dB antenna isolation
MSD = 33.5dB: n41 and n66 on different antennas and lower rejection from filter
  Using IMD3 at -25dBm/MHz for NS04 (no filter help) => IMD5 at -35 to -40dBm and 20dB filter rejection
  -65dBm to -70dBm used at both n66 RX antennas (no MRC gain)
Both architectures and calculations are valid with some adjustments still possible
WF: put [22-33.5dB] in the specification with resolution in next meeting on second architecture to see if MSD can be improved with lower IMD levels or higher filter rejection

## Slide 6: WF on IMD calculation framework
Main difference are limited to:
  Intra-band contiguous UL CA case for channel spacing
  To be finalized at next meeting
  Architecture and component differences that are expected from different implementations
  Part of what needs to be discussed in the AI to make sure the requirement covers multiple implementations
  IMD levels in intra-band contiguous ULCA for NS04
  How to account for filter help or not for the MPR.
WF: Given the general good agreement between the two companies and the few remaining differences the framework described in R4-2111016 can be used as a starting point with the understanding that when applicable the above points are subject to further discussion

## Slide 7: WF on further aspect to be studied for next meeting
Beyond aspects already discussed in the previous slides the following guidelines are provided:
  For contiguous UL CA limit the evaluation up to IMD11
  For non-contiguous UL CA limit the evaluation up to IMD9
  In some extreme cases higher order product can be discussed in the contribution or by experts in the meeting if justified technically

## Slide 8: References:
[1] R4-2107625 Revision of R4-2111476 MSD due to IMD from ULCA, Qualcomm Incorporated, R4#99-e
[2] R4-2111016 MSD Due to NR Intra-band ULCA IMD within Inter-band Combinations, Skyworks Solutions Inc., R4#99-e
[3] R4-2108930 MSD analysis for n77(2A) UL cases, Nokia, Skyworks Solutions Inc., R4#99-e
[4] R4-2108932 draft CR to 38.101-1: CA_n2-n77, Nokia, Skyworks Solutions Inc., AT&T, R4#99-e
[5] R4-2108931 draft CR to 38.101-1: CA_n5A-n77(2A) introduction of UL CA_n77(2A), Nokia, AT&T, R4#99-e