## Slide 1: WF on device type signaling for PC1.5
Apple
3GPP TSG-RAN WG4 Meeting #99-e R4-2107824
Electronic meeting, 19th May – 27th May, 2021

## Slide 2: Background
MPR for PC1.5 was originally introduced for typical UEs with dual Tx for n41
It is considered to use PC1.5 for FWA devices in n77, n78 and n79
Due to different form factors FWA devices could feature better performance regarding antenna and PCB isolation
Since some FWA devices could have superior performance, it is discussed to improve PC1.5 MPR and to introduce an associated device type/capability signaling
Notes: Discussion:
Huawei: it is too early to discuss the signaling before closing MPR requirements. The current scope is extended. In our view, Option 3 can still work.
Skyworks: we did not have preference to signaling. Beyond MPR of PC1.5, we have put note on FWA device. For FR1, we do see the large form factor is the way to improvement for MPR and other requirements. We need consider the capability signaling.
Qualcomm: agree with Skyworks. Even Huawei mentioned that the performance could be different between larger form factor FWA and smart phone. In the agreement, we propose to use Option 1 as starting point.
LGE: We almost have same view as Skyworks and Qualcomm. We see the reason to define the capability signaling to differentiate different type UE with different form factor.
Huawei: To Qualcomm, we recognize the performance difference between different form factors. But it does not mean that we need different capability signaling. We would like to see the evaluation resutls for MPR first.
Samsung: We have similar understanding as moderator.
Verizon: we fully support Qualcomm comments. The scope here exactly reflect the WF agreed. It is not harmful to discuss signaling. It is time.
Apple: add Option 3 as sub-option.
AT&T: Struggle to use Option 1 as starting point. We can consider different type of devices.

## Slide 3: Signaling
After the initial discussion three options remained for further considerations:
  Option 1: Signal the device type, i.e., Type A, Type B, Type C. A set of performance requirements would be associated with each device type.
  Option 2: Prefer not to have any signalling. Prefer not to have different requirements for FWA.
  Option 3: Other ideas, or still needs more study. Please offer ideas for future discussion.
Tentative Agreement: Use Option 1 as starting point and also take MPR evaluation results into account for further discussion whether the signaling is needed.
  Understand what different requirements are needed, take the MPR evaluation into account
  Compare whether the MPR requirements will be different before discussing the signaling
  Discussion are limited to PC1.5
Notes: Discussion:
Huawei: it is too early to discuss the signaling before closing MPR requirements. The current scope is extended. In our view, Option 3 can still work.
Skyworks: we did not have preference to signaling. Beyond MPR of PC1.5, we have put note on FWA device. For FR1, we do see the large form factor is the way to improvement for MPR and other requirements. We need consider the capability signaling.
Qualcomm: agree with Skyworks. Even Huawei mentioned that the performance could be different between larger form factor FWA and smart phone. In the agreement, we propose to use Option 1 as starting point.
LGE: We almost have same view as Skyworks and Qualcomm. We see the reason to define the capability signaling to differentiate different type UE with different form factor.
Huawei: To Qualcomm, we recognize the performance difference between different form factors. But it does not mean that we need different capability signaling. We would like to see the evaluation resutls for MPR first.
Samsung: We have similar understanding as moderator.
Verizon: we fully support Qualcomm comments. The scope here exactly reflect the WF agreed. It is not harmful to discuss signaling. It is time.
Apple: add Option 3 as sub-option.
AT&T: Struggle to use Option 1 as starting point. We can consider different type of devices.