## Slide 1: WF on PC5 requirements in n259
RAN4#99-e R4-2107839
e-Meeting, May 2021
Qualcomm Incorporated

## Slide 2: On min. peak EIRP requirement
The min. peak EIRP requirement:
  Alt-1: Based on scaling from existing requirements
    [26.7 to 27.5] dBm
  Alt-2: From averaging UE Tx budget-based proposals.
    Average power: 28.0 dBm
Agreement: FFS

## Slide 3: On REFSENS requirement
50 MHz CBW, -1 dB SNR target
The REFSENS requirement:
  Alt-1: Based on scaling from existing requirements
    [-89.2 to -89.7] dBm
  Alt-2: From averaging UE Rx budget-based proposals.
    Average power: -89.7 dBm
Agreement: FFS

## Slide 4: Multi-band relaxations
∆MBP,n (dB) = 0.5 dB
∆MBS,n (dB) = 0.5 dB

## Slide 5: Spherical coverage requirement
Spherical coverage requirement shall be derived based on following gain drop:
  8 dB degradation @ 85th%ile point
Beam correspondence requirements
  Option 1: Bit 0 OK to introduce
  Option 2: Bit 0 not OK to introduce
  Agreement: FFS