## Slide 1: WF on FR2 enhancement part 2: UL gap
Apple, …
3GPP TSG-RAN WG4#99-e Meeting R4-2107857
Electronic Meeting, May. 19-27, 202 Document for: Approval
Agenda item: 9.4.4, 9.4.7.3

## Slide 2: Way forward – General issue
Agreements: Subject to RAN plenary decision, RAN4 agrees to revise WID scope by deprioritizing gaps for PA calibration
Further discussion: Whether revise WID scope by deprioritizing gaps for TRX calibration

## Slide 3: Way forward – Tx power management: RF aspect
Agreements:
  It is feasible to enable non-zero P-MPR in Tx power management and BPS related UL gap testing.
  zero P-MPR assumption for the existing test cases keeps unchanged
On the test setups for UL gap based Tx power management.
  Option 1: Based on P-MPR report with/without blocking
  Option 2: Based on peak EIRP measurement with/without blocking
  Option 3: other method like jamming
On mandating P-MPR reporting for the UE who is configured with UL gap for BPS based Tx power management.
  Option 1: Yes (Qualcomm, Nokia, Sony, Verizon, Apple, Samsung, Intel)
  Option 2: No. It is optional (OPPO, Huawei, Hisilicon)
  Option 3: depending on the conclusion of test case setup (Ericsson, vivo, AT&T)
On phantom or blocking be introduced in UL gap testing.
  Possible agreement:
    Continue discussion the test setup and requirement with and without phantom or blocking until RAN4 101e.
    Discuss phantom simplification, e.g., size, material and position
On the RF requirement for the UE who is configured with UL gap for BPS based Tx power management
  Exact RF requirement will be based on test set up.

## Slide 4: Way forward – Tx power management: RRM aspect
Agreements: The baseline assumption for UL gap related configurations:
  UL gap is configured by NW via RRC signaling. Once UL gap is configured, it can be additionally activated or deactivated.
    It is up to network decision on whether to configure UL gap or not.
  It is FFS that the configured UL gap(s) can be activated/deactivated via MAC CE and/or DCI
Gap configuration candidates:
  Candidates for gap periodicity: 5ms, 10ms, 20ms, 40ms, 80ms, 160ms, 320ms
  Candidates for gap duration: 62.5us, 125us, 250us, 500us, 1000us,
  Implicit activation to minimizing signaling, e.g., depending on PHR report.

## Slide 5: Way forward – Coherent UL MIMO
Agreement:
  UL gap for coherent UL MIMO is within the scope of WI for FR2 enhancement.
  We should follow the previous agreement for the further discussion in phase I.
    Performance gain of coherent MIMO with calibration versus different gap overhead.
    NW impacts with respect to gap type (e.g. type 1 or 2) and the codebook assumption alignment between UE and NW

## Slide 6: Contributions List in RAN4#98-e
T-doc No. | Title | Company
R4-2108797 | UL Gap testability and configuration aspects | Qualcomm Incorporated
R4-2109341 | UL gaps for Tx power management RF aspect | Apple
R4-2109363 | UL gaps for Tx power management RRM aspect | Apple
R4-2109657 | Discussion on gap for PMPR calibration | vivo
R4-2109744 | Network impact of UE FR2 UL Gap for UE Tx power enhancement | Nokia, Nokia Shanghai Bell
R4-2109745 | Requirements and test cases of for P-MPR/EIRP enhancements for UE FR2 UL Gap | Nokia, Nokia Shanghai Bell
R4-2109762 | Discussion on UL gap for self-calibration and monitoring | ZTE Corporation
R4-2110033 | FR2 UL gap for power management (P-MPR) and Tx calibration (peak EIRP) | NTT DOCOMO INC.
R4-2110826 | R17 FR2 UL gap for coherent UL MIMO | OPPO
R4-2110827 | R17 FR2 UL gap for power management | OPPO
R4-2111151 | Further consideration on UL calibration gaps | Ericsson
R4-2111260 | Discussion on RRM impacts of UL gaps for self-calibration and monitoring | vivo
R4-2111383 | On FR2 UL gap for coherence calibration | Huawei, HiSilicon

## Slide 7: Reference
[1] R4-2107664, “Email discussion summary for [99-e][138] NR_RF_FR2_req_enh2_Part_2”, Apple