## Slide 1: WF on UE RF requirement for FR2 HST
Samsung
3GPP TSG-RAN WG4#99-e Meeting R4-2107861
Electronic Meeting, May 19-27, 2021

## Slide 2: Way Forward – UE RF Requirement Framework
RAN4 need to discuss how one UE type (i.e., existing power class or new power class) can have different sets of RF requirements, each of which is applicable under certain deployment scenario, for example:
  Different UE RF requirement for uni- vs. bi-directional deployment;
  Different UE RF requirement for HST vs. normal deployment scenario.

## Slide 3: Way Forward – Power Class
A new power class or reusing existing PC for FR2 HST UE:
  to be decided after RAN4 agree on min peak EIRP and spherical coverage requirements.

## Slide 4: Way Forward – Minimum Peak EIRP
Minimum peak EIRP requirement for FR2 HST UE:
  RAN4 adopt 30.x dBm (similar to PC5) as baseline.
  The baseline could be further discussed if technical issue identified.

## Slide 5: Way Forward – Spherical Coverage Requirement
The x%-tile point in EIRP CDF
  Option 1: 70%-tile point, i.e., 30% coverage with 2 back to back panels;
  Option 2: 80%-tile point, i.e., 20% coverage with 2 back to back panels;
  Option 3: 90%-tile point, i.e., 10% coverage with 2 back to back panels;
      FFS different x%-tile point needed for different scenarios.
FFS detailed requirement for minimum EIRP value at x%-tile.

## Slide 6: Way Forward – Beam Correspondence
Beam Correspondence requirement for FR2 HST UE:
For Rel-15 Beam Correspondence:
  FR2 HST UE (roof-mounted UE type) shall mandatorily support beamCorrespondenceWithoutUL-BeamSweeping.
For Rel-16 Beam Correspondence:
  Whether or not FR2 HST UE need to support Rel-16 optional feature beamCorrespondenceSSB-based-r16:
    FFS the benefits.
    If not, no need to define corresponding requirement for Rel-16 optional feature beamCorrespondenceSSB-based-r16 for Rel-17 FR2 HST UE.
  Whether or not UE need to support Rel-16 optional feature beamCorrespondenceCSI-RS-based-r16:
    FFS the benefits.
    If not, no need to define corresponding requirement for Rel-16 optional feature beamCorrespondenceCSI-RS-based-r16 for Rel-17 FR2 HST UE.

## Slide 7: Contributions List in RAN4#98-e
T-doc No. | Title | Company
R4-2109570 | On FR2 HST RF Requirements | Qualcomm, Inc.
R4-2110236 | Further Discussion on UE RF requirement for FR2 HST | Samsung
R4-2111128 | Consideration on UE beam and pwr requirements for FR2 HST | Ericsson
R4-2110237 | Further Discussion on Beam Correspondence for FR2 HST UE | Samsung
R4-2111008 | UE beam correspondence for FR2 HST | Nokia, Nokia Shanghai Bell
R4-2111146 | Views on Beam Correspondence requirements for FR2 HST UE | Ericsson

## Slide 8: Reference
[1] R4-2107667, “Email discussion summary for [99-e][141] NR_HST_FR2_enh”, Samsung
[2] R4-2107951, “Email discussion summary for [99-e][141] NR_HST_FR2_enh”, Samsung