## Slide 1: WF on MPR/A-MPR requirements for PC2 NR V2X UE
Agenda item: 9.14.6
Source: LG Electronics, Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #99-e R4-2107873
Electronic Meeting, 19th – 27th May, 2021

## Slide 2: Background
In RAN4 #99-e meeting, LGE & Huawei provided MPR requirements for High power (PC2) NR V2X UE.
In 1st round discussion, RAN4 treated the sub-topic 2-1 for PC2 MPR requirements and sub-topic 2-2 for PC2 A-MPR requirements as follow.
  Sub-Topic 2-1 : MPR
    2-1-1: MPR for PSCCH and PSSCH
    2-1-2: MPR for S-SSB
    2-1-3: MPR for PSFCH
  Sub-Topic 2-2 : A-MPR
    2-2-1: A-MPR for PSCCH and PSSCH based on EU regulation
    2-2-2: A-MPR for S-SSB based on EU regulation
    2-2-3: A-MPR for PSFCH based on EU regulation
In this WF, RAN4 can make initial agreement for MPR/A-MPR requirements for PC2 NR V2X UE.

## Slide 3: WF: MPR requirements for PSSCH/PSCCH
Issue 2-1-1: MPR for PSCCH and PSSCH
  Proposals
    Option 1: Reuse MPR for PC3.
    Option 2: relaxed MPR for PC2 based on R4-2105000(LGE)
    Option 3: FFS
WF: Option 2 is agreed as follow.

## Slide 4: WF: MPR requirements for S-SSB
Issue 2-1-2: MPR for S-SSB
  Proposals
    Option 1: Reuse MPR for PC3.
    Option 2: FFS
WF: Option 1 is agreed as follow.

## Slide 5: WF: MPR requirements for PSFCH
Issue 2-1-3: MPR for PSFCH
  Proposals
    Option 1: MPR proposed in R4-2110398.
    Option 2: FFS
WF: Option 1 is agreed as follow.
For contiguous and non-contiguous allocation for simultaneous PSFCH transmission for NR V2X will be specified as follow
MPR_PSFCH = CEIL {MA_PSFCH, 0.5}
Where MA is defined as follows
MA_PSFCH = 8.5 ; 0 ≤ NGap / NRB < 0.4
= 10 ; 0.4 ≤ NGap / NRB < 0.55
= 14 ; 0.55 ≤ NGap / NRB ≤ 1
Where
NGap is the gap RB amount between RBstart and RBend for contiguous and non-contiguous allocation simultaneous PSFCH transmission. (NGap = RBend - RBstart)
CEIL{MA, 0.5} means rounding upwards to closest 0.5dB.

## Slide 6: WF: A-MPR requirements for PSSCH/PSCCH (NS_33)
Issue 2-2-1: A-MPR for PSCCH and PSSCH
  Proposals
    Option 1: Proposed A-MPR in R4-2110399 (Huawei).
    Option 2: Proposed A-MPR for PC2 based on R4-2105000(LGE).
    Option 3: FFS
WF: Option 2 is agreed as follow.

## Slide 7: WF: A-MPR requirements for S-SSB (NS_33)
Issue 2-2-2: A-MPR for S-SSB
  Proposals
    Option 1: Proposed A-MPR in R4-2110399 (Huawei).
    Option 2: FFS
WF: Option 1 is agreed as follow.

## Slide 8: WF: A-MPR requirements for PSFCH (NS_33)
Issue 2-2-3: A-MPR for PSFCH
  Proposals
    Option 1: Proposed A-MPR in R4-2110399 (Huawei).
    Option 2: FFS
WF: Option 1 is agreed as follow.

## Slide 9: Reference
[1] R4-2107670, “RAN4#99-e_summary_144_NRSL_enh_Part3,” Moderator (Huawei)
[2] R4-2110398, “Discussion on n47 PC2 MPR simulation results,” Huawei
[3] R4-2110399, “Discussion on n47 PC2 A-MPR simulation results,” Huawei
[4] R4-2105000, “NR V2X PC2 UE MPR and A-MPR simulation results for PSCCH/PSSCH transmisison,” LGE