## Slide 1: WF on rule based approach for delta TIB and RIB
Nokia
R4-2107888

## Slide 2: Background 1/2
In RAN4#99 there was a contribution [1] proposing a discussion on rule set based approach for defining dTib and dRib values.
Parallel to this RAN4 has also discussed on ways to compress dTib and dRib tables.
Proposal on rule-based approach is not to replace table compression effort but to complement it.
[1] R4-2108915 New way for defining dTib and dRib

## Slide 3: Background 2/2
In [1] it was studies on how many current band combinations follow rule-set outlined below
  H-L dTib=0.3 and dRib=0
  L-L and H-H dTib=0.5 and dRib=0
  L-L-L and H-H-H maybe needs case by case study
  Carriers in bands with a harmonic falling onto one of the DLs: default dTIB = 0.6 dB
  42,77,78 gets dTib=0.8 and dRib=0.5
  n79 dTib = 0 and dRib=0 unless is combined with 3.5 GHz bands then dTib=0.8 and dRib=0.5
  dRib = dTib-0.5 dB
  Combinations with notes are handled case by case
Low bands in above are below 1GHz and high bands above 1 GHz but bands around 3.5 GHz and above are handled separately.
Some statistical analysis were presented

## Slide 4: Way forward - Rules
RAN4 continues discussion in next meeting on if it is possible to define rule-set from which dTib and dRib values are derived. Following topics at least should be discussed
  What kind of rules could be considered
  Analysis on how current dTib/dRib values correlate with rules
  Which are the combination types that need case by case treatment

## Slide 5: Way forward – How to apply Rules
In moderator summary on 151 there were also some discussion on how to apply rules if such are derived, see below. Further discussion on this is also welcomed.
  Just have rules and delete tables
  Have rules based approach and apply that all new combos but keep exiting tables
  Have rules based approach and apply that to majority combos but complex combinations are added into tables, like the ones with notes or 3 low bands etc
  Companies can use rules to derive relaxations but values are always captured into tables