## Slide 1: WF on 60 GHz Time-related issues
Apple
3GPP TSG-RAN WG4 Meeting #99-e
Electronic Meeting, May 19th – 28th, 2021
Agenda Item: 9.15.4
R4-2107972

## Slide 2: Background
The following issues related to 60 GHz beam switching have been summarized in the related email discussion:
  Issue 3.2.1-1: RX -TX and TX -RX beam switching
  Issue 3.2.1-2: Minimum duration between beam switches
  Issue 3.2.1-3: UE Beam switch time (beam direction switch only)
  Issue 3.2.1-4: UE Inter-panel Beam switch time (beam direction switch only)
  Issue 3.2.1-5: GNB Beam switch time (beam direction switch only)
  Issue 3.2.1-6: LS to RAN1 on beam switching
  Issue 3.2.2-1: TX ON-ON and TX ON-OFF transient period

## Slide 3: Issue 3.2.1-1: RX -TX and TX -RX beam switching
Proposals
  Option 1: For NR operation in the 52.6 – 71 GHz range, the Rx-Tx and Tx-Rx transition time shall reuse the FR2 value of 13792 Tc. (7.015 usec)
    Supported by ZTE, Ericsson, Apple, MediaTek, Huawei, Qualcomm, Nokia
  Option 2: RAN4 agrees on either [3 – 5] uS for switching time for both DL-to-UL and UL-to-DL.
    Supported by Intel
WF
  For NR operation in the 52.6 – 71 GHz range, the Rx-Tx and Tx-Rx transition time shall reuse the FR2 value of 13792 Tc. (7.015 usec) for 120 kHz SCS
  FFS for Rx-Tx and Tx-Rx transition time for 480/960 kHz SCS

## Slide 4: Issue 3.2.1-2: Minimum duration between beam switches
Proposals
  Option 1: For in panel case, minimum duration between beam switches is 5us on 60GHz Band. For cross panel case, FFS.
    Supported by Intel, Huawei
  Option 2: For 60 GHz The minimum duration between any two UE beam switches is 4.5 µsec
    Supported by Qualcomm, Nokia
  Option 3 (new): more discussion is needed
    Supported by Ericsson, MediaTek
WF
  Further discussion is needed to close on the following aspects:
    Definition of beam switch scenario(s) related to this proposed requirement
    Whether a requirement on the minimum duration between beam switches is needed
      If the requirement is needed, then how to decide the value

## Slide 5: Issue 3.2.1-3: UE Beam switch time (beam direction switch only)
Proposals
  Delay times reordered for clarity
  Added performance impact study option
WF
  Alt 1: simulation study
    Quantify impact of beam switch time on network performance
    TR38.808 uses the following assumptions:
      Network scenarios: {indoor scenario A, indoor scenario B, indoor scenario C, outdoor scenario B}
      DL:UL traffic ratios: {1:1, 2:1, 5:2}
      File size (MB): {27, 8, 2, 0.5}
  Alt 2: further discussion on UE feasibility
  Alt 3: analysis of the system impact (by some other means than sim study)
UE beam switch time | UE beam switch time | Supported by
Option 1 | ≤ 50 ns | Ericsson, Sony, Intel
Option 2 | ≤ 75 ns | Sony, Huawei
Option 3 | ≤ 100 ns | Sony, Huawei
Option 4 | ≤ 200 ns | Apple, MediaTek, Qualcomm
Option 5 | Performance should be considered when selecting the value | ZTE, Nokia

## Slide 6: Issue 3.2.1-4: UE Inter-panel Beam switch time (beam direction switch only)
Proposals
  Option 1: Same as within-panel
    Supported by Nokia
  Option 2: FFS
    Supported by ZTE, Ericsson, Apple, MediaTek, Intel, Huawei, Qualcomm
WF
  A conclusion of the intra-panel beam switch time is needed
  Companies are encouraged to provide analysis of delays in addition to intra-panel, if any, associated with inter-panel beam switch time

## Slide 7: Issue 3.2.1-5: GNB Beam switch time (beam direction switch only)
Proposals
  Option 1: Within panel: RAN4 to reply to RAN1 aligned with study item conclusions that gNB beam switching can take place in less than 59 ns (i.e. 50ns).
    Supported by ZTE, Ericsson, Intel, Nokia
  Option 2: For BS beam switching time, further study on the beam switching time after BS side has more input on transmission power requirement.
    Supported by Huawei
  Option 3: 20ns
    Supported by ZTE
WF
  Given multiple companies’ reference to the SI outcome (59 ns) and one company’s comment related to BS output power:
    RAN4 tentatively agrees [59 ns] with the understanding that the value can be confirmed once open issues related to BS output power are resolved

## Slide 8: Issue 3.2.2-1: TX ON-ON and TX ON-OFF transient period
Proposals
  Option 1: RAN4 agrees on [1 – 3] uS transient period for both ON/OFF and ON/ON transient period for 52.6 – 71 GHz range.
    Supported by Intel
  Option 2: Re-use UE transient time from current FR2:
    for ON/OFF, OFF/ON, and ON/ON transient time
      Supported by Apple, MediaTek, Huawei, Nokia
    for ON/OFF and OFF/ON only, with ON/ON using a different requirement
      Supported by Ericsson, Intel
WF
  Re-use UE transient time from current FR2 for 120 kHz SCS
  FFS on UE transient time for 480/960 kHz SCS