## Slide 1: WF on CBM UE architecture
RAN4#99-e R4-2107853
e-Meeting, May 2021
Qualcomm Incorporated

## Slide 2: Background -1
Moderator summary from 1st round of discussion as captured in R4-2107663 ->
This WF accordingly focuses on ‘define CBM requirements in such manner that both single chain and multi chain architectures are possible’ for UEs supporting DL inter-band CA based on CBM
Sub-topic #1-3 CBM UE architecture | Most (11) of the companies prefer to define requirements so that both single chain and multi chain architectures are possible while three companies consider that requirements should be based on only single chain architecture. Tentative agreements: RAN4 agrees to define CBM requirements in such manner that both single chain and multi chain architectures are possible. Recommendations for 2nd round: WF assigned to Qualcomm.

## Slide 3: Background - 2
‘Single-chain architecture’: single beam forming network shared by both bands top figure
‘Multi-chain architecture’: multiple beam forming networks, each dedicated to one band bottom figure

## Slide 4: WF – General
Agreement: RAN4 agrees to define CBM requirements in such manner that both single chain and multi chain architectures are possible.
Common beam management reference signal location is FFS

## Slide 5: WF – CBM Tx/Rx requirement framework
The requirement framework and PSD condition of each below requirement shall be FFS for each one, respectively.
  REFSENS requirement
  EIS spherical coverage requirement
  ACS and IBB requirement
  Max. input power requirement
  Others
Potential requirement framework as starting point
  Option 1: Intra-band NC framework including relaxations
  Option 2: Inter-band CA framework including relaxations (∆RIB)
  Other framework is not precluded

## Slide 6: WF – Fs_inter
Companies to provide feasibility studies for next meeting for a single RF chain CBM UE to support inter-band CA with and without Fs_inter capability
  Assuming performance degradation is allowed