## Slide 1: 3GPP TSG-RAN WG4 Meeting #99-e Electronic Meeting, 19 – 27 May, 2021
Intel
WF on R17 NR MG enhancements – Pre-configured MG
R4-2108034

## Slide 2
Agreements in the 1st round/GTW
Agreements in the 2nd round
Still open after 2nd round discussion

## Slide 3: Others
unified abbreviations:
  Pre-MG : Pre-configured measurement gap

## Slide 4: Using scenarios
FFS on Whether is the pre-configured MG needed for PRS measurement:
  Option 1. Yes
  Option 2. No
  Option 3. Pre-configured MG falls back to the legacy MG
FFS on Whether is the pre-configured MG needed for CSI-RS L3 measurement:
  Option 1. Yes
  Option 2. No
  Option 3. Pre-configured MG falls back to the legacy MG

## Slide 5: Configuration procedure(1)
Pre-configured MG per BWP needs not be considered in the 1st stage of this WI.
  FFS in the 2nd stage of this WI
FFS on the specific RRC configuration parameters for the new aspects of pre-configured MG to be introduced
  Option1: The parameters used to differentiate with the legacy MG
  Option 2a: The parameters used to indicate the pre-configured MG (de)activation status per BWP, which can be also served as the flag to differentiate with the legacy MG
  Option 2b: The parameters used to indicate the pre-configured MG (de)activation status per UE/FR, which can be also served as the flag to differentiate with the legacy MG

## Slide 6: Configuration procedure(2)
Pre-configured MG status (activated/deactivated) after configuration completed
  Status of pre-configured MG is not fixed at RRC configuration
  NW can know the pre-configured status when/after the pre-MG being configured by itself
  FFS NW can fully control whether the pre-configured MG will be activated/deactivated
  FFS on how UE can know pre-configured MG’s activation status (activated/deactivated) after the pre-MG being configured
    Option 1: signaling
    Option 2: pre-defined rules
MG configuration of Pre-MG can NOT be changed after BWP switching
FFS on relation of pre-configured MG pattern and with the current RRC configured MG
  Option 1. (CATT, xiaomi):
    The pre-configured MG is the same as RRC configured MG after it is activated.
    Whether the deactivated pre-configured MG and the RRC configured MG can be configured simultaneously needs to be studied
  Option 2a (Ericsson, ZTE)
    The already configured P-MGP is transformed into legacy MGP (with same MGL/MGRP) if the UE is configured to measure on any carrier (e.g. inter-RAT) which always need gaps for performing the measurement.
    Network can transform an already configured P-MGP into legacy MGP with same MGL/MGRP or vice versa without deconfiguring the P-MGP
    Deconfigure P-MG and reconfigure legacy pattern if P-MG is not suitable for MO configuration e.g. inter-RAT, PRS etc.
  Option 2b (Huawei, MTK, vivo, Apple):
    Network can transform a pre-configured MG into legacy MG or vice versa with same MG configuration.
  Option 3 (Intel, Qualcomm, Nokia)
    NW can configure the pre-configured MG and legacy MG independently. The transformation between the pre-MG and legacy MG has not any benefits in both singnaling and latency reduction.
  [Moderator notes: If the pre-MG ON/OFF status is not fixed after being configured, for NW the serving gNB can enable it as ON/OFF by themselves completely. But for UE, UE needs to justify the pre-MG’s status based on the pre-defined rules or NW’s indication.]

## Slide 7: Activation/Deactivation procedures(1)
Criteria of activation/deactivation pre-configured MG
  Option 1 (Huawei, MTK, vivo, ZTE) :
    If MG is not required by any of the configured measurements, the MG is deactivated.
    If MG is required by one or more of the configured measurements, the MG is activated.
  Option 2 (Ericsson, vivo, OPPO, ZTE):
    The UE needs gaps to measure SSBs when the measured SSB is not fully within the BW of the active BWP. Otherwise, the UE can measure the SSBs without gaps. This change between gap based and gapless measurement is triggered by active BWP switching.
  Option 3(Intel, Apple, Qualcomm, Nokia): No need to define such criteria in the spec if the NW indication was included in pre-configured MG configuration.

## Slide 8: Activation/Deactivation procedures(2)
FFS on how pre-configured MGs can be activated/deactivated:
  Option 1 (CATT, Ericsson, Intel, xiaomi, CMCC, NEC, OPPO, Huawei, ZTE) Autonomously/implicitly triggered by BWP switching DCI/Timer.
  Option 2 (Intel, Apple, Qualcomm, vivo, CMCC, Nokia) the pre-configured MG activation/deactivation is triggered by the BWP switch and pre-configured under the control by the NW via its RRC configuration message.
    Option 2a (CMCC): If the use case of MG pattern change following BWP switch is considered, to activate/deactivate the pre-configured MG by the network indication
  Option 3 (Huawei, MTK, Nokia) : Besides BWP switching, there could be also other RRC and MAC procedures that could trigger a change in need for MG and thus activation and deactivation of pre-configured MG, e.g.
    RRC (re)configuration of MO
    RRC (re)configuration of serving cells
    SCell activation and deactivation

## Slide 9: RRM requirements with Pre-configured MGs
FFS on additional transition time for pre-configure MG (de)activation can be taken count into the total pre-configured MG activation/deactivation delay beside the BWP switching delay.
  If agreed the exact value of such transition time can be FFS.
FFS on measurement period for the measurements with the pre-configured MGs
Not any limitation on the maximum number of transitions between gapless and gap-based measurements
Existing scheduling restriction for RRM measurement without MG applies can be applied to UEs when pre-configured MG is deactivated
FFS on UE behavior after deactivation of pre-configured MG

## Slide 10: Gap patterns for pre-configured MGs
Number of pre-configured MG patterns:
  Defer this discussion until the joint discussion with multiple concurrent MG
FFS on MG patterns used for the pre-configured MG mechanism
  Option 1: The existing gap patterns (0~23) in Rel16 can be reused for the pre-configured MG.
  Option 2: The existing gap patterns (0~25) in Rel16 can be reused for the pre-configured MG.