## Slide 1: WF on RRM test case related issues
Ericsson
3GPP TSG-RAN WG4 Meeting # 99-e
Electronic Meeting, May 19-27, 2021
Agenda: 4.1.8
R4-2108038

## Slide 2: CA channel BW configuration shortage for RRM TCs
Shortage of channel bandwidth configurations in RRM test configurations identified in R4-2108849.
Candidate options:
  Option 1: Define channel bandwidth configurations for RRM CA tests in generic manner. Generic solution requires resolution of at least following 3 issues:
    Io depends on BW:
      FFS if same Io can be used in different bandwidth by defining:
        New PDSCH RMC where PDSCH has same RBs as CORESET, and
        New OCNG pattern where OCNG only covers CORESET RBs.
    RMC degradation by the generalization:
      FFS if degradation is avoided by restricting minimum channel BW to ensure sufficient RBs are in supported BWs for consistent physical allocation.
    Necessity to define maximum channel BW:
      FFS if maximum channel BW can be limited.
  Other option is not precluded.

## Slide 3: PDSCH scheduling issue during SMTC for interruption TC
Apply following changes to the scheduling for the interruption test case.
  Shift SSB for SCell 10 ms
  Shift SMTC pattern to measure SCell 10 ms to make consistent with SSB
  Define a new RMC to allocate PDSCH at special subframe only for SCS 15 kHz cases
Note: RMCs for scheduling in interruption test cases are provided in Annex A.
CRs will be provided in RAN4#100-e.

## Slide 4: FR2 inter-frequency relative RSRP accuracy
Further investigate the following until RAN4#100-e:
  Whether to revise the current test requirements for FR2 SS-RSRP relative accuracy (A.5.7.1.2 and A.7.7.1.2), which only introduce the gain difference margin X in the upper bound, but not in the lower bound?
  Whether the current test requirements for FR2 SS-RSRP relative accuracy (A.5.7.1.2 and A.7.7.1.2) can also be applied to inter-frequency measurement on a different band?
CRs will be provided in RAN4#100-e

## Slide 5: Further considerations on LTE/FR1+FR2 test case design
Testability issue for RRM test case which requires performance verification on cells of:
  Both FR1 and FR2 or
  Both LTE and FR2
FFS: Criteria to identify/select test cases that can be performed and their performance can be verified out of the test cases with OTA testability issue as identified in bullet # 1:
  Option 1: Based on power level:
      Absolute power measured on LTE/FR1 cell or
      Relative power measured between LTE and FR2 cells or between FR1 and FR2 cells
  Other options/criteria are not precluded.
  Companies are encouraged to provide the list of affected test cases.
Mechanism to exclude testing of the test cases (or parts of requirements of the test cases) identified in bullet #1 (with OTA testability issues) but not determined to be testable through bullet #2 criteria:
  Option 1: General rule/applicability rule is defined in Annex of TS 38.133:
    Following tests are not currently performed e.g., RRM test cases which have testability limitation:
      Test cases are FFS
    Section numbers of the tests which are not currently performed will be listed in the section containing applicability rule.
  Other options are not precluded.
Companies are encouraged to provide input on the above issues in RAN4#100-e.

## Slide 6: Annex A: RMCs for scheduling in interruption test case

## Slide 7: Annex A1: Scheduling: TDD SCS 15 kHz Inter-band CA
SFN |  |  |  |  |  |  |  | 2n-1 |  | 2n |  |  |  |  |  |  |  |  |  | 2n+1 |  |  |  |  |  |  |  |  |  | 2n+2 | 
SF |  |  |  |  |  |  |  | 8 | 9 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 0 | 1
Slot |  |  |  |  |  |  |  | U | D | D | S | U | U | D | D | S | U | U | D | D | S | U | U | D | D | S | U | U | D | D | S
SSB on Pcell(SSB.1 FR1) |  |  |  |  |  |  |  |  |  | x |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | x | 
SMTC for Pcell SSB frequency(SMTC.1) |  |  |  |  |  |  |  |  |  | x |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | x | 
SSB on Scell(new SSB pattern) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | x |  |  |  |  |  |  |  |  |  |  | 
SMTC for Scell SSB frequency(new SMTC pattern) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | x |  |  |  |  |  |  |  |  |  |  | 
Possible interruption |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2 |  | 4 |  |  |  |  |  |  |  |  |  | 
Not-allowed interruption |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 |  | 3 |  | 5 |  |  |  |  |  |  |  |  | 
PDSCH (new RMC) |  |  |  |  |  |  |  |  | x |  | x |  |  | x | x | x |  |  | A | B | C |  |  | x | x | x |  |  | x |  | x
HARQ feedback (e.g. k1=2) |  |  |  |  |  |  |  | x |  |  | x |  | x |  |  | x | x | x |  |  | A | B | C |  |  | x | x | x |  |  | x
Allowed DTX |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2,4 |  | 4 |  |  |  |  |  |  |  | 
Not-allowed DTX |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 |  |  |  | 3,5 |  |  |  |  |  |  |  |  | 

## Slide 8: Annex A2: Scheduling: TDD SCS 15 kHz Intra-band CA
SFN |  |  |  |  |  |  |  | 2n-1 |  | 2n |  |  |  |  |  |  |  |  |  | 2n+1 |  |  |  |  |  |  |  |  |  | 2n+2 | 
SF |  |  |  |  |  |  |  | 8 | 9 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 0 | 1
Slot |  |  |  |  |  |  |  | U | D | D | S | U | U | D | D | S | U | U | D | D | S | U | U | D | D | S | U | U | D | D | S
SSB on Pcell(SSB.1 FR1) |  |  |  |  |  |  |  |  |  | x |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | x | 
SMTC for Pcell SSB frequency(SMTC.1) |  |  |  |  |  |  |  |  |  | x |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | x | 
SSB on Scell(new SSB pattern) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | x |  |  |  |  |  |  |  |  |  |  | 
SMTC for Scell SSB frequency(new SMTC pattern) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | x | x | x |  |  |  |  |  |  |  |  | 
Possible interruption |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2 | 3 | 4 | 5 | 6 |  |  |  |  |  |  |  | 
Not-allowed interruption |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 |  |  |  |  |  | 7 |  |  |  |  |  |  | 
PDSCH (new RMC) |  |  |  |  |  |  |  |  | x |  | x |  |  | x | x | x |  |  | A | B | C |  |  | D | x | x |  |  | x |  | x
HARQ feedback (e.g. k1=2) |  |  |  |  |  |  |  | x |  |  | x |  | x |  |  | x | x | x |  |  | A | B | C |  |  | D | x | x |  |  | x
Allowed DTX |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2,4 | 3,5 | 4,6 |  |  |  |  |  |  |  | 
Not-allowed DTX |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 |  |  |  |  |  |  |  | 7 |  |  |  |  | 

## Slide 9: Annex A3: Scheduling: TDD SCS 30 kHz Inter-band CA
SFN |  |  |  |  |  |  |  | 2ｎ-1 |  | 2ｎ |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2ｎ+1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SF |  |  |  |  |  |  |  | 9 |  | 0 |  | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |  | 0 |  | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 | 
Slot |  |  |  |  |  |  |  | 18 | 19 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Slot Type |  |  |  |  |  |  |  | D | D | D | D | D | S | U | U | U | U | D | D | D | D | D | S | U | U | U | U | D | D | D | D | D | S | U | U | U | U | D | D | D | D | D | S | U | U | U | U | D | D
SSB on Pcell(SSB.1 FR1) |  |  |  |  |  |  |  |  |  | x |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SSB on Scell(new SSB pattern) |  |  |  |  |  |  |  |  |  | x | x |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SMTC for Scell SSB frequency(new SMTC pattern) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | x |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SMTC for Scell SSB frequency(SMTC.1) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | x | x |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Possible interruption |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2 |  |  | 5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Not-allowed interruption |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 |  | 3 | 4 |  | 6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PDSCH (SR.2.1 TDD) |  |  |  |  |  |  |  | x | x |  |  | x |  |  |  |  |  | x | x | x | x | x |  |  |  |  |  | A | B | C | D | E |  |  |  |  |  | x | x | x | x | x |  |  |  |  |  | x | x
HARQ feedback (e.g. k1=5) |  |  |  |  |  |  |  |  |  |  |  |  | x | x | x | x | x |  |  |  |  |  | x | x | x | x | x |  |  |  |  |  | A | B | C | D | E |  |  |  |  |  | x | x | x | x | x |  | 
Allowed DTX |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2 |  |  | 5 |  |  |  |  |  |  |  |  |  |  |  | 
Not-allowed DTX |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1,6 |  | 3 | 4 |  |  |  |  |  |  |  |  |  |  |  |  | 

## Slide 10: Annex A4: Scheduling: TDD SCS 30 kHz Intra-band CA
SFN |  |  |  |  |  |  |  | 2ｎ-1 |  | 2ｎ |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2ｎ+1 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SF |  |  |  |  |  |  |  | 9 |  | 0 |  | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 |  | 0 |  | 1 |  | 2 |  | 3 |  | 4 |  | 5 |  | 6 |  | 7 |  | 8 |  | 9 | 
Slot |  |  |  |  |  |  |  | 18 | 19 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19
Slot Type |  |  |  |  |  |  |  | D | D | D | D | D | S | U | U | U | U | D | D | D | D | D | S | U | U | U | U | D | D | D | D | D | S | U | U | U | U | D | D | D | D | D | S | U | U | U | U | D | D
SSB on Pcell(SSB.1 FR1) |  |  |  |  |  |  |  |  |  | x |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SSB on Scell(new SSB pattern) |  |  |  |  |  |  |  |  |  | x | x |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SMTC for Scell SSB frequency(new SMTC pattern) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | x |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
SMTC for Scell SSB frequency(SMTC.1) |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | x | x |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Possible interruption |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2 | 3 | 4 | 5 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
Not-allowed interruption |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1 |  |  |  |  | 6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 
PDSCH (SR.2.1 TDD) |  |  |  |  |  |  |  | x | x |  |  | x |  |  |  |  |  | x | x | x | x | x |  |  |  |  |  | A | B | C | D | E |  |  |  |  |  | x | x | x | x | x |  |  |  |  |  | x | x
HARQ feedback (e.g. k1=5) |  |  |  |  |  |  |  |  |  |  |  |  | x | x | x | x | x |  |  |  |  |  | x | x | x | x | x |  |  |  |  |  | A | B | C | D | E |  |  |  |  |  | x | x | x | x | x |  | 
Allowed DTX |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 2 | 3 | 4 | 5 |  |  |  |  |  |  |  |  |  |  |  | 
Not-allowed DTX |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  | 1,6 |  |  |  |  |  |  |  |  |  |  |  |  |  |  |  |