## Slide 1: WF on NeedForGap measurements
Ericsson, Huawei, HiSilicon
3GPP TSG-RAN WG4 Meeting #99-e
Electronic meeting, 19 – 27 May 2021
Agenda item: 5.1.7.3
Document for: Approval
R4-2108039

## Slide 2: Background
In Rel-16 TEI, RAN2 has introduced NeedForGapsInfoNR capability for NR measurement as follow.
The related requirements for NeedForGap are not defined in Rel-16.
NeedForGapsInfoNR information element -- ASN1START -- TAG-NeedForGapsInfoNR-START NeedForGapsInfoNR-r16 ::= SEQUENCE { intraFreq-needForGap-r16 NeedForGapsIntraFreqlist-r16, interFreq-needForGap-r16 NeedForGapsBandlistNR-r16 } NeedForGapsIntraFreqlist-r16 ::= SEQUENCE (SIZE (1.. maxNrofServingCells)) OF NeedForGapsIntraFreq-r16 NeedForGapsBandlistNR-r16 ::= SEQUENCE (SIZE (1..maxBands)) OF NeedForGapsNR-r16 NeedForGapsIntraFreq-r16 ::= SEQUENCE { servCellId-r16 ServCellIndex, gapIndicationIntra-r16 ENUMERATED {gap, no-gap} } NeedForGapsNR-r16 ::= SEQUENCE { bandNR-r16 FreqBandIndicatorNR, gapIndication-r16 ENUMERATED {gap, no-gap} } -- TAG-NeedForGapsInfoNR-STOP -- ASN1STOP

## Slide 3: Agreements
‘NeedForGap’ in Rel-16 is only applied in NR SA.

## Slide 4: Work Scope
Potential new objective - NeedForGap for NR-SA only
  Limited to SSB based measurements configured via measurement objects
  Study whether the additional interruption is allowed when UE reporting ‘no gap’
    Further define the interruption length, occasion and ratio, if the interruption is allowed
  Study the related requirements, such as CSSF, measurement period, scheduling restriction etc.
  RAN4 to further consider the relation with other UE capabilities, such as NCSG etc.
  Analyse other WG impact although impact is not expected.
  Decide if it is feasible that the UE requirements are defined in R16 or release independent from Rel-16.