## Slide 1: WF on 5G NR UE Application Layer Data Throughput Performance
Qualcomm
3GPP TSG-RAN4 Meeting #99-e
Electronic Meeting, May 19th – May 27th 2021
Agenda item: 10.7
R4-2108102
Document for: Approval

## Slide 2: Simulation Results Alignment – I
Number of slots containing PDSCH grant
  Skip scheduling PDSCH grant on special slots and slots containing SSB, TRS, CSI-RS for CSI reporting.
    This results in number of allocated full DL slots within 20ms as: 14 for FR1 FDD, 22 for FR1 TDD and 58 for FR2 TDD.

## Slide 3: Simulation Results Alignment – II
Processing Delay (Based on aperiodic CSI reporting)
  FR1 FDD: 6ms
  FR1 TDD: 5.5ms
  FR2 TDD: 1.375ms
Target BLER for simulations
  Option 1: 2%-20% for FR1; 1%-20% for FR2
  Option 2: 2%-30% for FR1; 1%-30% for FR2
  Other options not precluded
How to calculate Median CQI
  Based on CQI values belonging to median RI for considered SNR point

## Slide 4: Simulation Results Alignment – III
Additional Reported Metrics (in addition to median CQI, median RI) to aid with simulation alignment:
  BLER with link adaptation for each SNR point.
Alignment Results Criteria
  Option 1: Absolute throughput span within X% of average throughput across companies at a given SNR.
    Decide X based on simulation results. Possible values of X = [5]% or [10]%.
  Option 2: SNR G±Gspan can be reached for the T% of maximum throughput
    Maximum throughput is derived with TBS corresponding to CQI index 15 with rank 2 for 2Rx/4Rx UE.
    Decide Gspan based on simulation results. Candidate option is Gspan = [2.5] dB.

## Slide 5: Simulation Assumptions
Whether to consider OLLA algorithm for BS/TE
  Option 1: Yes
  Option 2: No (Baseline)

## Slide 6: Feasibility Criteria
The requirements of Absolute Physical Layer Throughput with Link Adaptation can be declared feasible if
  Option 1: RAN4 can find at least one SNR point where companies’ simulation results align.
  Option 2: RAN4 can find several SNR points where companies’ simulation results align depending on Rank 1 and Rank 2 regime.
  Other options not precluded.

## Slide 7: Requirements Definition – I
If it is found to be feasible to define requirements for link adaptation (LA) physical layer throughput:
  Set the physical layer throughput requirements:
    Option 1: By multiplying the averaged throughput by Y (%), e.g., Y=95% or 90%.
    Option 2: Use methodology from PDSCH demodulation requirements with fixed RMC (i.e. average of impairments results + X dB margin).
    Depends on outcome for alignment result criteria on Slide 4. If Option 1 is agreed, use Option 1. If Option 2 is agreed, use Option 2.

## Slide 8: Requirements Definition – II
Number of SNR points for defining requirements (if found feasible to define such requirements):
  Option 1: one in rank 1 and one in rank 2 operation SNR range.
  Option 2: one in rank 2 operation SNR range.
  Note: This will be discussed in WI phase.

## Slide 9: Simulation Results
Companies are encouraged to provide the following based on simulation assumptions and test parameters in R4-2106122 in addition to slides 2-5:
  For each SNR point:
    Absolute Physical Layer Throughput
    CQI and RI statistics (At least Median CQI and Median RI)
    BLER with Link Adaptation

## Slide 10: CR Work Split
Topic | Company
General | Qualcomm
Simulation Alignment Criteria | Ericsson
Simulation Assumptions | Huawei
Simulation Results (Same company will drive the effort for collection of simulation results) | Intel
Summary | Qualcomm
Companies are encouraged to provide CRs in the next meeting following the TR structure agreed in R4-2111255.