## Slide 1: WF on FR2 HST Deployment Scenario Analysis
Samsung
3GPP TSG-RAN WG4#99-e Meeting R4-2108660
Electronic Meeting, 19th – 27th May, 2021

## Slide 2: Way Forward – General (1/3)
Large difference in propagation delays
  FFS the impact of the large difference in propagation delays from different RRHs in a cell when DPS scheme is used:
    Large difference in propagation delays exist in
      Uni-directional RRH deployment
      Some schemes for bi-directional RRH deployment
    Whether or not one deployment scenario should be precluded in Rel-17 needs to consider the decision from RRM session.
    RRM session will investigate and decide on potential methods to mitigate the propagation delay issue

## Slide 3: Way Forward – General (2/3)
Limitation on RRH beam direction
  FFS RRH beam’s possible range of angle on azimuthal plane
    Option 1: Limit RRH beam angle w.r.t. boresight direction <= 40 degree to ensure UE reception signal quality in Scenario B. Exact limitation can varies with Dmin, but such limitation due to ensure UE reception quality needs to be taken into consideration for deployment.
    Other options for the range of angle are not precluded
  Possible range of angle is not intended to restrict practical RRH deployment;
  Following information are encouraged to provide together with the simulation results:
    RRH panel direction information;
    RRH beam(s) direction information.
    CPE boresight direction with reference to RRH panel
Potential Handover Issue:
  Potential handover problem due to sudden RX signal increase of the target cell can be alleviated by DPS transmission scheme with carefully allocated SSB-index among neighboring cells to avoid inter-cell interference.
  FFS another potential handover issue due to the sudden degraded serving cell quality for UE moving toward the serving beam in uni-directional deployment.

## Slide 4: Way Forward – General (3/3)
  RRH/Beam switching point for Uni-directional Scenario-A
  Agreement from GTW (24th May):
    If the channel model which needs Ds_offset derived from typical deployment scenario, RAN4 shall discuss Ds_offset value based on deployment scenario study.
    For Ds_offset, companies’ analysis is encouraged to be provided in TR 38.854 for information.
  Above agreement also applied to Scenario-B
  Beam dwelling time:
  The value or range of beam dwelling time is not necessarily to be agreed;
  Companies’ analysis on beam dwelling time is encouraged to be captured in TR38.854:
    Contribution-driven
    Individual analysis can be conducted based on companies’ selected parameters and scheme.

## Slide 5: Way Forward – Scenario-A
Comparison btw. uni- and bi-directional RRH deployments for Scenario-A:
  From signal strength and beam coverage perspective:
    Bi-directional deployment will not provide significant throughput improvement comparing to uni-directional deployment based on deployment scenario analysis.
    Only need to consider uni-directional deployment for Scenario-A
  Bi-directional deployment can be considered if the feasibility issue of uni-directional deployment is identified.

## Slide 6: Way Forward – Scenario-A
Schemes for Bi-directional deployment, Scenario-A:
  Agreements from GTW (24th May):
    [Scheme 1 under Bi-directional scenario is feasible without coverage hole issue, and no propogation delay jump between switching points]
  FFS Scheme 2 from deployment scenario perspective :
    on potential coverage hole issue,
    on propagation delay jump issue.
  Number of Beam for bi-directional RRH deployment, Scenario-A
  If bi-directional deployment is confirmed to be used for Scenario-A:
    1 beam per RRH panel, two panels in opposite directions
    1 beam per UE panel (i.e., 2 beam per UE), already agreed in RAN4#98-Bis-e

## Slide 7: Way Forward – Scenario-B
Comparison btw. uni- and bi-directional RRH deployments for Scenario-B:
  From signal strength and beam coverage perspective:
    FFS Bi-directional deployment’s advantage over uni-directional deployment based on deployment scenario analysis.
    FFS only need to consider uni-directional deployment for Scenario-B
  Number of Beam(s) for uni-directional (if confirmed to be used), Scenario-B:
  RRH parameter:
    2 beams per RRH panel
    Other options not precluded
      FFS the benefits of implementing more beams per RRH panel
  UE parameter:
    1 beam per UE panel
    Other options not precluded
      FFS the benefits of implementing more beams per UE panel

## Slide 8: Way Forward – Scenario-B
Schemes for Bi-directional deployment, Scenario-B:
  FFS based on last meeting’s WF:
  Number of Beam(s) for bi-directional (if confirmed to be used), Scenario-B:
  RRH parameter:
    2 beams per RRH panel
    Other options not precluded
      FFS the benefits of implementing more beams per RRH panel
  UE parameter:
    1 beam per UE panel
    Other options not precluded
      FFS the benefits of implementing more beams per UE panel
WF (R4-2106100) approved in RAN4#98-bis-e:
  For Scenario-B Bi-directional RRH deployment:
    FFS the pros and cons between bi-directional deployment and uni-directional deployment
    FFS the potential issue of coverage when close to RRH locations.
    Schemes above can be used as starting points for further analysis

## Slide 9: Way Forward – Dual Uni-directional Deployment
Dual Uni-directional Deployment (Uni-directional Mode Operation in Two Opposite Directions):
  In this implementation-based scheme, the two UEs to operate in uni-directional mode but in two opposite directions;
  No standard impact observed if the operation in uni-directional deployment is introduced;
  Illustrated as the below figure:

## Slide 10: Way Forward – Signaling and Others
Dedicated network for roof-mounted CPE:
  RAN4 assume that in HST FR2 Scenario A and B, only high-speed CPEs installed on the roof of the train can be present in the network.
  No need to differentiate roof-mounted CPE from other FR2 UEs in HST FR2 scenario.
  Track curvature and impact on RRH separation
  Do not consider track curvature area in FR2 HST WI.

## Slide 11: Contributions List in RAN4#99-e
T-doc No. | Title | Company
R4-2110533 | Discussion on general issues for NR FR2 HST deployment scenario | Huawei, HiSilicon
R4-2111282 | TR for FR2 HST | Nokia, Nokia Shanghai Bell
R4-2109571 | On NR FR2 HST Deployment Scenario Discussion | Qualcomm, Inc.
R4-2109755 | Discussion on NR HST_FR2 scenario-A | ZTE Corporation
R4-2110234 | Further Discussion on FR2 HST Deployment Scenario-A | Samsung
R4-2110534 | Discussion on NR FR2 HST deployment Scenario-A | Huawei, HiSilicon
R4-2110728 | Further discussion on HST scenario A deployment | Ericsson
R4-2110952 | Discussion on FR2 HST Scenario-A deployment aspects | Intel Corporation
R4-2111493 | Discussions on HST FR2 Deployment Scenario A | Nokia, Nokia Shanghai Bell
R4-2110235 | Further Discussion on FR2 HST Deployment Scenario-B | Samsung
R4-2110535 | Discussion on NR FR2 HST deployment Scenario-B | Huawei, HiSilicon
R4-2110729 | Further discussion on HST scenario B deployment | Ericsson
R4-2110953 | Discussion on FR2 HST Scenario-B deployment aspects | Intel Corporation
R4-2111496 | Discussions on HST FR2 Deployment Scenario B | Nokia, Nokia Shanghai Bell

## Slide 12: Reference
[1] R4-2108453, “Email discussion summary for [99-e][328] NR_HST_FR2_Scenarios”, Samsung
[2] R4-2108694, “Email discussion summary for [99-e][328] NR_HST_FR2_Scenarios”, Samsung