## Slide 1: Way Forward on NR TxD & Power Class
vivo
3GPP TSG-RAN WG4 Meeting # #99-e
Electronic Meeting, 19th – 27th May., 2021
R4-210xxxx

## Slide 2: LS related - Applicable power class for capability signaling in different releases
Proposals:
  Option 1: Applies for all Power Classes for both Rel-15 and Rel-16
  Option 2: Applies for only PC2 for Rel-15, and for all power classes in Rel-16;
  Option 3: Others
Agreement(GTW): Option 1

## Slide 3: LS related - Relation with full power capability
Clarify the relationship between transparent TxD capability signalling and full Tx power capability
Proposals
  Option 1: No dependency
  Option 2: A UE can support only one of the two capabilities
      Agreements:
  [Option 1]

## Slide 4: LS related - Relation with SRS antenna switching
Clarify the relationship between transparent TxD capability signalling and SRS antenna switching
Proposals
  Option 1: No dependency
  Option 2: A UE that supports 1T2R antenna switching SRS should have at least one full power PA
    In another word, transparent TxD UE capable UE with an architecture of 23+23 for PC2, are not allowed to be 1T2R antenna switching capable
  Option 3: Others
      Agreements:
  [Option 1]

## Slide 5: LS related - Relation with Non-codebook based transmission
Clarify the relationship between transparent TxD capability signalling and non-codebook based transmission
Proposals
  Option 1: No dependency
  Option 2: Non-codebook based UEs required full power PAs per Tx chain for power efficient operation.
  Option 3: Others
      Agreements:
  FFS

## Slide 6: LS related - Relation with other multi-antenna features
Clarify the relationship between transparent TxD capability signalling and other multi-antenna features
Proposals
  Option 1: No dependency
  Option 2: A TxD capable UE can indicate support for a feature only if UE behavior and performance for the feature is unaffected by TxD capability.
  Option 3: Others
      Agreements:
  FFS

## Slide 7: Remaining Issues - MPR
Proposals
  Following offset range based on 1TX was proposed.
Agreements option 1 option 2
    Edge MPR for QPSK/16QAM (D1): [0.5~1.5]dB (D1): [0.5~3.0]dB
    Outer MPR for QPSK/16QAM (D2): [0.5~1.5]dB (D2): [0.5~2.5]dB
    Edge DFT-S MPR for 64QAM (D3): [0.5~1.5]dB (D3): [0.5~3.0]dB
    Outer/Inner DFT-S MPR for 64QAM (D4): [0.5~1.5]dB (D4): [0.5~2.0]dB
    CP-OFDM MPR for 64QAM (D5): [0.5~1.5]dB (D5): [0.5~2.0]dB
    Inner (other than High order) (D6): [0~0.5]dB (D6): [0~1.5]dB
    256QAM proposals marked in the table;
    Pi/2 BPSK currently leave unchanged
Agreement : Detail MPR values will be determined in next RAN4 meeting based on MPR simulation results
Modulation |  | MPR (dB) |  | 
 |  | Edge RB allocations | Outer RB allocations | Inner RB allocations
DFT-s-OFDM | Pi/2 BPSK | ≤ 3.5 | ≤ 0.5 | 0
 | QPSK | ≤ 3.5+D1 | ≤ 1+D2 | 0+D6
 | 16 QAM | ≤ 3.5+D1 | ≤ 2+D2 | ≤ 1+D6
 | 64 QAM | ≤ 3.5+D3 | ≤ 2.5+D4 | 
 | 256 QAM | ≤ 4.5 + [1] |  | 
CP-OFDM | QPSK | ≤ 3.5+D1 | ≤ 3+D2 | ≤ 1.5+D6
 | 16 QAM | ≤ 3.5+D1 | ≤ 3+D2 | ≤ 2+D6
 | 64 QAM | ≤ 3.5+D5 |  | 
 | 256 QAM | ≤ 6.5 + [2] |  | 

## Slide 8: Remaining Issues - TxD EVM spectrum flatness
Proposals
  Based on R4-2108793 with the following updated equation for composite equalizer:
      Agreements :
  [Suggestion Confirmed]

## Slide 9: Remaining Issues - Testing related issues
Proposals
  Option 1: Leave these discussions to RAN5 and not pursue them before agreement of RAN4 CR.
  Option 2: Continue discussion in RAN4.
      Agreements :
  [Option 1]

## Slide 10: Remaining Issues - TxD antenna and channel models
Proposals
  Option 1: No more discussion on these issues.
  Option 2: Further discuss the relevant antenna and channel models and their impact as part of, and prior to, concluding on conformance testing methodologies and reference receivers for TxD with conducted measurements.
      Agreements :
  [Option 1]

## Slide 11: Power class related- The Pcmax for NR for Rel-15 EN-DC
Proposals
  Option 1: The Pcmax for NR is modified to use the lower possible power class to decide the lower bound of the configured power. (Huawei)
  Option 2: The Pcmax for NR is modified according to the declared NR power capability for NSA so that the PHR becomes correct. (Ericsson)
  Option 3:Do not consider further refinements of Pcmax for NR.
  Option 4: Others
      Agreements :
  FFS

## Slide 12: Power class related- Fallback to 1-port Tx for SA in Rel-15
Proposals
  Option 1: Confirm ue-PowerClass should always be supported for 1-port transmission fall back mode for SA in Rel-15.
    UE do not support TxD capability would equip a full power chain
    For UE support TxD capability, when falls back to 1-port transmission, it is also reasonable to suppose it would use TxD to achieve ue-PowerClass in standalone mode
  Option 2: Others
      Agreements :
  Option 1
  [Rel-15 CR would be introduced to clarify the understanding]