## Slide 1: WF on introduction of lower 6GHz NR unlicensed operation for Europe
RAN4
Nokia, …

## Slide 2: General - Band plan
Proposals
  Option 1: Re-using already defined band n96 (HPE, Nokia, Intel, Skyworks, facebook, Charter, Apple, Qualcomm)
    FFS if additional notes and/or clarifications are needed. Regional specific requirements to be included in relevant specifications.
  Option 2: Defining a new band n[xx] (Ericsson, ZTE, Huawei)
    On top of specific requirements provided by ECC, the new band shall reuse requirements already defined for n96, where possible.
  Agreement:
    It is noted that 3GPP should not try to influence the regulation group.

## Slide 3: General - Band plan
Suggested WF from BT (HPE, Facebook (can accept), Apple (can accept)
  RAN4 waits for the EC assessment of EN 303 687 on 30th June.
  If the EC assessment decide 6GHz RLANs require additional receiver protection, then select option 2 (introduce a new NR-U band for Europe); otherwise select option 1 (re-used NR band n96).
  NOTE: 6 GHz WAS/RLAN devices within the scope of EN 303 687 are already covered by ECC and EU regulation as follows: ECC Decision (20)01on the harmonised use of frequency band 5 945 MHz to 6 425 MHz for WAS/RLAN

## Slide 4: General - LPI and VLP deployment
Agreement from GTW May 20th
  VLP deployment can be included in specification given the available regulations.
    Send LS to regulation to check if the BS is allowed. If there is problem, RAN4 will revisit the agreement.

## Slide 5: MPR
Agreement from GTW May 20th
  Merge/compromise the values from R4-2105383 and R4-2109430 to a combined proposal.
Combined proposal to be captured in TR:
Pre-coding | Modulation | RB Allocation | 
 |  | Full2 (dB) | Partial3 (dB)
DFT-s-ODFM | Pi/2 BPSK4 | ≤ 1.5 | ≤ 2.5
 | QPSK | 2.0 | [3.5]
 | 16 QAM | 2.5 | 4.0
 | 64 QAM | 3.5 | 4.5
 | 256 QAM | ≤ 5.0 | ≤ 5.5
CP-OFDM | QPSK | 3.5 | [4.5]
 | 16 QAM | 4.0 | [4.5]
 | 64 QAM | 5.5 | 5.5
 | 256 QAM | ≤ 7.0 | ≤ 7.0
NOTE 1: The A-MPR shall apply to all SCS in all active 20 MHz sub-bands contiguously allocated in the channel. The MPR applies to interlaced allocations with uplink resource allocation type 2 as specified in TS 38.214 [10]. NOTE 2: Full RB allocation A-MPR applies when all RB’s in a 20 MHz channel or all RB’s in all sub-bands for wideband operation are fully allocated and sub-bands are transmitted according to configuration A in Table 6.2F.2-2. NOTE 3: Partial RB allocation A-MPR applies when one or more RB’s in one or more sub-bands are not allocated or when the transmitted sub-bands for wideband operation are transmitted according to configuration B in Table 6.2F.2-2. NOTE 4: Applicable to Pi/2-BPSK modulation when IE powerBoostPi2BPSK is set to 0. NOTE 5: The A-MPR applies instead of MPR for 20 MHz channel centered at the nearest NR-ARFCN corresponding to 5955 MHz, 40 MHz channel at the nearest NR-ARFCN corresponding to 5965 MHz, 60 MHz channel at the nearest NR-ARFCN corresponding to 5975 MHz, and 80 MHz channel at the nearest NR-ARFCN corresponding to 5985 MHz. For all other channels, A-MPR is zero and MPR as specified in Table 6.2F.2-1 applies. |  |  |