3GPP WG RAN4 Meeting #98e	R4-21xxxxx

Electronic meeting, 19 – 27th May 2021.

Title:	[draft] LS on applicability of 3GPP NR-U Access Points in VLP mode

Response to:

Release:	Rel-17

Work Item:	NR_6GHz_unlic_EU

Source:	[Apple]

To:	ECC

Cc:	3GPP RAN

Contact Person:

Name:	Alexander Sayenko

Tel. Number:

E-mail Address:	asayenko@apple.com

Send any reply LS to:	3GPP Liaisons Coordinator, mailto:3GPPLiaison@etsi.org

Attachments:

1. Overall Description:

After the 3GPP RAN#90 meeting (December 2020), RAN WG4 has started normative work to enable support of the 5945-6425MHz frequency range according to the ECC Decision (20)01. The corresponding regulatory framework defines two modes: low power indoor (LPI) and very low power (VLP) indoor/outdoor. While for the LPI devices it is clearly stated that access points are allowed, for the VLP devices it is just mentioned that "The VLP outdoor use is intended to cover short range applications for small area direct communications" and "The VLP device is a portable device".

Since the 3GPP NR-U operation in the license-exempt spectrum is possible only between access point and client devices, we kindly request to clarify whether the VLP mode is applicable also to the 3GPP NR-U access points.

2. Actions:

ACTION: 	3GPP RAN WG4 kindly asks ECC to clarify whether the VLP mode is applicable not only to the client devices, but also to the 3GPP NR-U access point devices.

3. Date of Next WG4 Meetings:

RAN WG4 Meeting #100-e 	16th – 27th August 2021

RAN WG4 Meeting #101-e	01st – 12th November 2021.