## Slide 1: WF on introduction of NR-U intra-band ULCA requirements
Qualcomm Inc., …
R4-21xxxxx
3GPP TSG-RAN WG4 Meeting #99-e
Electronic meeting, 19 – 27 May 2021

## Slide 2: Background:
In [1], NR-U ULCA transmitter requirements such as SEM, ACLR and General Spurious Emissions were proposed
There were tentative agreements for ACLR and General Spurious Emissions
SEM needs further discussion

## Slide 3: WF - ACLR:
Agreement:
 | ACLR / Measurement bandwidth
CA ACLR | 27 dB
CA Measurement bandwidth (NOTE 1) | Nominal channel space+MBWACLR,low/2+ MBWACLR,high/2
Adjacent channel centre frequency offset (in MHz) | + BWChannel_CA / - BWChannel_CA
Difference between ACLR MBW center and Fc,low | MBWshift= (MBWACLR_CA-MBWACLR,low)/2
NOTE 1: MBWACLR,low and MBWACLR,high are the single-channel ACLR measurement bandwidths specified for channel bandwidths BWchannel(low) and BWchannel(high) in 6.5.2.4.1-1(see Appendix), respectively. | 
Table [2]: General requirements for intra-band contiguous NR-U CA ACLR

## Slide 4: WF – General Spurious Emissions:
Agreement:
Frequency Range | Maximum Level | Measurement bandwidth | NOTE
9 kHz ≤ f < 150 kHz | -36 dBm | 1 kHz | 
150 kHz ≤ f < 30 MHz | -36 dBm | 10 kHz | 
30 MHz ≤ f < 1000 MHz | -36 dBm | 100 kHz | 
1 GHz ≤ f < 12.75 GHz | -30 dBm | 1 MHz | 4
 | -25 dBm | 1 MHz | 3
12.75 GHz ≤ f < 5th harmonic of the upper frequency edge of the UL operating band in GHz | -30 dBm | 1 MHz | 1
12.75 GHz < f < 26 GHz | -30 dBm | 1 MHz | 2
NOTE 1: Applies for Band that the upper frequency edge of the UL Band more than 2.69 GHz NOTE 2: Applies for Band that the upper frequency edge of the UL Band more than 5.2 GHz NOTE 3: Applies for Band n41, CA configurations including Band n41, and EN-DC configurations that include n41 specified in clause 5.2B of TS 38.101-3 [3] when NS_04 is signalled. NOTE 4: Does not apply for Band n41, CA configurations including Band n41, and EN-DC configurations that include n41 specified in clause 5.2B of TS 38.101-3 [3] when NS_04 is signalled. |  |  | 
Aggregated Channel bandwidth | OOB boundary FOOB (MHz)
BWChannel_CA | BWChannel_CA + 5
Table [3]: Boundary between out of band and spurious emission domain for intra-band contiguous carrier aggregation
Table [4]: Requirement for general spurious emissions limits for NR-U CA

## Slide 5: WF – SEM:
Agreement for fully allocated Sub-bands for contiguous CC
  Only consider sub-bands being contiguous over 2CCs
Table [1]: General NR-U CA spectrum emission mask
Study SEM for partially or fully allocated sub-bands for non-contiguous CCs
    Only consider contiguous sub-bands in each CC
    Options:
      Consider restricting to contiguous sub-bands across the 2 CCs(No unused sub-band between scheduled sub-bands in each CCs.)
      Apply NR-U wideband operation single carrier mask per CC
      Apply a composite mask for in-gap emissions between CCs using the least restrictive emission requirement for each CC
    Other options not precluded
ΔfOOB (MHz) | Spectrum emission limit (dBr) | Measurement bandwidth
± 0 - 1 |  | [100kHz]3
± 1 - 5 | NOTE 1 | 1 MHz
± 5 - BWChannel_CA | NOTE 2 | 1 MHz
± BWChannel_CA – (BWChannel_CA +5) | -40 | 1 MHz
NOTE 1: Given as: where NOTE 2: Given as: where NOTE 3: The measured value shall be scaled by a factor equal to the ratio of the reference bandwidth (1 MHz) to the measurement bandwidth before the emission limit (dBr) is applied. |  | 
ΔfOOB (MHz) | Spectrum emission limit (dBr) | Measurement bandwidth
± 0 - 1 |  | [100kHz]3
± 1 - 5 | NOTE 1 | 1 MHz
± 5 - BWChannel_CA | NOTE 2 | 1 MHz
± BWChannel_CA – (BWChannel_CA +5) | -40 | 1 MHz

## Slide 6: References:
[1] R4-2111253 Introducing NR-U Intra-band UL CA UE RF requirements , Qualcomm Incorporated, R4#99-e
[2]