3GPP TSG-RAN WG4 Meeting #99-e							R4-21xxxxx revision of R4-2111475

# Electronic Meeting, May 19-27, 2021

Source: 	Qualcomm Incorporated

Title: 	Triple beat and 3ULCC MSD

Agenda item:	8.8.1

Document for:	Approval

# Introduction

In this document, we show if MSD is required for band combinations involving 3 UL CCs as summarized in the WF [1].

# Discussion

## Background or Problem Description

- Triple beat products can be generated and pose a problem even if coexistence requirements can be met.

- For 2UL CCs with a NR single carrier aggressor, the triple beat is simply a cross modulation issue, but there is not much of an issue due to the lower transmission BW not being large enough to exceed the duplex offset of the FDD band. Even if the transmission BW was large enough, the PSD level of the emission along with the filter attenuation of the TDD band TX blocker at the FDD RX/TX frequency was enough to quench the cross-modulation level for any observable impact. Even if this issue exists, it is yet to be reported in RAN4.

- With the advent of ULCA in the aggressor band, non-contiguous allocations can arise along with the wider end-end aggregated CA BW on top of the relatively weak TDD filtering, leaving some band combinations vulnerable to de-sense.

- We intend to flush out these band combinations and deep dive any potential MSD requirement.

## Triple Beat Detection and Vulnerable Band Combinations

- From the WID and the last meeting, the following band combinations arose.

- Using the triple beat detection criteria outlined in [1] [2], we can detect which band combinations show a potential problem.

- We define the jammer band as the band that contains the single carrier. That band can be a FDD or TDD band. If it is a TDD band, then there is no triple beat issue because the RX/TX are at the same frequency, and the triple beat product is always offset from the TX frequency of the jammer band.

- If the jammer band is a FDD band, then a problem exists when the triple beat noise is fully contained within the RXBW at the duplex offset. This happens for the 1RB+1RB in the ULCA configuration and the regular REFSENS configuration in the jammer/FDD band.

- The 1RB+1RB tone spacing can be further configured to optimally locate the noise with a minimum ULCA MPR taken to meet the general spurious/coexistence requirement. This can happen when the potential ULCA BW is large to enable that tone spacing variation flexibility.

- If the ULCA BW is small, then sometimes it takes a large jammer/FDD band channel BW to have triple beat detection. In this case the triple beat de-sense is mitigated due to larger back off taken due to the smaller ULCA BW and a correction factor due to partial overlap of the triple beat noise with the large RXBW.

- MSD analysis was done for the highlighted band combinations to further investigate the issue. Forward and reverse triple beat measurements were completed on a few PAs. The distortion is maximum on the PA generating the ULCA signal because the distortion varies 2:1 with ULCA output power and 1:1 with the FDD jammer power.

- Band combinations with the ULCA back off set at the minimum to meet the minimum general requirements had the highest MSD value. These band combinations are listed below:

- The actual diagram showing possible mechanisms coming into play is shown in Figure 1. PA forward and reverse triple beat mechanisms come into play as well as LNA non-linearity. The latter still needs some more investigation. PA measurements are provided in figure 2.

Figure 1: How triple beat impacts RF performance with coinciding IMD15

Figure 2: Forward and Reverse PA triple beat measurements with PA output at max power

- Key observations are as follows:

- Observation1: There is a possibility of a triple beat and IMD15 coinciding for DC_3A_n41C and DC_25A_n41C combinations.

- Observation2: Forward triple beat is more dominant than the reverse triple beat suggesting PCB isolation will be a key factor in lowering this interference

- Observation3: Triple beat is more dominant at the ULCA PA because the triple beat product goes as 2:1 with ULCA output power and only 1:1 with FDD TX power

- Observation4: Reverse triple beat at the FDD PA can be neglected. Forward triple beat at the FDD PA maybe neglected pending more measurements on PAs from other bands.

- Observation 4: Triple beat is affected by the RX LNA as well as the PA and analysis and measurements for RX will be updated during the meeting.

## RX Measurements ans Analysis

In consideration of observation 4 and from the diagram in figure 1, it can be observed that the triple beat product can be generated at the ULCA PA as well as RX LNAs. Preliminary measurements and analysis were recorded the generated triple beat product. For large ULCA BWs such as n41C, the tone spacing can be reduced such that the emission requirements are satisfied at a much a higher TX power, so the back-of number for TX becomes relevant, especially when looking at the RX LNA contribution. For n41C in China, the inner MPR value can be used, and then more back-off is subsequently provided to meet the power class. For n41C in US, the back off for IMD3 levels below -25dBm/MHz must be used. Table 2.3-1 shows basic MRC analysis and triple beat contributions across components. The analysis shows the triple beat at the RX LNA dominates and for the 3A_n41C, 25A_n41C combinations, the IMD15 coincide with the triple beat. Table 2.3-2 shows the triple beat for PC2 capable bands where you have the case for PC2 case b, where FDD+TDD= 23dBm+26dBm for a total of 26dBm.

Table 2.3-1: Triple beat contribution to MSD for PC3

Table 2.3-2: Triple beat contribution to MSD for PC2 capable bands

## Triple Beat MSD and specification

Table 7.3B.2.3.5.3-1: MSD test points for PCell due to dual uplink operation for EN-DC in NR FR1 (two bands)

| NR or E-UTRA Band / Channel bandwidth / NRB / MSD |
| --- |
| EN-DC Configuration | EUTRA or NR band | UL Fc (MHz) | UL/DL BW (MHz) | UL LCRB | DL Fc (MHz) | MSD (dB) | Duplex mode | Triple beat order |
| DC_3A-n41C | 3 | 1782.5 | 5 | 25 | 1877.5 | [FFS] | FDD | 3 |
|  | n41C | 2545 2595 | 50 50 | 1 (RBstart=0) 1 (RBstart=250) | 2545 2595 | N/A | TDD | N/A |
| DC_25A-n41C | 25 | 1912.5 | 5 | 25 | 1992.5 | [FFS] | FDD | 3 |
|  | n41C | 2545 2595 | 50 50 | 1 (RBstart=0) 1 (RBstart=250) | 2545 2595 | N/A | TDD | N/A |
| DC_8A-n79C | 8 | 912.5 | 5 | 25 | 957.5 | [FFS] | FDD | 3 |
|  | n79C | 4545 4595 | 50 50 | 1 (RBstart=0) 1 (RBstart=250) | 4545 4595 | N/A | TDD | N/A |

Proposal 1: Use MSD for triple beat structure as shown in Table 7.3B.2.3.5.3-1 and consider preliminary MSD values proposed in Table 2.3-1 and Table 2.3-2 pending further investigation.

# Conclusion

Observation1: There is a possibility of a triple beat and IMD15 coinciding for DC_3A_n41C and DC_25A_n41C combinations.

Observation2: Forward triple beat is more dominant than the reverse triple beat suggesting PCB isolation will be a key factor in lowering this interference

Observation3: Triple beat is more dominant at the ULCA PA because the triple beat product goes as 2:1 with ULCA output power and only 1:1 with FDD TX power

Observation4: Reverse triple beat at the FDD PA can be neglected. Forward triple beat at the FDD PA maybe neglected pending more measurements on PAs from other bands.

Observation 4: Triple beat is affected by the RX LNA as well as the PA and analysis and measurements for RX will be considered in the next meeting.

Proposal 1: Use MSD for triple beat structure as shown in Table 7.3B.2.3.5.3-1 and consider preliminary MSD values proposed in Table 2.3-1 and Table 2.3-2 pending further investigation.

# References:

- R4-2105335, “Way forward on analysis and framework of triple beat issue of  3CC UL with contiguous intra band UL CA“, Qualcomm, 3GPP RAN4$98-bis-3

- R4-2