## Slide 1: WF on REFSENS Table Split and Simplification
Apple
3GPP TSG-RAN WG4 Meeting #99-e
Electronic Meeting, May 19th – 27th, 2021
R4-21xxxxx

## Slide 2: Background
Due to the gradual introduction of brand new FR1 channel bandwidths, the REFSENS table based on the current format in TS 38.101-1 Table 7.3.2-1 has expanded substantially in horizontal direction and gone beyond the word document page width which has caused REFSENS requirements virtually unreadable in both Rel-16 and Rel-17 specifications as illustrated below where band numbers have become invisible.

## Slide 3: Background
To mitigate the current FR1 REFSENS table readability issue and accommodate more potential new channel BWs in future [1], in this meeting, a few methods for FR1 REFSENS table simplification based on equation-based representation for TDD bands only or all FR1 bands were proposed:
  Option 1: One table for TDD bands (equation-based REFSENS) and the other table for FDD and SDL bands (explicit REFSENS values) [2]
  Option 2: One table for all FR1 bands without MSD (equation-based REFSENS) and the other table for FDD bands with MSD (MSD is additive to the same band with equation-based REFSENS) [3]
  Option 3: One table for all FR1 bands (unified equation-based REFSENS) [4]
Issue for equation-based REFSENS table format on RAN5 specifications impact was also raised in this meeting [5].
  A variant of REFSENS table structure for TDD bands based on band grouping was proposed. The explicit TDD band REFSENS values however does not resolve the horizontal table dimension issue.

## Slide 4: Way Forward
Based on the tentative agreement in [99-e][121] email discussions [6], equation-based representation is used to simplify the FR1 REFSENS table format.
Decide the simplification of FR1 REFSENS table format based one of the following options in next RAN4 meeting:
  Option 1: One table for TDD bands (equation-based REFSENS) and the other table for FDD and SDL bands (explicit REFSENS values) [2]
  Option 2: One table for all FR1 bands without MSD (equation-based REFSENS) and the other table for FDD bands with MSD (MSD is additive to the same band with equation-based REFSENS) [3]
  Option 3: One table for all FR1 bands (unified equation-based REFSENS) [4]
Companies are encouraged to assess whether equation-based REFSENS representation would have impact on RAN5 specifications.
  Notice that equation-based representation has been applied in some UE RF requirements, such as ACS requirements.

## Slide 5: References
[1] R4-2105365 “WF on REFSENS Table Split and Simplification”, Apple (98bis-e)
[2] R4-2110160 “CR for TS 38.101-1: FR1 REFSENS table split and simplification”, Apple (99-e)
[3] R4-2111538 “FR1 FDD SDL REFSENS Table Simplification”, Skyworks Solutions Inc. (99-e)
[4] R4-2109418 “A unified equation for specifying REFSENS for both TDD and FDD bands”, ZTE (99-e)
[5] R4-2111149 “REFSENS table structure, band groups”, Ericsson (99-e)
[6] R4-2107647 “Email discussion summary for [99-e][121] NR_FR1_35MHz_45MHz_BW”, 1st round (99-e)