## Slide 1: WF on PC2 intra-band UL NC CA architecture options and MPR requirements
Skyworks Solutions Inc., …
R4-210xxxx
3GPP TSG-RAN WG4 Meeting #99-e
Electronic meeting, 19 – 27 Apr. 2021

## Slide 2: GTW agreements
Agreement:
Further evaluate all the optional architectures to ensure the performance is not worse than PC3, considering
  MPR values
  In-gap relaxation requirements and applicable conditions
  Regulations, considering
    n77 PC2 with n48 in-gap, (to check if it is valid use case or not)
  Swapping time for Arch#4
  In-gap exception requirements (only for ACLR) for Rel-16 legacy power class 3 UE

## Slide 3: Background: architecture cases and attributes
Arch | description | Additional RF requirement | Architecture attributes | MPR
#1 | 2x26dBm PA + 2LO with 100MHz BW |  | Can cover all BW separation cases without scheduling restriction and support PC1.5 and single CC and contiguous 2CC UL MIMO Needs >2PA to support non-contiguous 2CC UL MIMO or use #2 with two PAs | Best
#2 | 1x26dBm PA + 1LO with 200MHz BW | In-gap requirement when LO or image fall inside | Only applicable to BW separation up to 200MHz Can support single and two contiguous or non-contiguous CC UL-MIMO if second PC2 PA (same as #1) | Worst (bust slightly less than #3 thanks to 31dB ACLR linearity and no RIMD) and depending on in-gap requirement may need additional MPR cases
#3 | 2x23dBm PA + 1LO with 200MHz BW | In-gap requirement when LO or image fall inside | Only applicable to BW separation up to 200MHz Can support single CC and 2CC contiguous or non-contiguous UL MIMO | Worst (both FW and Reverse IMD, lower linearity than PC2 PA) and depending on in-gap requirement may need additional MPR cases
#4 | 1x23dBm + 1x26dBm + 2LO with 100MHz BW | PA swap time | Can cover all BW separation cases with scheduling restriction or power limitation in secondary cell Can Support single CC UL-MIMO. Needs >2PA to support simultaneous 2CC UL MIMO | 1.5dB worse vs best but further losses if swap time is >15us

## Slide 4: WF on architectures and MPR
All architectures have their limitations and those providing the best MPR do not readily support UL MIMO concurrently with UL CA
PC2 MPR shall provide benefits over PC3 in actually reaching higher power without additional restriction
WF: all 4 architectures are pursued for evaluation
One LO architectures (#2 and #3) are further checked for exceptions and have a dedicated MPR table to enable simultaneous UL CA + UL MIMO with 2 transmit paths.
Two LO architectures (#1 and #4) MPR is evaluated separately and the decision on using the same or separate MPR tables or delta MPR for #4 is based on:
  PC2 MPR providing significant improvement vs PC3
  Further discuss how to consider the PA swapping time for #4 and its impact to performance versus PC3
    Either impact of swap time is negligible (<CP – MRTD - usec)
    Or Scell is allowed to reach only PC3 (no swap) but MPR including delta MPR provides at least 1.5dB higher total power vs PC3

## Slide 5: WF on regulation aspects for exceptions needed for architecture #2 and #3
Operators are encouraged to provide input whether 3dB ACLR or carrier and image leakage SEM relaxation complies with regulation:
  Per country/region
  Depending on deployment (co-located, synchronous…)
  Depending on the relaxation level
For n77(2A) PC2 in the US whether the use-case where :
  First CC is in 3.45-3.55GHz
  And Second CC is in 3.7-3.98GHz
  And image leakage falls in 3.55-3.7GHz range (n48 frequency range)
  Is compliant with regulation
  Note that given that the gap is 150MHz and architecture #2 and #3 only support 200MHz total the aggregated BW is limited to 50MHz max.

## Slide 6: WF on in-gap relaxation for architectures #2 and #3
Aside from the regulation check that is needed:
Unless lower Image leakage is assumed (better than 28dB) the ACLR relaxation of 3dB is not sufficient for PC2 as it leaves no room for non-linearity contribution
WF: relaxation of 4dB or better image assumptions are decided at next meeting
Image leakage can result in significant interference to in-gap carriers and is probably not acceptable in all deployment scenarios:
WF: for next meeting mitigation or deployment restrictions are further studied:
  Restricting to gap < aggregated BW (in gap SEM limited to -13dBm/MHz)
  Restricting to the two respective configured CC sizes to be the same(in a symmetric fashion)
  Allow exception to SEM but at a defined dBm/MHz level and based on improved image leakage
  Only allow in co-located scenario and/or if the affected spectrum belongs to the same operator (may imply signaling)
Carrier leakage being less harmful:
WF: remove exception from PC3 based on improved carrier leakage level

## Slide 7: References:
[1] R4-2108799 26+23 dBm w 2LOs and 1LO architecture considerations, Qualcomm Incorporated, R4#99-e
[2] R4-2109260 PC2 1PA Intra-band UL NC CA MPR Simulations, Nokia, Nokia Shanghai Bell, R4#99-e
[3] R4-2109261 PC2 1PA Intra-band UL NC CA MPR, Nokia, Nokia Shanghai Bell, R4#99-e
[4] R4-2109965 MPR results for NR PC2 intra-band non-contiguous CA UE according to RF architecture, LG Electronics, R4#99-e
[5] R4-2110820 R17 FR1 UL NC CA, OPPO, R4#99-e
[6] R4-2111384 intra-band UL NC CA architecture and MPR, Huawei, HiSilicon, R4#99-e
[7] R4-2111480 Input on exceptions for non-baseline PC2 NC UL CA architectures, Skyworks Solutions, Inc. , R4#99-e