## Slide 1: WF on intra-band UL contiguous CA for UL MIMO
Huawei, HiSilicon, []
R4-210XXXX
3GPP TSG-RAN WG4 #99-e
May 19 – 27, 2021
Electronic meeting

## Slide 2: GTW agreement
Agreement:
  Option 3 for MIMO configurations for CA+UL MIMO requirements:
  2 layer configuration , 1 layer 2 port configuration and transparent TxD configuration are all considered
    If we find the problematic case, we could revisit the agreement.
Follow the single CC requirements as baseline
  Identify the UL-MIMO+CA specific requirements
  Refer to the CA requirement, e.g., configured output power, power control tolerance, if needed

## Slide 3
RF requirements Structure for CA+MIMO
CA+MIMO RF requirements are defined in new sub clausea that with dedicated suffix
  To avoid replication wording, structure the CR as deviation from existing CA and MIMO requirements
For EVM requirement, follow the single CC requirements defined in 6.4D.2
  If anything update in TS 38.101 for single CC UL MIMO, further revise corresponding part for CA+MIMO
For transmit on/off time mask, follow single carrier agreement made in thread [159]: Transmit ON/OFF time mask requirements for UL MIMO are defined at each antenna connector

## Slide 4
MPR requirement for CA+MIMO
Candidate Reference RF architectures for CA+MIMO MPR requirements:
  For Power class 3: 2*23dBm PA +1LO
  For Power class 2: 2*23dBm PA +1LO
  For Power class 2: 2*26dBm PA +1LO
RAN4 to further study on MPR requirements based on the reference architecture focused on following aspects:
  How much delta MPR induced by RIMD and emissions sum up on both connectors, compared with PC3 contiguous CA MPR in TS 38.101
  Other evaluations on MPR based on the reference architectures are not precluded

## Slide 5: Signalling
In RAN4 #99-e meeting, it is proposed to Report the UE supported aggregated CBW for UL CA+UL MIMO feature to NW.
RAN4 further check whether new capability signalling is needed for CA+MIMO and decide in next RAN4 meeting.

## Slide 6
Reference
[1]
[2]