## Slide 1: 3GPP TSG-RAN WG4 Meeting #99-e Electronic Meeting, 19 – 27 May, 2021
Huawei, HiSilicon
WF on UE PRS measurement requirements
R4-21xxxxx

## Slide 2: Measurement period for RSTD (1)
Upper bound of N_muting
  If Tprs * dl-PRS-MutingBitRepetitionFactor-r16 > 10240 ms
    N_muting = 1 (effectively no type1 muting)
  else
    N_muting = X * dl-PRS-MutingBitRepetitionFactor-r16, where
    X = min( L, 10240/( Tprs * dl-PRS-MutingBitRepetitionFactor-r16 ) ) and
    L is the size of NR-MutingPattern-r16 for mutingOption1-r16.
  FFS requirement applicability
  FFS further enhancement for the case where Tprs * dl-PRS-MutingBitRepetitionFactor-r16 * L < 10240
FFS whether option 2 muting is already accounted in the requirements or additional clarification is needed

## Slide 3: Measurement period for RSTD (2)
Observation window for LPRS is Tavailable_PRS,i
  This can be revisited if any technical issue is identified based on outcome of relation between the observation windows of Lprs and UE processing capability ‘N’
FFS Relation between the observation windows of Lprs and UE processing capability ‘N’
  Option 1 (Nokia)
    A UE needs to use the observation window for N same as LPRS,i observation window that was agreed as the aggregating duration of all the PRS resources that fall within MGs and are not muted.
    If the window T ms is not set same as the window LPRS,i, the requirement applies another scaler as , where P is the observation window of LPRS,i period.
  Option 2 (CATT, HW)
    No relation between the two observation windows
LPRS,i does not have to be same as K defined in 38.214 clause 5.1.6.5
Replace LPRS,i with or and clarify that it is calculated in the same way as PRS duration K defined in TS 38.214 clause 5.1.6.5.

## Slide 4: Measurement period for RSTD (3)
FFS measurement period when UE is configured with concurrent NR positioning methods, e.g. RSTD for DL-TDOA and PRS-RSRP for DL-AoD
  Option 1a (ZTE, OPPO)
    RSTD measurement period is not impacted by the PRS-RSRP measurement configured for another positioning method, if they are measured on the same set of PRS resources.
  Option 1b (CATT, Nokia, vivo, OPPO, Intel, ZTE)
    RSTD measurement period is not impacted by PRS-RSRP measurement.
  Option 2a (HW)
    When UE is configured measurement for more than one positioning requests, the measurement period for each requests can be longer than measurement period when UE is configured measurement for that single positioning request.
  Option 2b (Ericsson)
    When PRS-RSRP and RSTD are configured using separate OTDOA assistance data then the measurement periods of RSTD and PRS-RSRP may be different.
  Option 2c (QC, vivo, HW, OPPO)
    RAN4 not to specify requirements for scenarios involving concurrent NR positioning methods in Rel-16.
    Measurement period requirements in TS 38.133 sections 9.9.2.5, 9.9.3.5 and 9.9.4.5 do not apply when there are concurrent positioning requests. If there are concurrent positioning requests the starting point and duration of the measurement period may be different.
  Option 2d (OPPO, Ericsson)
    PRS measurement requirements do not apply when UE is configured PRS measurement for more than one positioning methods with different sets of PRS resources to measure.

## Slide 5: Measurement period for RSTD (4)
MG reconfiguration per UE request
  RAN4 does not specify the exact measurement period extension due to MG reconfiguration during the measurement period
  Add the following text to TS 38.133 sections 9.9.2.5, 9.9.3.5 and 9.9.4.5:
    Option 1 (Intel, QC, CATT, vivo, HW, OPPO, Ericsson):
      If during the measurement period of one or more positioning frequency layers, the MG pattern is reconfigured, the measurement period can be longer.
    Option 2 (Nokia):
      If the MG pattern is reconfigured during the measurement period of one or more positioning frequency layers, the measurement period requirement is not applicable.
    Option 3 (ZTE):
      If during the measurement period of one or more positioning frequency layers, the MG pattern is reconfigured (at most once for each positioning frequency layer) to enable UE to measure DL PRS resources, the measurement period can be longer.
  For MG reconfiguration during measurement period not per UE request, apply same requirements as MG reconfiguration based on UE request.

## Slide 6: CSSF (1)
CSSF calculation is based on Rel-15 per MG occasion approach
For CSSF calculation for a positioning frequency layer, in each MG occasion
    Only RRM frequency layers are considered, and no other PFL is considered
    For a PFL that satisfies the long periodicity condition, CSSF = 1
For CSSF calculation for an RRM frequency layer, in each MG occasion
    Only one PFL is considered
    When multiple PFLs are configured, FFS which PFL is assumed measured.
FFS CSSF calculation for an RRM frequency layer when multiple PFLs are configured.

## Slide 7: CSSF (2)
  Define the long periodicity condition as Tavailable_PRS,i > 160 ms (or >=320ms)
  Applicability condition for long periodicity measurement
  Option 1 (QC, vivo)
    Measurement requirements apply even if some of the PRS resources in the PFL can be measured with periodicity shorter or equal to 160 ms. i.e. all of the PRS resources would be measured with high priority (CSSF = 1).
  Option 2 (OPPO, HW, Intel, CATT, Ericsson, Nokia)
    Measurement requirements do not apply if some of the PRS resources in the PFL can be measured with periodicity shorter or equal to 160 ms. i.e. none of the PRS resources in the PFL would be measured.

## Slide 8: CSSF (3)
Calculation of parameter Ri is defined same as in Rel-15
  This can be revisited if any technical issue is identified based on outcome of selection of one PFL in CSSF calculation.

## Slide 9: Requirements applicability considering UE capability (1)
  The measurement requirements do not apply for a PRS resource, if time span of the PRS resource instance (including at least the minimum number of repetitions specified in the accuracy requirements) is greater than UE reported capability N.

## Slide 10: Requirements applicability considering UE capability (2)
  If the time span of a DL PRS resource instance (including at least the minimum number of repetitions specified in the accuracy requirements) is greater than the configured measurement gap length excluding RF switching time, then measurement requirements do not apply for the PRS resource instance.

## Slide 11: Requirements applicability considering UE capability (3)
  PRS resource being overlapped with (or fully covered by) MG
  Option 1 (QC)
    The measurement requirements apply for a PRS resource only if at least the minimum number of repetitions specified in the accuracy requirements are covered by the MGL excluding RF switching time.
  Option 2 (vivo)
    If at least part of the PRS resource including at least the minimum number of repetitions specified in the accuracy requirements is fully covered by MGL, then the PRS resource is considered being fully covered by MGL.
  Option 3 (HW)
    A PRS resource is considered to be fully (partially) overlapped with MG if all (some) of its instances are overlapped with an MG occasion.
    A PRS resource instance is considered to be overlapped with an MG occasion if the minimum number of repetitions of the instance is fully covered by the MGL excluding RF switching time, where the minimum number is given in the accuracy requirements.

## Slide 12: Measurement period for PRS-RSRP
Applicable requirements for PRS-RSRP configured for DL-TDOA
  Option 1 (HW, Nokia, Intel)
    Requirements for RSTD in clause 9.9.2 apply
  Option 2a (ZTE, vivo, OPPO, Ericsson)
    Requirements for PRS-RSRP in clause 9.9.3 apply
  Option 2b (OPPO)
    Current requirements in clause 9.9.3 also apply for the case when PRS-RSRP is measured for DL-TDOA, except the following scenarios:
      If handover occurs while PRS-RSRP measurements for Multi-RTT are being performed, or
      If other cell change impacting SRS configuration occurs while PRS-RSRP measurements for Multi-RTT are being performed
      When PRS-RSRP is configured for multi-RTT, UE Rx-Tx time difference and PRS-RSRP measurements are performed over the same measurement period

## Slide 13: Measurement period for UE Rx-Tx (1)
Value of X in PRS/SRS proximity condition
  Option 1 (ZTE, QC, HW)
    80ms
  Option 2 (CATT, Nokia, OPPO, vivo, Ericsson, HW)
    160ms
  UE behavior and requirements when proximity condition is not met
  Proposals for UE behaviour
    Option 1 (ZTE, CATT, Nokia, OPPO, vivo, HW)
      The UE should still measure and report UE Rx-Tx measurement even if PRS/SRS proximity condition is not met
    Option 2 (QC, Ericsson)
      Up to UE implementation
  Proposals for requirements
    Option 1a (CATT, Ericsson)
      UE Rx-Tx time difference accuracy requirements may not apply
    Option 1b (Nokia)
      Accuracy requirement impact can be FFS.
    Option 2 (QC, Ericsson, HW)
      UE Rx-Tx time difference measurement requirements do not apply.
  In RRM tests, test case setup should ensure that the PRS/SRS proximity condition is met

## Slide 14: Measurement period for UE Rx-Tx (2)
TA change due to TA command
  Proposals for UE behaviour
    Option 1 (Intel, CATT, Nokia, HW)
      UE shall continue UE Rx-Tx time difference measurement
    Option 2 (OPPO, vivo, Ericsson)
      UE shall discard the UE Rx-Tx time difference measurement
  Proposals for requirements
    Option 1 (CATT, Intel, Nokia, HW)
      UE Rx-Tx measurement period requirements are not impacted
    Option 2 (QC, OPPO, vivo, Ericsson)
      UE Rx-Tx time difference measurement requirements are not applicable

## Slide 15: Measurement period for UE Rx-Tx (3)
TA change due to NTA_offset change
  Proposals for UE behaviour
    Option 1 (vivo, Ericsson)
      UE shall discard the UE Rx-Tx time difference measurement
  Proposals for requirements
    Option 1a (CATT, HW)
      No need to clarify UE Rx-Tx measurement requirements in case of NTA_offset change
    Option 1b (HW, Intel)
      UE Rx-Tx measurement period requirements are not impacted
    Option 2 (QC, OPPO, vivo, Ericsson, Intel)
      measurement requirements are not applicable if the NTA_offset changes during the measurement period

## Slide 16: Measurement period for UE Rx-Tx (4)
Measurement period requirements with cell change impacting SRS
  Option 1 (ZTE, CATT, OPPO, vivo, Ericsson, HW, Nokia)
    UE shall restart the UE Rx-Tx time difference measurement after the SRS reconfiguration on the target cell is complete.
  Option 2 (QC, Intel, HW)
    UE Rx-Tx measurement requirements do not apply. The UE may resume the measurements after SRS is configured in the target cell
Measurement period requirements with cell change not impacting SRS
  Option 1a (ZTE, CATT, vivo, Ericsson, HW, Intel, Nokia)
    UE shall continue the on-going UE Rx-Tx time difference measurement, and the current measurement period and accuracy apply.
      CATT: no need to capture it in the specification
  Option 1b (OPPO, Ericsson)
    UE shall continue the on-going UE Rx-Tx time difference measurement, and longer measurement period is expected.
  Option 2 (QC)
    FFS