## Slide 1: WF on RLM/BFD relaxation for UE Power Saving enhancements (All agreements in RAN4#99-e in email thread #231)
MediaTek
3GPP TSG-RAN WG4 Meeting #99-e R4-2108351
Electronic Meeting, May. 19-27, 2021.
Agenda Items: 9.13

## Slide 2: General
Strive to send LS to RAN2 for RAN4’s agreement on low mobility criteria in the next meeting as agreed work plan

## Slide 3: Relaxation Scenarios
Issue 2-1-3: Relaxation for deployment scenarios
Relaxed BFD/RLM requirements shall be supported for all deployment scenarios supported by current specification which includes: NR SA, EN-DC, NE-DC, NR intra-band CA, NR inter-band CA and NR-DC.

## Slide 4: Entering Relaxation criteria
Issue 2-2-1: Good serving cell quality criteria for RLM/BFD: the radio link quality metric for RLM
  UE reuse the SINR for RLM/BFD evaluation when determine whether the serving cell quality criteria is fulfilled or not
  FFS: what is the SINR definition UE uses L1-RSRP for BFD evaluation when determine whether the serving cell quality criteria is fulfilled or no
  FFS whether RSRP is also needed for RLM/BFD as additional condition
Issue 2-2-2: Good serving cell quality criteria for RLM/BFD: predefined or configured threshold
  Option A: The thresholds are configured to the UE by the network based on a set of discrete threshold values.
    FFS: based on a set of discrete threshold values.
  Option B: The thresholds can be pre-defined.

## Slide 5: Entering Relaxation criteria
Issue 2-2-5/2-2-6: Low mobility criteria of RLM/BFD relaxation
UE verifies whether the low mobility criterion is fulfilled or not based on the RSRP variation and/or SINR variation, provided that the variation thresholds are configured by the NW.
FFS the variation thresholds for low mobility criterion
  Option 1: RSRP variation
  Option 2: SINR variation
  Option 3: RSRP variation and SINR variation.
FFS how to calculate the variation

## Slide 6: Exiting Relaxation criteria
Issue 2-3-1: Exiting criteria of RLM/BFD relaxation – Basic
FFS the following options, which have been discussed in this meeting.
Option 1: exit relaxation mode at least when any entering relaxation criterion is not met
  Option 1a: If the UE fulfills any of serving cell quality exit condition or low mobility exit condition, or DRX cycle length is NOT allowed for relaxation, UE will exit relaxation mode.
  Note1: Whether the exit condition for serving cell quality is explicitly specified or not is up to issue 2-3-2.
  Note2: FFS the details of the exit condition of low mobility’
Option 2: if entering condition SINR threshold is larger than exit condition SINR threshold, UE can stay in relaxation mode when SINR is below entering condition but above exit condition. If exit condition is violated, UE should exit relaxation mode.
FFS the observation period for the exiting criteria

## Slide 7: Exiting Relaxation criteria
Issue 2-3-2: Exiting criteria of RLM relaxation – Additional
FFS the following options, which have been discussed in this meeting.
  Option 1: exit relaxation mode when the radio link quality of the serving cell is worse than a certain threshold, which is higher than Qout.
    Option 1a: a hysteresis value could be used to avoid ping-ping effect, e.g. SINRexit = SINRenter - 3dB
    Option 1b: SINRexit = Qout + 7dB
    Option 1c: SINRexit = Qout +Margin or SINRexit = Qin
    Option 1d: The threshold can be configured by network with margin
  Option 2: exit relaxation mode when the radio link quality is worse than Qout, and the UE is still in the relaxation mode when the radio link quality is better than Qout.
    Option 2b: UE shall revert to non-relaxed RLM/BFD measurement and evaluation period at the 1st Qout based on relaxed RLM/BFD measurements and evaluation period.
  Option 3: Leave the fall back mechanism as UE implementation, as long as UE makes sure it has already fallen back to normal measurement if it has identified one out-of-sync indication.
  Option 4: exit when certain consecutive out-of-sync indications

## Slide 8: During Relaxation
Issue 2-4-0: UE behaviour when the measured SINR is worse than Qout during the relaxation mode
FFS whether it would happen if the threshold for exiting criteria is defined as a certain value higher than Qout
FFS the following options
Option 1:
  UE is required to send the first OOS indication to higher layers and required to start N310 immediately
  The evaluation period of the first OOS indication is the relaxed evaluation period in the relaxation mode.
  For information, assuming the relaxation factor is K,
    the fist OOS evaluation period is K*T_evaluate_out_SSB,
    the observation period for the exit criteria is K*T_evaluate_out_SSB.
Option 2:
  UE is not required to send the first OOS indication to higher layers.
    The OOS indication based on relaxed measurement is not sent to higher layers.
  After exit, UE is required to send the first OOS indication after normal evaluation period if SNR<Qout. The evaluation period of the first OOS indication is the summation of the evaluation period in the relaxation mode + normal evaluation period.
  For information, assuming UE is applying RLM/BFD measurement relaxation the relaxation factor is K,
    given the fist OOS evaluation period is 2*T_evaluate_out_SSB,
    the observation period for the exit criteria is T_evaluate_out_SSB. The power saving gain when applying RLM/BFD relaxation with relaxation factor of K is achieved by using less samples for exit criteria evaluation. Measurement accuracy needs to be investigated
Option 3: UE follows the legacy behaviour for sending OoS indications. RLM/BFD behavior shall apply

## Slide 9: During Relaxation
Issue 2-4-2: Relaxed evaluation period of RLM/BFD
FFS the following options, which have been discussed in this meeting.
Option 1: The similar definition of RLM/BFD evaluation period in Rel-15 can be reused as Max(T, Ceil([Y] x P x N) x Max(TDRX, TRLM-RS/BFD-RS)).
  FFS the Y
Option 2a: For FR1, If power saving conditions are satisfied, allow TEvaluate_ps_out_SSB for the first OOS indication and the original TEvaluate_out_SSB doesn’t apply.
Option 2b: For FR1 and FR2, If power saving conditions are satisfied, for the first OOS indication the original TEvaluate_out_SSB apply.
Option 3: extended based on the legacy RLM/BFD requirements by considering the scaling factors.
  the new evaluation period TEvaluate_out_SSB-Relaxed is specified as K1* TEvaluate_out_SSB, where TEvaluate_out_SSB is as specified in clause 8.1.3.2 in TS 38.133 .
  FFS the new indication period TIndication_interval-Relaxed is specified as K2* TIndication_interval where TIndication_interval is as specified in clause 8.1.6 in TS 38.133.
Option 4 :
  For RLM, the oos triggering latency requirements should be extended with an additional delay not shorter than (K-1) 1.5 DRX cycles, while K is the relaxation factor.
  For BFD, the beam failure instance triggering latency requirements should be extended with an additional delay not shorter than (K-1) 1.5 DRX cycles, while K is the relaxation factor.
  Extending the out-of-sync evaluation period requirements and beam failure evaluation period requirements by a same factor X can be considered. X can be 2 for DRX <= 40ms, and X can be 1.5 for 40ms <DRX <= 80ms.

## Slide 10: During Relaxation
Issue 2-4-3: Relaxation scheme and specification impact
FFS
  Option 1: Relaxed RLM/BFD requirements are introduced in new subsections within the existing RLM/BFD sections TS 38.133.
  Option 2: no new subsection only for short DRX
Issue 2-4-4a: Different Relaxation factors between FR1 and FR2
Different Relaxation factors are allowed for FR1 and FR2.
  FFS whether to apply different relaxation factors for SSB and CSI-RS based evaluations in FR2

## Slide 11: Other aspects
Issue 2-5-1/2: Entering and exiting relaxation mode in intra-band CA
FFS whether or not RAN4 to specify RLM/BFD relaxation for the scenario that “CSI-RS based RLM on SpCell and CSI-RS based BFD in SCell in the same band.”
FFS:
  For intra-band CA with CSI-RS based RLM/BFD, if UE has fulfilled the criterion for operating RLM/BFD in relaxed mode in one serving cell, then it is allowed to operate RLM/BFD in relaxed mode in all other serving cells if same type of RS are used for RLM/BFD in the serving cell and other serving cells.
  For intra-band CA with CSI-RS based RLM/BFD, if UE meets the conditions of reverting to the normal RLM/BFD in one serving cell, it is expected the reversion operations are applied to all other serving cell(s) if same type of RS are used for RLM/BFD in the serving cell and other serving cells.
Issue 2-5-3: Entering and Exiting Relaxation criteria for multiple RLM-RS/BFD-RS
FFS
  Option 1:
    radio link quality is better than the threshold (Qout + X1) for any RLM-RS resource.
    The exiting condition of RLM relaxation for multiple RLM-RS resources can be defined as when the radio link quality is worse than the threshold (Qout + X2) for all the RLM-RS resources.
    FFS X1, X2
  Option 2:
    radio link quality is better than the threshold (Qout + X1) for all RLM-RS resource.
    The exiting condition of RLM relaxation for multiple RLM-RS resources can be defined as when the radio link quality is worse than the threshold (Qout + X2) for any the RLM-RS resources.
    FFS X1, X2