Title: Report of the 3GPP TSG RAN WG4 AdHoc meeting #01				Tdoc R4-10xxxx
Sophia Antipolis, France, 18/01 - 22/01 2010

Type: Draft Version for Comments v.0.0.x

Source: Issam Toufik, MCC

LEGEND:

NOT HANDLED

‘RETURN TO’ DURING THE MEETING

E-MAIL DISCUSSION

Approved LS OUT

Reminder

# Table of Contents

Table of Contents	2

Opening of the meeting	3

1	Sessions for LTE Advanced studies	3

1.1	Approval of the agenda	3

1.2	Studies for Overall aspect of IMT-Advanced study [Time plan, TR review]	3

1.3	Studies for Deployment Scenarios for IMT-Advanced	4

1.3.1	Carrier aggregation aspect	4

1.3.2	Other deployment aspect	8

1.4	Studies for LTE Advanced requirements	8

1.4.1	Common requirements for UE and BS	8

1.4.2	Studies for UE RF requirements	9

1.4.2.1	General	9

1.4.2.2	Transmitter characteristics	10

1.4.2.3	Receiver characteristics	10

1.4.3	Studies for BS RF requirements	10

1.4.3.1	General	11

1.4.3.2	Transmitter characteristics	11

1.4.3.3	Receiver characteristics	12

1.4.4	Studies for Radio Resource Management aspect	12

1.5	Close of Meeting (No later than Tuesday, 5 p.m.)	13

2	Sessions for Work Items [Rel-9 and beyond]	14

2.1	Approval of the agenda	14

2.2	Home eNodeB RF Requirements	14

2.2.1	Common requirements for TDD and FDD Home eNodeB [HeNB-RF_TDD, HeNB-RF_FDD]	14

2.2.2	FDD Home eNodeB RF Requirements [HeNB-RF_FDD]	16

2.2.3	TDD Home eNodeB RF Requirements [HeNB-RF_TDD]	17

2.3	HeNB/HNB inbound mobilities [EHNB-RAN2,]	18

2.4	RF requirements for LTE Pico NodeB (Conformance test) [Pico eNB-RF]	19

2.5	RF requirements for Multicarrier and Multi-RAT BS (Conformance test) [RInImp9-RFmulti]	21

2.5.1	General (Common sections of conformance test aspect)	21

2.5.2	Transmitter characteristics	22

2.5.3	Receiver characteristics	24

2.5.4	Others	24

2.6	Dual-Cell HSUPA [RANimp-DC_HSUPA] <R1>	25

2.7	Enhanced Dual-Layer transmission for LTE [LTEimp-eDL] <R1>	27

2.8	MBMS support in LTE [MBMS_LTE] <R2>	27

2.9	Positioning Support for LTE [LCS_LTE] <R2>	28

2.10	Close of the second session Meeting (No later than Friday 5 p.m.)	32

Phrases of the Week:	33

Annex A	: List of Documents	34

Annex B:	List of Endorsed Change Requests	35

Annex C:	List of documents discussed via reflector	36

Annex D:	List of non treated documents	37

Annex E:	List of agreed outgoing Liaison Statements	38

Annex F:	List of ingoing Liaison Statements	39

Annex G:	Registered Attendees	40

# Opening of the meeting

The meeting started on Monday January the 18th at 9 o’clock.

Intellectual Property Rights Policy

The attention of the delegates to the meeting of this Technical Specification Group is drawn to the fact that 3GPP Individual Members have the obligation under the IPR Policies of their respective Organizational Partners to inform their respective Organizational Partners of Essential IPRs they become aware of. The delegates are asked to take note that they are thereby invited: - to investigate whether their organization or any other organization owns IPRs which are, or are likely to become Essential in respect of the work of 3GPP. - to notify their respective Organizational Partners of all potential IPRs, e.g., for ETSI, by means of the IPR Statement and the Licensing declaration forms (http://webapp.etsi.org/Ipr/).

# 1	Sessions for LTE Advanced studies

## 1.1	Approval of the agenda

| R4-100001 | Approval | Proposed agenda | Chair |
| --- | --- | --- | --- |

Status: day 1 and day 2 agenda is Approved

## Studies for Overall aspect of IMT-Advanced study [Time plan, TR review]

| R4-100022 | Approval | Work plan for the "Carrier Aggregation for LTE" WI in RAN4 | Nokia Siemens Networks, Nokia |
| --- | --- | --- | --- |

Comments:

Ericsson commented that it should be avoided to write TP in a TR coming from SI.

Motorola commented that it is important to know where to capture this information. They agree with the creation of the annex where to capture the draft of the specification and where modifications can captured.

They also commented that it is important to align with RAN1 and RAN2 so that specification coming from these WGs can still relevant and are for practical scenarios.

Huawei :	-Time plan refer to Ad-hoc/bis meetings in 2011 but there is no final decision if to keep these meetings in the plan for 2011.

- comment on section 3.2 : time schedule has been extended compared to what has been approved previously.

- comment on Section 3.5, special consideration are to be taken regarding intra non-contiguous CA.

- comment on section 3.7 on RRM and mobility: they ask for clarification on the difference between initial study and further study.

NSN: - agrees with Huawei that the AdHoc/bis meeting are not sure to be kept and in which case the time plan should be rediscussed.

- Regarding comment on section 3.2: This for discussion on how we move on with these studies.

- Regarding comment on Section 3.5: Wait to have input from operators to see if non-contiguous should specified at this stage.

- Regarding comment on Section 3.7: Initial means defining the concepts how things should work and what are the key parameters and further study means go more in the detail of parameters

Vodafone is fine with time plan from NSN. And with the creation of the new TR.

Offline discussion on where to capture these aspects: current assumption is for BS, existing LTE TR (36.804). For UE a totally new TR.

Chairman: proposal is to agree on this Time plan and as we go through the documents in this meeting, if needed, we can update the time plan.

Status: in principal agreed

| R4-100126 | Approval | Organization of Relay RAN4 Specs | Qualcomm Incorporated |
| --- | --- | --- | --- |

Comments:

E///, Huawei and Motorola agree with Qualcomm to have separate specification and refer to the existing spec.

E/// wants to make sure that the new requirements which are specific to relay should be captured in the new spec.

E/// commented that there might be need for a new separate TR.

Huawei commented that the UE requirements may not be applicable to the relay UE component as there might be differences.

Motorola wants to know How to link between the specs?

Qualcomm agrees with E/// in that every thing which is new should be captured in the new spec.

They agree with Huawei that the UE component of a relay can have different characteristic than a “Normal” UE and thus this should be considered when defining the requirements.

Answer to Comment from Motorola: every existing requirement should apply and if there is any new requirement then this should be captured in the new spec.

Comment from LGE regarding documents R4-100126/R4-100127(received by email the day after the document was presented):

In my understanding, even though RelayNode seems to be as repeater based on it’s interaction between ENB and UE, but, indeed the type1 relay node regards as eNB because the type 1 relay has a independent cell ID and generate the signal for UE. And other relay type does not determined to discuss in RAN1 or other WGs. So in Rel-10, we can consider the type 1 relay.

We agreed with Qualcomm's proposal that make the new specification for RN using the existing spec. Also we agreed that RN to UE transmission could be followed the BS specification(36.104). But in case of the eNB-to RN transmission is new wireless transmission, it is similar to eNB to eNB wireless transmission.

And also we consider that RN-RN transmission, in this case, it should be defined that which Equipment is as UE or eNB.

Therefore, when designing Relay FRO and performance criteria, this point should be taken into account for future evolution. For example, wireless interface b.t.w. eNBs , general RF and performance spec. should be considered.

And next RAN4 meeting, we will prepare a contribution for relay transmission of these aspects.

Way forward take note of this document and in the TP in R4-100127 and to have TS and TR created.

Status: Noted

| R4-100127 | Approval | Text Proposal on Relay Requirements | Qualcomm Incorporated |
| --- | --- | --- | --- |

Comments:

E/// commented that this TP is related to WI which covers only type 1 relay and thus not sure this is applicable to all type relays. They think this can be misleading.

Huawei commented that there is a need for more study on the back-haul link to use the same requirements as for UE.

Status: noted

## 1.3	Studies for Deployment Scenarios for IMT-Advanced

### Carrier aggregation aspect

| R4-100215 | LS in | Response LS on carrier aggregation (R2-097497 Source: TSG RAN WG2, To: TSG RAN WG1,TSG RAN WG4, Cc: ) | TSG RAN WG2 |
| --- | --- | --- | --- |

Status: Noted

| R4-100012 | Approval | Bandwidth Aggregation Scenarios | US Cellular, Alcatel-Lucent, Huawei |
| --- | --- | --- | --- |

Comments:

T-mobile commented in the sentence “It should be noted that the actual implementation in a single device may not cover entire bands.”

that this should be discussed further as the network need to know what band the device supports and that a UE should support the entire band not a part of the band. If UE supports part of bands than new signalling is needed.

U.S. Cellular commented that this sentence is not restrictive, it only say that the entire band may not be supported.

E/// and ST-E/// agree with T-mobile that if a UE implements a band than it should support the whole band.

ST-E/// pointed out that there may be some difficulties of some combinations of carrier aggregation and this should be considered in the study and should be captured some where. They also commented that they have no problem maintaining the sentence.

Motorola also agrees that a UE should support the entire band but asked if this should still be the case for CA?

U.S. Cellular have no problem with the removing this sentence if it seems to be misleading

Discussion on how to handle these scenarios, where to capture them, which one should be considered for release-10.

Motorola deplores the fact that all inputs from all operators are not available in this meeting to come to a conclusion.

NTT Docomo would like to have list of higher priority scenarios.

ST-E/// commented that there should be a differentiation between potential scenarios and the ones to specify in Rel-10.

Alcatel Lucent suggested (step 1) make an agreement on a set of scenarios and then (Step 2) operators come with a list of higher priority scenarios.

US Cellular: capturing this information somewhere in a release independent manner can be useful.

Vodafone: intra band contiguous scenarios have the highest priority. Ideal scenario: have requirements that apply to all scenarios which is unlikely to be the case. And asked if this should be capture in a new TR or in 36.815 TR ? preferable way is to have a separate TR.

Huawei suggest to have this in release independent captured some where so that it can be possible to refer to and then work in the RF requirements for release 10.

AT&T: it can premature to come to come in conclusion.

Chairman: let this decision on where to capture this to offline discussion.

Status: Noted

| R4-100016 | Discussion | LTE-Advanced carrier aggregation aspects for Rel-10 | TeliaSonera |
| --- | --- | --- | --- |

Comments:

Status: Noted

| R4-100086 | Discussion | Some considerations on Rel-10 Carrier Aggregation Deployment Scenarios | Verizon |
| --- | --- | --- | --- |

Comments:

Status: Noted

| R4-100184 | Discussion | LTE-A deployment scenario for CA, Enhanced DL and UL antenna transmission | Motorola |
| --- | --- | --- | --- |

Comments:

China Mobile, for TDD, would like to see 50 instead of 40 MHz

ST-E asked if bands combinations that may represent some difficulties should also be considered?

Motorola agree with ST-E. every combination can be considered the worst case from one aspect. But which one will be considered as the worst case for all aspects ?

Motorola wants to choose a set of practical scenarios that will allow RAN-1 and RAN2 physical layer parameters and thus they propose to Focus on 2 (or 3) bands To minimise the number of potential deployment scenarios.

TeliaSonera do not see why should limit to 10+10MHz and commented that if 20+20 is considered then we have the 10+10Mhz inside.

Motorola commented that it is not very likely that an operator will have 20-20Mhz, thus see no point on having the 20-20MHz.

Vodafone: 20-20 is unlikely to be used, but when talking about 5years timeframe, they would like to see at least some study of 20-20MHz.

Huawei and Qualcomm would like to know if the inter-band non contiguous CA are be considered or should this be considered of lower priority and pushed into a later stage.

ST- E/// comment is that it is beneficial to agree on a criteria to choose the bands combination and asked how is important to satisfy ITU requirements regarding the rel-10 time frame. It can be useful to consider a subset of scenarios which are interesting from a deployment point of view also.

NTT Docomo commented that at this point on time, there is no proposal from operators regarding inter-band non contiguous.

US cellular point of view is that to aspect are to be

- should a Generic set of RF requirements, to be applied to combination scenarios, be defined ?

- or consider a subset of scenarios from which RAN1 and RAN2 can define signalling and other ?

Both are important and both are to be addressed.

Status: Noted

| R4-100181 | Approval | Prioritization of carrier aggregation scenarios | Qualcomm Incorporated |
| --- | --- | --- | --- |

Comments:

China Mobile asked for clarification if this limitation is valid only for FDD.

Qualcomm: there might be also some situation where it can be limiting in TDD

Status: Noted

| R4-100089 | Discussion | Inter-band carrier aggregation scenarios | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

Comments:

Motorola about the combination of two band (High band with low band): band having different wavelengths thus different path-loss. Is such a combination make sense ?

NTT-Docomo, Vodafone, TeliaSonera, US cellular and T-mobile: High band-low band combination can be used. Low band is useful for coverage and High band for capacity.

Vodafone is fine with the guidelines in this document but thinks should not exclude at this stage the FDD+TDD combination.

Status: Noted

| R4-100112 | Discussion | Implementation issues for combining multiple carriers | Ericsson, ST- Ericsson |
| --- | --- | --- | --- |

Comments:

The typical value of N has been discussed and a general comment from NSN is that from a specification point of there is no need to agree on anything here and that the specification should be implementation independent.

Status: noted

| R4-100137 | Discussion | Carrier Spacing and Placement for Contiguous Carrier Aggregation | Huawei |
| --- | --- | --- | --- |

Status: Withdrawn

| R4-100138 | Discussion | Spectrum Shaping for Multiple carrier OFDM | Huawei |
| --- | --- | --- | --- |

Comments:

Status: Noted

| R4-100053 | Discussion | Analysis of UL Carrier Aggregation | CATT |
| --- | --- | --- | --- |

Comments:

ST-E/// commented that spectral mask is violated in case of only 300KHz spacing however as far as a raster multiple of 15 KHz is used are subcarriers are still orthogonal.

[that is what justifies the use of the 300 KHz = smallest multiple of 100KHz (raster) and 15KHz (subcarrier spacing)].

CATT agrees that the interference impact may be limited however regarding their simulation they think there is a need for more study.

Qualcomm pointed out that SEM requirements has been agreed previously (document R4-093151).

E/// commented in section 2.3.2 that RAN1 will define new format thus it premature and should wait till RAN1 progressed on this.

Status: Noted

| R4-100068 | Discussion | Considerations of UE architectures for Carrier aggregation | Nokia |
| --- | --- | --- | --- |

Comments:

Chairman proposed to Use this as basis to set the requirements and invite delegates to decide how to capture this (new TR ?)

Status: noted

| R4-100069 | Discussion | Considerations of UE categories for Carrier aggregation | Nokia |
| --- | --- | --- | --- |

Comments:

The consideration of enhanced MIMO with CA has been discussed.

Comment from E/// is that RAN1 will only finish work enhanced MIMO by June, and thus RAN4 defining requirements for CA with enhanced MIMO by December will be very challenging.

Motorola:

Vodafone commented that technically speaking both (CA and MIMO) should be possible to achieve within the same category, and that from a RF requirements point of view we can proceed in parallel.

NTT Docomo would like to reduce the number of categories.

Status: Noted

| R4-100072 | Approval | TP for LTE-A RAN4 feasibility studies TR 36.815: Subclause 5.4.4 Implementation feasibility of carrier aggregation scenarios | Nokia Siemens Networks |
| --- | --- | --- | --- |

(Document submitted in Agenda 1.4.3.1)

Comments:

Huawei Assumption is to define power per antenna port not per CC

NSN not proposing in this document to define power per CC and NSN have the same understanding as Huawei on this.

Status: noted

| R4-100045 | Discussion | UE to UE coexistence study for Carrier aggregation | Samsung |
| --- | --- | --- | --- |

Status: Noted

| R4-100188 | Discussion | Simulation assumptions for LTE-A co-existence study | NTT DOCOMO |
| --- | --- | --- | --- |

(Document submitted in Agenda 1.4.1)

Comments:

ALU wants to make sure the ACIR is calculated based on the 20MHz and Would like to clarify the definition of ACIR if based on power or PSD.

E/// agrees with ALU on the need for a clarification of the ACIR definition.

Motorola commented that RAN1 didn’t yet come into a conclusion on PC and asked if one PC or sepearte PC should be assumed.

NTT Docomo answered that yes we should wait for RAN1 but we can use the assumption of one power control (as it is the simplest assumption) in order to progress.

E/// asked for clarification on the UE distribution and commented that it is possible for a UE to be less than 3m from eNB and the current assumption in this document does not support this case.

NTT Docomo commented that the purpose is to first agree on a concept and then look on the details. Needs to check for distance <3m

Status: Noted

| R4-100139 | Approval | Further consideration on LTE-A coexistence study | Huawei |
| --- | --- | --- | --- |

(Document submitted in Agenda is 1.3.2)

Comments:

Qualcomm asked for clarification on the macro proposal used?

Huawei: The same as Rel-8

Motorola pointed out a Typo in section 2.1.1 (ACIR, Uplink), in Figure 3. The number of RBs shown for the 10MHz LTE aggressor should be 16+16+16.

E/// commented that emission masks are already defined in other standards (e.g. MSR specifications), so there may be no need to redefine them.

Qualcomm: Hotspot PC needs careful consideration. UL PC need further study on the number of UEs per cell.

Huawei offline discussion to progress took place ( outcome document to be submitted to RAN4

Status: Noted

| R4-100134 | Discussion | Coexistence between LTE-Advanced and LTE in DL: ITU-R Base Coverage Urban and Microcellular deployment scenarios | Qualcomm Incorporated |
| --- | --- | --- | --- |

Comments:

Huawei pointed out that there is differences between assumptions in this document and the ones assumed by RAN1 and asked if

there should alignment between RAN1 and Ran4 assumptions?

Qualcomm answered RAN1 follow the ITU channel models regarding the submission to ITU-R and commented that considering that there are different aspects/goals of the evaluations, we can consider modified channel models.

Status: Noted

| R4-100135 | Discussion | Coexistence between LTE-Advanced and LTE in DL: ITU-R Base Coverage Urban and Microcellular deployment scenarios | Qualcomm Incorporated |
| --- | --- | --- | --- |

Status: Noted

| R4-100039 | Discussion | Downlink simulation results for coexistence between LTE-A and LTE | Samsung |
| --- | --- | --- | --- |

Status: Withdrawn

| R4-100046 | Discussion | ACIR modelling for Uplink LTE-A co-existence simulation | Samsung |
| --- | --- | --- | --- |

Status: Revised in R4-100201

| R4-100201 | Discussion | ACIR modelling for Uplink LTE-A co-existence simulation | Samsung |
| --- | --- | --- | --- |

Status: Withdrawn

| R4-100183 | Discussion | LTE-A coexistence simulation result for scenario #1 | LG Electronics |
| --- | --- | --- | --- |

Status: Noted

| R4-100113 | Discussion | Co-existence issues for contiguous carrier aggregation | Ericsson, ST- Ericsson |
| --- | --- | --- | --- |

(Document submitted in Agenda 1.4.3.2)

Comments:

Motorola and Huawei commented that this should not be considered as a conclusion (before even begin the study) and should not exclude that study may result some differences with the masks already specified in existing specs.

E///: this more an observation that it exists and would like people to have this in mind.

NSN, regarding the BS emission requirements, need more time to discuss with E/// the exact meaning before having any commitment on this.

Status: Noted

R4-100220	LTE-A deployment scenarios (NTT DOCOMO, Deutche Telekom, TeliaSonera, US Cellu)

Comments:

Vodafone: Didn’t have time to look deeply in the document, Will come back in SF to finalise, but generally they are ok with the document.

ST-E/// In the inter- band non-contiguous carrier aggregation there is a TBD.

NTT Docomo: to be addressed later. This a starting point.

US cellular TP should go to a TR that captures these scenarios and should also capture the related requirements. Wants to capture the agree upon scenarios in this document as the market requirements and then have the derived approach and generic characteristics captured in the same TR as these scenarios. They also commented that there is no need to wait one more cycle for approval. Operator’s Consensus on the market requirements for rel-10 time frame is captured in this document and the TP is already in the annex, what needed to be address is only where to put this scenarios and the corresponding requirements.

Motorola welcome the feedback from operators and think this is important to study the scenarios in order to come up with a generic approach.

They suggested to capture these scenarios in a TR and discuss what is in TBD in the document.

Vodafone would like have feedback from vendors on which is feasible on which is not in this document.

Way forward: Document is agreed on (formally technically endorsed) and will be sent in the reflector to have feedback from vendors and use this document as assumption for future studies.

Status: in principle agreed

Way forward on the simulation assumptions:

NTT Docomo: Use Huawei (R4-100139) as a basis and then based on this then derive the critical parameters.

Qualcomm: R4-100139 can be used as a framework but there are some important issue that they would like to agree on and make changes in this document. Or change the open issue to TBD and thus no need to have an agreement in this meeting.

Vodafone: BS antenna pattern, 3D antenna pattern is considered by RAN1.

Huawei: again objectives are not the same, thus we can consider simplified pattern/assumptions to progress fast.

Way forward: ( - use R4-100139 as framework for simulation assumption.

- 36.942 will be used to capture TP from further results and simulation outcomes.

R4-100247	Draft reply LS on mobility measurements for carrier aggregation (Nokia)

Status: in principle agreed

### 1.3.2	Other deployment aspect

## 1.4	Studies for LTE Advanced requirements

### Common requirements for UE and BS

| R4-100140 | Discussion | LTE-A carrier aggregation inter-modulation analysis in certain scenarios | Huawei |
| --- | --- | --- | --- |

Status: Noted

| R4-100207 | Discussion | Release 10 UE PUCCH/PUSCH configuration | Motorola |
| --- | --- | --- | --- |

Comments:

Motorola invites other companies to investigate this issue to confirm their findings and then decide in a way to progress and coordinate with RAN1.

Proposed way forward: feedback from other companies in this issues next meeting is encouraged and then send feedback to RAN1.

Nokia agrees with the severe IMD issue if simultaneous PUCCH and PUSCH. Nokia confirm to do some more work in this for next meeting and encourage to coordinate with RAN1 who may not be aware of these issues.

ST-E supports and think it is important to coordinate with RAN1 at early stage.

Qualcomm agrees with the issues in this paper and commented that they had a look in this in generic way for the worst case in some of previous contributions. But also think that RAN4 should also consider the benefits and thinks there might be some scenarios where this issue in not faced. Qualcomm also commented that there is a general problem in the WI for clustered SC-FDMA. solving the problem on distributed PUSCH will then solve in the same way this one. So sees no point on emphasising this issue.

Motorola answered to the first comment that changes in the emission mask will be a big issue on the LTE-A deployment and RAN4 should come up with a generic solution that will work for all bands. For the second comment, RAN1 will finish the work in this WI in September and thus it will be too late to address the problem. The point is address if there is an issue, to make RAN1 aware of the problem and then it is up to RAN1.

ST- E/// supports Motorola’s view on this and think it is important to send feedback to RAN1 in at an early stage.

Disagreement between Huawei and Motorola on the importance of the severity of missing the emission mask

Vodafone would like to know the final IMD product.

Chairman proposed way forward is to work based on this contribution to address the IMD and issues addressed in this paper.

Status: Noted

| R4-100043 | Discussion | Effective antenna gain proposal in TR35.942 | Samsung |
| --- | --- | --- | --- |

Comments:

NTT Docomo disagrees on the change of this value as this will require more study and feels that -9dBi is not appropriate and it is better to keep the current.

TeliaSonera has the same view as NTT Docomo. No need to change the value

Samsung the attention of have this is only for handset devices.

Agilent regarding the sentence “Since handset UE has effective body loss due to the position during call, it is realistic to use effective antenna gain which is measured from the OTA performance test” commented that at this stage there in nothing measured in OTA performance tests.

ST-E///: values can range from -10dBi to much higher values. difficult to still use only one value in the specification.

Status: Noted

### 1.4.2	Studies for UE RF requirements

#### 1.4.2.1	General

| R4-100189 | Discussion | Analysis on LTE-A UE RF requirements | NTT DOCOMO |
| --- | --- | --- | --- |

Status: Noted

| R4-100185 | Discussion | LTE-A Tx Architecture | Motorola |
| --- | --- | --- | --- |

Comments:

TeliaSonera disagrees with the restriction to 2 scenarios. Different combinations ( different IMDs thus there might be a need for more scenarios.

Motorola suggests to focus on the impact on RAN1 and RAN2 work. Thus there is a need for some generic scenarios and to limit their number in order to progress or it will be difficult to move forward and finish the spec in a timely manner.

TeliaSonera commented that they have no problem with being generic but think this scenario is not generic. Choosing a particular band is biased and thus is not so generic.

Motorola commented that there is no bias on the choice of band. Hypothetic bands A and B can be chosen but in this case some issues might be missed. That is the reason for choosing one particular band and there is no particular bias from Motorola on the choice of the band and have no problem with changing the band to another one.

Vodafone commented about the max UL BW being 40 MHz and asked if 50MHz can be ok in order to support other scenarios.

They commented that without a deeper analysis it is difficult to know which band is used in the UL, but for fragmented “bandwidth”, 40MHz may not be enough and thus some higher numbers could be used as well. Also Would like to see if there is Any difference between TDD and FDD.

Motorola: this is valid for both TDD and FDD.

Chairman: this is good starting point to start work on the TX architecture and suggest to consider this proposed architecture for future analysis.

Status: Noted

| R4-100090 | Discussion | Contiguous carrier aggregation: impact on UE radio requirements | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

Comments:

ALU commented on the figure-3 and the fact that the black curve surpasses the spectrum mask and asked if this indicate we may need to revise the Rel8 UE emission mask for CA?

ST-E/// Yes

Qualcomm questioned the considered scenario and commented that non-contiguous case could be worst.

ST-E/// agrees that there might be scenarios that may be worst. But commented that the number of scenarios is very big and should limit the number of considered ones.

Status: noted

| R4-100198 | Discussion | LTE-A TDD UE Performance | Vodafone |
| --- | --- | --- | --- |

Status: Withdrawn

#### 1.4.2.2	Transmitter characteristics

#### Receiver characteristics

| R4-100141 | Discussion | Initial work on UE sensitivity in LTE-A | Huawei |
| --- | --- | --- | --- |

Comments:

ST-E/// commented that type of reference symbol used to address all the possible cases is something that has to be addressed.

Huawei agrees with comment.

Status: Noted

| R4-100142 | Discussion | MIMO impact on MSD in LTE-A | Huawei |
| --- | --- | --- | --- |

Status: Noted

## 1.4.3	Studies for BS RF requirements

| R4-100023 | Discussion | Expected changes to TS 36.104 due to CA WI | Nokia Siemens Networks |
| --- | --- | --- | --- |

Comments:

E///” commented that should keep on mind that emission mask is already defined MSR specification and should reuse previous work and this also valid for requirements. They also commented that the way to view CA (i.e. as a one larger carrier or two carriers coming from 2 # BSs) has an impact in the way you write the spec and E///: would like to have this in mind. And not have the spec not restrictive to one or the other.

Huawei: why using the single carrier for testing while we have BS already capable of RX

Agilent: it is becoming unrealistic to proceed with conductive testing for UE. should we rethink the way testing are conducted.

Status: Noted

| R4-100105 | Discussion | Contiguous carrier aggregation: Overview of impact on BS radio requirements | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

Comments:

NSN commented that the content is aligned with NSN’s view but for the RX part they commented that refsens should reuse the existing. Regarding Blocking and IMD they agree to use HSUPA requirements but offsets should be changed.

should consider development from work of RAN1 and should discuss if there is any benefit from the use extension and segments test with respect to the demodulation requirements.

Huawei Commented that extension carriers and segment are already discussed in RAN1. They questioned the need for a new reference channel. Asked if the intention is a Format change or methodology change in the “FRC “. They also commented that the definition of the new bandwidth does not mean we need to modify the test specification. 5+5=10MHz,. use the 10 MHz tests. the new channel bandwidth depends on the way you implement the CA .

E/// agrees on the comment NSN.

Agrees on the fact that extension carriers and segments are discussed in RAN1 and the intention is not to open a new work task in RAN4. Commented that a format change can trigger a FRC but also agree that should look into the methodology and may need to change the methodology for Rel-10

Motorola commented that this can be a good material for TR.

Status: Noted

| R4-100106 | Discussion | Contiguous carrier aggregation: Overview of impact on BS demodulation requirements | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

Comments:

NSN: comments on R4-100105 still valid for this one also.

Comment on the table in the document, Some aspects need to be detailed further and that some test cases are not needed. should think what is beneficial to be tested or not.

E///: acknowledge it is a correct comment.

Status: Noted

| R4-100107 | Discussion | Inter-band carrier aggregation across different bands; feasibility of using RBs per CC as per rel-8 | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

Status: Noted

#### General

| R4-100122 | Discussion | Practical design considerations for LTE-Advanced power amplifiers | Motorola, Inc. |
| --- | --- | --- | --- |

Comments:

China Mobile commented that AP’s prices dropped and technology advanced thus thinks that 50MHz is feasible.

Status: noted

| R4-100071 | Approval | TP for LTE-A RAN4 feasibility studies TR 36.815: Subclause 5.4.1 General | Nokia Siemens Networks |
| --- | --- | --- | --- |

Comments:

Huawei: the content is mainly for WA BS. how will this be considered for pico BS regarding RF requirements?

Qualcomm: same for HomeNB.

Huawei and Qualcomm feel a Prioritization of macro BS and wants to clarify this

NSN: It is left open and no class is excluded. Any BS class could be added to the subclause and this is also valid for all requirements.

Status: in principal agreed

#### Transmitter characteristics

| R4-100145 | Discussion | Impact of cross carrier frequency/time error | Huawei |
| --- | --- | --- | --- |

Status: Noted

| R4-100146 | Discussion | Cross carrier interferences introduced by phase noise | Huawei |
| --- | --- | --- | --- |

Status: Noted

| R4-100073 | Approval | TP for LTE-A RAN4 feasibility studies TR 36.815: Subclause 5.4.2.1 General | Nokia Siemens Networks |
| --- | --- | --- | --- |

Status: in principal agreed

| R4-100074 | Approval | TP for LTE-A RAN4 feasibility studies TR 36.815: Subclause 5.4.2.2 Base Station output power | Nokia Siemens Networks |
| --- | --- | --- | --- |

Comments:

E///: which TR we should use? Preference is to use BS existing TR. We need an agreement before the next RAN4 meeting.

NSN: this for the study item TR and would expect same (modified) TP for the WI TR. This need to be revisited for the WI TR.

E///: for MSR, intermediate power “the configured power” is used, this to be considered and kept in mind.

Status: in principal agreed

| R4-100075 | Approval | TP for LTE-A RAN4 feasibility studies TR 36.815: Subclause 5.4.2.3 Transmitted signal quality | Nokia Siemens Networks |
| --- | --- | --- | --- |

Status: in principal agreed

| R4-100076 | Approval | TP for LTE-A RAN4 feasibility studies TR 36.815: Subclause 5.4.2.4 Unwanted emissions | Nokia Siemens Networks |
| --- | --- | --- | --- |

Status: in principal agreed

| R4-100144 | Approval | TP Unwanted emission requirement for LTE-A BS | Huawei |
| --- | --- | --- | --- |

Comments:

NTT Docomo commented regarding the gaps in carrier allocation for intra band non contiguous that it is premature to state that there is no need to define ACLR.

E/// commented that it is premature to agree on this TP. Several issues are still open. One of them is regarding Co-existence studies where it early to conclude on spurious and out of band emissions and it is better to wait for the approval of this proposal.

NSN is in line with NTT Docomo’s view.

Motorola asked about scenario 5 modelling if it is aligned with intermodulation as addressed in earlier paper (R4-100140)?

Huawei: think it is consistent.

Status: Noted

#### 1.4.3.3	Receiver characteristics

| R4-100014 | Approval | TP for LTE-A RAN4 feasibility studies TR 36.815: Subclause 5.4.3 Receiver characteristics | Nokia Siemens Networks |
| --- | --- | --- | --- |

Comments:

Motorola: this fit well with other documents from NSN 100071 to 100076. Motorola supports approval of the proposal

ALU: this document states that intra frequency non contiguous case can be considered and in R4-100023 it is proposed not to consider this case.

NSN: This is for SI TR and R4-100023 is for 36.104

Status: in principal agreed

| R4-100143 | Discussion | Consideration on LTE-A BS dynamic range | Huawei |
| --- | --- | --- | --- |

Comments:

NSN: premature to decide on the detail for dynamic range.

Status: Noted

| R4-100147 | Discussion | Reference sensitivity level for LTE-Advanced BS | Huawei |
| --- | --- | --- | --- |

Status: Noted

### 1.4.4	Studies for Radio Resource Management aspect

| R4-100085 | Discussion | Mobility measurements and carrier aggregation | Nokia, Nokia Siemens Networks |
| --- | --- | --- | --- |

Comments:

Disagreement from Qualcomm and E/// with Nokia and NSN of the consideration of DRX with CA. The document states that the use of DRX with gaps will degrade the performances. It suggested to decide whether it is possible for the UE to perform the measurements and when it comes to performance then evaluate these. Also in the single carrier case the performance are worst in the case of DRX.

E///, Qualcomm and Huawei question the power saving due to gaps in the documents.

Qualcomm: notices no difference in power consumption between measurements with gap vs without-gaps.

NSN: depends on which data traffic (load) is considered.

Status: Noted

| R4-100091 | Discussion | Mobility Measurements in Carrier Aggregation Scenarios | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

Status: Noted

| R4-100124 | LS out | Draft Reply LS on MC Measurements | Qualcomm Incorporated |
| --- | --- | --- | --- |

Status: Noted

| R4-100125 | Discussion | Discussion on MC Measurements | Qualcomm Incorporated |
| --- | --- | --- | --- |

Comments:

Nokia commented on the statement from Qualcomm regarding the battery life, that this is true only in the case of high data transmission, but in this case UE may be using more than one carrier than only the active carrier anyway. So do not agree in this case with the one to one statement between the power due to measurements without gaps and with gaps.

Huawei: example in document is not always true. Example UE with wider receiver may receive both carriers in the same time.

Status: Noted

| R4-100148 | Discussion |  | Considerations on mobility measurements for Carrier aggregation | Huawei |
| --- | --- | --- | --- | --- |

Comments:

Nokia: Should take into account the considerable differences between HSPA and LTE.

Huawei: if one antenna then similar if multiple then yes it is different.

Qualcomm: do not agree on the statement: “… data loss is unavoidable”.

Status: Noted

| R4-100149 | LS out |  | Reply LS on mobility measurements for carrier aggregation | Huawei |
| --- | --- | --- | --- | --- |

Status: Noted

| R4-100192 | Discussion |  | Carrier aggregation deployment scenarios for RRM | NTT DOCOMO |
| --- | --- | --- | --- | --- |

Comments:

Huawei: asked if there are any priority over these scenarios and which one is the preferable.

NTT Docomo: this needs further study and other scenarios could be expected.

E/// commented that for inter-band carrier aggregation, when aggregated carriers are from different bands, then mobility is based on the lower band since it has better coverage. When the carriers are from the same band, the coverage is then the same and thus should look at the two frequencies when it comes to mobility.

Status: noted

| R4-100021 | Approval | TP for TR 36.815: RRM aspect | Nokia Siemens Networks, Nokia |
| --- | --- | --- | --- |

Qualcomm: Statement about DRX could be removed then it will be ok.

Status: Noted

## 1.5	Close of Meeting	(No later than Tuesday, 5 p.m.)

# 2	Sessions for Work Items [Rel-9 and beyond]

| R4-100087 | Information | Reference sensitivity and MSD | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

No formal presentation.

Status: Not handled

| R4-100123 | Information | 2GHz S-band Overview | TerreStar & DBSD |
| --- | --- | --- | --- |

No formal presentation.

Status: Not handled

| R4-100190 | Information | 3GPP: L-Band Overview | Skyterra |
| --- | --- | --- | --- |

Status: Revised in 196

| R4-100196 | Information | 3GPP: L-Band Overview | Skyterra |
| --- | --- | --- | --- |

Status: Revised in 210

| R4-100210 | Information | 3GPP: L-Band Overview | Skyterra |
| --- | --- | --- | --- |

No formal presentation.

Status: Not handled

## 2.1	Approval of the agenda

| R4-100001 | Approval | Proposed agenda | Chair |
| --- | --- | --- | --- |

Status: Agenda for days 3,4 and 5 is approved

## 2.2	Home eNodeB RF Requirements

### 2.2.1	Common requirements for TDD and FDD Home eNodeB [HeNB-RF_TDD, HeNB-RF_FDD]

| R4-100054 | CR | Rel-9 | Corrections of operating band unwanted emissions for Home BS | CATT | 36.104 |
| --- | --- | --- | --- | --- | --- |

Status: Technically endorsed

| R4-100191 | CR | Rel-9 | Operating band unwanted emissions requirement for Home eNodeB | CMCC, CATT | 36.141 |
| --- | --- | --- | --- | --- | --- |

Status: Technically endorsed

| R4-100175 | CR | Rel-9 | Dynamic range requirement for Home eNodeB | CMCC, CATT | 36.141 |
| --- | --- | --- | --- | --- | --- |

Status: Revised in 200

| R4-100200 | CR | Rel-9 | Dynamic range requirement for Home eNodeB | CMCC, CATT | 36.141 |
| --- | --- | --- | --- | --- | --- |

Status: Technically endorsed

| R4-100002 | Approval | Text Proposal on Home eNodeB Transmit Power Conformance Testing for Adjacent Channel Protection | Alcatel-Lucent |
| --- | --- | --- | --- |

Comments:

Vodafone commented that they are ok with the concept of adjacent channel protection but really like to see some analysis for the adjacent rejection for HeNB and expects some revision before agreeing on this.

Status: in principle agreed

| R4-100129 | Discussion | Discussion on victim UE aware interference management | Qualcomm Incorporated |
| --- | --- | --- | --- |

Comments:

PicoChip Design: related document with the same analysis but different conclusions is in R4100195

Need some offline discussion

Status: Noted

| R4-100187 | Discussion | Victim UE transmission detection at the HeNB | picoChip Designs |
| --- | --- | --- | --- |

Status: Revised in R4-100195

| R4-100195 | Discussion | Victim UE transmission detection at the HeNB | picoChip Designs, Kyocera |
| --- | --- | --- | --- |

Status: Noted

| R4-100197 | Approval | Text proposal for TR 36.9xx: Reducing interference from CSG cells by dynamically changing their CSG IDs | Motorola |
| --- | --- | --- | --- |

Status: in principle agreed

| R4-100040 | Discussion | Handling of missed HeNB performance requirements | Samsung |
| --- | --- | --- | --- |

Status: revised on 227

R4-100227	Handling of missed HeNB performance requirements (Samsung)

Comments:

NSN: agreement in Jeju (meeting #53) was to reuse the values from macro scenarios and there is a need for further discussion.

Status: Noted

| R4-100041 | CR | Rel9 | Corrections on HeNB performance requirements | Samsung | 36.104 |
| --- | --- | --- | --- | --- | --- |

Status: revised on 228

R4-100228	Corrections on HeNB performance requirements (CR 143r1 to 36.104 Rel9) (Samsung)

Comments:

ALU: is the intention is to apply this to WA BS?

Huawei: need more time to discuss the document.

NSN: reuse the values from macro scenarios so not to re-discuss as the information is already there.

Status: Noted

| R4-100042 | CR | Rel9 | Corrections on HeNB performance requirements | Samsung | 36.141 |
| --- | --- | --- | --- | --- | --- |

Status: revised on 229

R4-100229	Corrections on HeNB performance requirements (CR 146r1 to 36.141 Rel9) (Samsung)

Status: Noted

| R4-100003 | Discussion | Simulation results for ACK/NACK multiplexed to PUSCH over EVA5 | Alcatel-Lucent |
| --- | --- | --- | --- |

Status: Noted

| R4-100128 | Approval | TP Correction to Resource Partitioning | Qualcomm Incorporated |
| --- | --- | --- | --- |

Status: revised on 232

R4-100232	TP Correction to Resource Partitioning (Qualcomm Incorporated)

Status: in principle agreed

R4-100250	Simulation assumptions for additional performance requirements of E-UTRA LA and Home BS class (NTT DOCOMO, Nokia Siemens Networks, Alcatel-Lucent)

Comments:

Huawei: ok with contrib.

Want to make sure that this issues will not block the closer of the WI for pico-NB so suggests to put this under TEI-9 if it can not be finished within the time allocated to set the requirements.

China mobile: agree with Huawei comment and also suggests to have this in the WI TEI-9

Status: in principle agreed.

### FDD Home eNodeB RF Requirements [HeNB-RF_FDD]

| R4-100034 | Approval | Simulation results of interference mitigation schemes and text proposal for TR 36.921 | ETRI |
| --- | --- | --- | --- |

Comments:

Qualcomm: commented in  the statement “Interference Management based on mapping between PCIs and transmission patterns requires a centralized coordinator” that it Can be done without need for a centralized coordinator. If the document can be revise to remove this statement can be good but basically no problem with the remaining.

Status: in principle agreed

| R4-100051 | Discussion | Victim UE Aware Downlink Interference Management | picoChip Designs |
| --- | --- | --- | --- |

Status: Revised in 193

| R4-100193 | Discussion | Victim UE Aware Downlink Interference Management | picoChip Designs, Kyocera |
| --- | --- | --- | --- |

Status: Noted

| R4-100052 | Approval | Text Proposal for TR36.921: Victim UE Aware Interference Management | picoChip Designs |
| --- | --- | --- | --- |

Status: Revised in 194

| R4-100194 | Approval | Text Proposal for TR36.921: Victim UE Aware Interference Management | picoChip Designs, Kyocera |
| --- | --- | --- | --- |

Comments:

Qualcomm: still have problems with this as there is differences in the simulation results presented by the two companies. Suggests to Discuss this offline and come back to this document.

Status: Noted

| R4-100018 | Approval | Text Proposal for 36.9xx: HeNB Adaptive Frequency Selection | NEC |
| --- | --- | --- | --- |

Status: in principle agreed

| R4-100019 | Approval | HeNB Power Control Based on HUE Measurement | NEC |
| --- | --- | --- | --- |

Status: in principle agreed

| R4-100017 | Approval | Text Proposal for 36.9xx: HeNB Measurements | NEC, picoChip Designs, Kyocera |
| --- | --- | --- | --- |

Status: in principle agreed

| R4-100020 | Approval | Revision on Information Exchange Option 2 of TR36.921 | Kyocera, PicoChip Designs, Qualcomm Incorporated, Institute for Information Industry (III), Coiler Corporation, NEC |
| --- | --- | --- | --- |

Comments:

Motorola Don’t see a strong need of the added sentence but have no problem to agree on the TP

Status: in principle agreed

| R4-100048 | Approval | Text Proposal for TR 36.921: Interference control for LTE Rel-9 HeNB cells | Nokia Siemens Networks, Nokia |
| --- | --- | --- | --- |

Status: Revised in 204

| R4-100204 | Approval | Text Proposal for TR 36.921: Interference control for LTE Rel-9 HeNB cells | Nokia Siemens Networks, Nokia |
| --- | --- | --- | --- |

Comments:

PicoChip Design commented that concerning the UL part, a TP has been approved in the last meeting and thus there is need to merge and align the two.

E/// had the same comment and also had concerns on terminology RSRP used. RSRP is a UE measurement and not a (H)eNB measure.

E/// also commented about the UL Power control that it already exists on legacy and don’t see the need for re-introducing it.

Status: revised in 235

R4-100235	Text Proposal for TR 36.921: Interference control for LTE Rel-9 HeNB cells (Nokia Siemens Networks, Nokia)

Comments:

Vodafone: Need further clarification of definition of the CRS in the TR or in the Spec. CRS E_c and RSRP are basicaly the same

NEC: RSRP is a useable terminology it only states it is received power.

E///: now it looks fine.

Status: in principle agreed

### 2.2.3	TDD Home eNodeB RF Requirements [HeNB-RF_TDD]

| R4-100217 | LS in | LS on providing backhaul signalling in support of time and frequency synchronization using network listening | TSG RAN |
| --- | --- | --- | --- |

Status: Noted

| R4-100218 | LS in | e:Response LS on the support for time and frequency synchronisation for TDD HeNB | TSG SA WG5 |
| --- | --- | --- | --- |

Status: Noted

| R4-100049 | Approval | Text Proposal for TR 36.922: TDD HeNB Synchronization using Network Listening | Nokia Siemens Networks, Nokia, Qualcomm Europe |
| --- | --- | --- | --- |

Status: in principle agreed

| R4-100176 | Approval | LTE TDD Home eNodeB RF requirements TR36.922 v1.1.0 | CMCC |
| --- | --- | --- | --- |

Status: in principle agreed

| R4-100050 | Discussion | Further consideration on LTE TDD HeNB synchronization use case and extra signaling | Nokia Siemens Networks, Nokia |
| --- | --- | --- | --- |

Comments:

Qualcomm : macro cell scenario is considered here but that other scenarios can be used.

After Offline discussion: propose a joint TP for next meeting.

Status: Noted

| R4-100177 | Approval | Text proposal on LTE TDD HeNB synchronization requirement | CMCC, NSN |
| --- | --- | --- | --- |

Status: in principle agreed

| R4-100182 | Discussion | Conversion of UTC Time to Frame Start Timing | Qualcomm Incorporated |
| --- | --- | --- | --- |

Comments:

ALU: What consequence ? Changes on RAN2 specs (36.331 ???) ?

E///: not sure RAN4 is the right group to decide. RAN2 should decide.

Qualcomm: same paper submitted to ran2,. so ran2 decides, this for information for RAN4

Status: Noted

| R4-100178 | Approval | Text proposal on LTE TDD HeNB interference control | CMCC |
| --- | --- | --- | --- |

Status: in principle agreed

| R4-100205 | Approval | Text Proposal for TR 36.922: Interference control for LTE Rel-9 HeNB cells | Nokia Siemens Networks, Nokia, Panasonic |
| --- | --- | --- | --- |

Status: revised to R4-100234

R4-100234	Text Proposal for TR 36.922: Interference control for LTE Rel-9 HeNB cells (Nokia Siemens Networks, Nokia, Panasonic)

Comments:

Vodafone: concerns about the terminology. Need an other round of discussion to ensure the terminology is aligned. Basically CRS and RSRP are the same.

NEC: prefer the previous terminology using RSRP. We can then add a description of what RSRP is at the beginning.

Chairman: if it is only a terminology problem get an agreement before San Francesco. Agree on this one and then perform a clean up of the terminology.

Status: in principle agreed

## HeNB/HNB inbound mobilities [EHNB-RAN2,]

| R4-100214 | LS in | LS on CSG mobility performance (R2-097463 Source: TSG RAN WG2, To: TSG RAN WG4, Cc: ) | TSG RAN WG2 |
| --- | --- | --- | --- |

Status: Noted

| R4-100036 | Discussion | Consideration on the HeNB inbound mobility simulation assumptions | Samsung |
| --- | --- | --- | --- |

Comments:

NTT Docomo: agrees with this analysis. If we consider the worst case, then this analysis should be taken into account.

Qualcomm: also agrees with the analysis. Regarding the simulation, not sure we need 7 radio frames and thinks 4 can be enough but regarding tests agrees that it should be carried over 7 subframes.

Status: Noted

| R4-100206 | Discussion | Discussions on HeNB inbound mobility performance requirements | NTT DOCOMO |
| --- | --- | --- | --- |

Comments:

E///: Is there an additional RRC procedure delay to be added ?

NTT Docomo: Value for RRC is included in the requirement (15ms) may be need to recheck the value of requirement but RAN2 has already introduced it.

Motorola: Inter frequency case: Consider the difference in SNR level between the serving and other cells.

Motorola: in Intra-frequency case, how many repetitions of test we need to perform to reach the proposed requirement?

Qualcomm: agrees with the frame work and commented that what we care about is the functional behaviour not the performance so we can make this easier by considering AWGN. [Regarding comment from Motorola, you need a few repetitions (may be 100 repetitions ???) to achieve 90% performance.]

NTT Docomo: this is more function testing than performance, thus AWGN can be sufficient as Qualcomm suggested.

Status: Noted

| R4-100133 | Discussion | In-bound mobility minimum performance requirements | Qualcomm Incorporated |
| --- | --- | --- | --- |

Comments:

Vodafone: Reuse macro cell requirements.

Samsung: agree with coupling of PDSCH with MIB/Sib1.

Qualcomm: (regarding comment from Vodafone) do not have overall requirement for latency.

Vodafone: for inter frequency/intra frequency measurements the requirements are there. Need only to define the SI reading requirements.

Qualcomm: Proposal for the way forward is to use the proposal from NTT Docomo in R4-100206.

Status: Noted

| R4-100174 | Discussion | Simulation assumptions for HNB inbound mobility | Qualcomm Incorporated |
| --- | --- | --- | --- |

Status: Revised in 209

| R4-100209 | Discussion | Simulation assumptions for HNB inbound mobility | Qualcomm Incorporated |
| --- | --- | --- | --- |

Comments:

E///: we should be clear about how the delays are defines, does it for example include the PCI decoding?

Status:  Noted

| R4-100078 | Discussion | Performance requirements for UTRA inbound handover | Nokia, Nokia Siemens Networks |
| --- | --- | --- | --- |

Comments:

Qualcomm: agrees with most of content however the understanding is that the description of the normal procedure is 2 step for intra and 1 step for inter. Here appears that 2 step is applied also for intra.

Also commented that one attempt can be ok for AWGN, but need more then one attempt for multi-path. General requirements are derived for the worst case.

Nokia: need to check with RAN2 procedure.

Way forward: Offline discussion/clarification needed between Qualcomm and Nokia/NSN and try to agree on some thing during this meeting.

Status: Noted

| R4-100132 | Discussion | In-bound mobility simulation results | Qualcomm Incorporated |
| --- | --- | --- | --- |

Status: Noted

| R4-100035 | Discussion | HeNB inbound mobility simulation results | Samsung |
| --- | --- | --- | --- |

Comments:

NTT Docomo: what propagation condition is considered AWGN or EVA5?

Samsung: EVA5

Status: revised in 233

R4-100233	HeNB inbound mobility simulation results (Samsung)

Status: Noted

| R4-100037 | Discussion | Consideration on the response to RAN2 LS on CSG mobility requirements | Samsung |
| --- | --- | --- | --- |

Comments:

Status: Noted

R4-100244	Way forward on HeNB inbound mobility requirements (NTT DOCOMO, Samsung)

Comments:

AWGN as propagation for test requirements.

Status: in principle agreed

## 2.4	RF requirements for LTE Pico NodeB (Conformance test) [Pico eNB-RF]

R4-100225	Editorial correction in TS36.104 for Pico NodeB (CR 146 to 36.104 Rel-9) (Huawei)

Comments:

E///: changes are ok but the removal of the NOTE in section 6.6.4.4 is not appropriate ( Same wording as for UTRA in 25 series (25.104) should be used.

Huawei suggest to add a note for each different class

ALU: agrees with E/// on keeping the note instead of adding note on every single class.

Status: revised to R4-100237

R4-100236	Editorial correction in TS36.104 for Pico NodeB (CR 146r1 to 36.104 Rel-9) (Huawei)

Status: withdrawn

R4-100237	Editorial correction in TS36.104 for Pico NodeB (CR 146r1 to 36.104 Rel-9) (Huawei)

Comments:

Status: Technically endorsed

| R4-100055 | CR | Rel-9 | Corrections of operating band unwanted emissions for Local Area BS | CATT | 36.104 |
| --- | --- | --- | --- | --- | --- |

Comments:

Band 21 has been modified in the latest spec

Status: revised in R10-100238

R4-100238	Corrections of operating band unwanted emissions for Local Area BS (CR 145r1 to 36.104 Rel-9) (CATT)

Comments:

Status: endorsed

| R4-100150 | CR | Rel-9 | E-UTRA BS classification | Huawei | 36.141 |
| --- | --- | --- | --- | --- | --- |

Status: Technically endorsed

| R4-100151 | CR | Rel-9 | Maximum output power for Pico NodeB | Huawei | 36.141 |
| --- | --- | --- | --- | --- | --- |

Status: Technically endorsed

| R4-100152 | CR | Rel-9 | Frequency error requirement for Pico NodeB | Huawei | 36.141 |
| --- | --- | --- | --- | --- | --- |

Status: Technically endorsed

| R4-100155 | CR | Rel-9 | ACLR requirement for Pico NodeB | Huawei | 36.141 |
| --- | --- | --- | --- | --- | --- |

Status:  Technically endorsed

| R4-100156 | CR | Rel-9 | Operating band unwanted emissions requirement for Pico NodeB | Huawei | 36.141 |
| --- | --- | --- | --- | --- | --- |

Status: Technically endorsed

| R4-100056 | CR | Rel-9 | Spurious emissions requirement for Local Area BS | CATT | 36.141 |
| --- | --- | --- | --- | --- | --- |

Comments:

Same comment as R4-100225 regarding the removal of the NOTE

E///: general comment is the spec expansion due to BS classes and there are table that have the same content except may be from one value so may consider for next meeting how to avoid this.

Also Band 21 has been modified in the latest spec

Status: revised into R4-100239.

R4-100239	Spurious emissions requirement for Local Area BS (CR 147r1 to 36.141 Rel-9) (CATT)

Comments:

Status: endorsed

| R4-100153 | CR | Rel-9 | Reference sensitivity level requirement for Pico NodeB | Huawei | 36.141 |
| --- | --- | --- | --- | --- | --- |

Status: Technically endorsed

| R4-100057 | CR | Rel-9 | Dynamic range requirement for Local Area BS | CATT | 36.141 |
| --- | --- | --- | --- | --- | --- |

Status: Technically endorsed

| R4-100058 | CR | Rel-9 | In-channel selectivity for Local Area BS | CATT | 36.141 |
| --- | --- | --- | --- | --- | --- |

Status: Technically endorsed

| R4-100059 | CR | Rel-9 | ACS and narrow band blocking for Local Area BS | CATT | 36.141 |
| --- | --- | --- | --- | --- | --- |

Status: Technically endorsed

| R4-100154 | CR | Rel-9 | Blocking requirement for Pico NodeB | Huawei | 36.141 |
| --- | --- | --- | --- | --- | --- |

Status: revised in R4-100224

R4-100224	Blocking requirement for Pico NodeB (CR 157r1 to 36.141 Rel-9) (Huawei)

Comments:

Same comment as R4-100225 and R4-100056 regarding the removal of the NOTE.

NSN:	- In table 7.6.4.2 references to pico base station are missing.

- In table 7.6.3.6 for E-UTRA TDD band 34: “WA” is missing in front of E-UTRA.

- Also at the end of the table 7.6-4, the reference to TR 25. is false (set to [8] while in the list of references it is [11]).

Status: revised to 240

R4-100240	Blocking requirement for Pico NodeB (CR 157r2 to 36.141 Rel-9) (Huawei)

Comments:

Status: technically endorsed

| R4-100060 | CR | Rel-9 | Receiver intermodulation for Local Area BS | CATT | 36.141 |
| --- | --- | --- | --- | --- | --- |

Status: Technically endorsed

| R4-100061 | CR | Rel-9 | Performance requirement for Local Area BS | CATT | 36.141 |
| --- | --- | --- | --- | --- | --- |

Status: Technically endorsed

## 2.5	RF requirements for Multicarrier and Multi-RAT BS (Conformance test) [RInImp9-RFmulti]

| R4-100033 | LS in | LS on European Harmonised Standard for MSR Base Stations (TFES-09-121r1 Source: ETSI MSGTFES, To: TSG RAN WG4,TSG GERAN WG1, Cc: TSG RAN,ETSI ERM) | ETSI MSGTFES |
| --- | --- | --- | --- |

Comments:

Discussion regarding the time plan. Do we need to have this ready by march?

E///: we don’t need to have every thing ready. But still it is very tough schedule. agreed CRs (but not approved by RAN) can be accepted by TFES. RAN-4 can continue working on this until May meeting.

Status: Noted

| R4-100211 | LS in |  | Reply to LS Response on support of non-contiguous frequency bands for MSR BS | TSG GERAN WG1 |
| --- | --- | --- | --- | --- |

Status: Noted

| R4-100212 | LS in |  | Reply LS to “LS on Status of the MSR Work Item” | TSG GERAN WG1 |
| --- | --- | --- | --- | --- |

Comments:

Discussion on the work load on RAN4 and how to handle the actions from GERAN and TFES.

Status: Noted

| R4-100213 | LS in |  | LTE Base Station mask options | ECC SE PT 42 |
| --- | --- | --- | --- | --- |

Comments:

Status: Noted

### 2.5.1	General (Common sections of conformance test aspect)

| R4-100108 | Discussion | Test configurations overview | Ericsson |
| --- | --- | --- | --- |

Comments:

NSN: test configuration should be different for Rx and Tx.

Regarding Rx part, test config 2: 5mhz is considered but MSR may not support 5 mhz BW.

Regarding Tx part, it is a good start however need for single carrier test to be here not only referring to the existing spec.

TC4 could be divided to TC4A and TC4B as there is UTRA and EUTRA.

Huawei: Different view in the principle 3. Some concern about this principle.

E///: generally this should be seen as a starting point.

Status: Noted

| R4-100109 | Approval | Test configurations further details | Ericsson |
| --- | --- | --- | --- |

Comments:

Huawei:

TC4: again have a different view on the configuration.

Status: Noted

| R4-100114 | Approval | TP for TS 37.141 clause 2,3 and 4. | Ericsson |
| --- | --- | --- | --- |

Comments:

NSN: concern about table of mapping in 4.9. Needs further discussion

NSN: have also a contribution for the same sections of 37.141 in R4-100027.

(revised to merge with R4-100027)

Status: revised to 241

R4-100241	TP for TS 37.141 clause 2,3 and 4. (Ericsson)

Status: in principle agreed

| R4-100028 | Approval | TP for TS37.141: Selection of configurations for testing | Nokia Siemens Networks |
| --- | --- | --- | --- |

Status: in principle agreed

| R4-100029 | Approval | TP for TS37.141: General test conditions and declarations | Nokia Siemens Networks |
| --- | --- | --- | --- |

Comments:

E///: A good starting point but we may need some additions: We need an extensive chapter that describe the power and carriers declarations

NSN: suggests to note the doc and have discussion on how to move forward

Status: Noted

| R4-100027 | Approval | TP for TS37.141: Regional requirements | Nokia Siemens Networks |
| --- | --- | --- | --- |

Comments:

E///: similar to E/// to R4-100114. suggests as way forward to have both merges. Basically there is not conflict of the two.

Status: noted

| R4-100026 | Approval | TP for TS37.141: Format and interpretation of tests | Nokia Siemens Networks |
| --- | --- | --- | --- |

Status: in principle agreed

| R4-100025 | Approval | TP for TS37.141: Manufacturers declarations of regional and optional requirements | Nokia Siemens Networks |
| --- | --- | --- | --- |

Comments:

E///: proposal in general is good.

Status: Notes

| R4-100030 | Discussion | MSR corrections in TS 37.104 | Nokia Siemens Networks |
| --- | --- | --- | --- |

Comments:

E///: Concerns about the removal note 1: agrees that we should point to the requirements that apply but may need to modify the note in stead of removing it.

Status: Noted

| R4-100024 | Approval | TP for TS37.141: Applicability of requirements | Nokia Siemens Networks |
| --- | --- | --- | --- |

Comments:

E///: also has a proposal on this.

Consider why do we need to repeat these table?

Status: Noted

| R4-100115 | Approval | TP for TS 37.141 clause 5; Applicability of requirements | Ericsson |
| --- | --- | --- | --- |

Status: Noted

### Transmitter characteristics

| R4-100110 | Approval | TX requirements test configurations | Ericsson |
| --- | --- | --- | --- |

Comments:

NSN: We Need to Understand which configurations are involved in certain declarations. What if a BS to support 3RAT then would it be to test TC4A or TC4B or TC4A and TC4B  (see comment in R4-100108 for TC4A TC4B meaning for NSN)???

We need to determine what it is the more limiting case and do not go through all test cases.

Need to discuss requirement by requirement.

E///: Suggest to proceed on 2 steps: first the declaration what you are capable of, and then for each configuration derive the tests.

Status: Noted

| R4-100077 | Discussion | MSR Tx test configurations | Nokia Siemens Networks |
| --- | --- | --- | --- |

Comments:

E///: once you select a given declaration you pick a column and execute all the tests in this column ?

If you look the columns are mutually exclusive. Each column has its possible configurations. The proposal is to test only one specific configuration.

Huawei: Slightly prefer NSN’s proposal.

Telecom Italia: In single carrier, We refer to the existing requirements ?

NSN: Yes and no. not always use the for Single carrier configuration. It depends on the requirement.

E///: we need to have an MSR self contained spec.

Status: Noted

| R4-100186 | Discussion | Tx test configurations for MSR test specification | Huawei |
| --- | --- | --- | --- |

Comments:

E///: good to see this. Principle one is inline of what is proposed by E///

Principle 2: you should make sure that you have the highest PSD at the edge.

Good to bring this.

Principle 3:

Minimum of the RF BW and maximum of the filter bandwidth, this an implementation related and should avoid test definition based on implementations.

Status: Noted

| R4-100116 | Approval | TP for TS 37.141 clause 6.2; Base station output power | Ericsson |
| --- | --- | --- | --- |

Comments:

NSN: Why not just Reference to single carrier tests.

E///: agree that test procedures could be referred.

Status: Noted

| R4-100117 | Approval | TP for TS 37.141 clause 6.6.1; Transmitter spurious emissions | Ericsson |
| --- | --- | --- | --- |

Comments:

NSN: similar comments as previous

Needs more discussion

Status: Noted

| R4-100199 | Discussion | Operating Band Unwanted emission mask (UEM) for Band Category 2 | Vodafone |
| --- | --- | --- | --- |

Comments:

Telecom Italia: R4100212 from GERAN indicates how to deal with.

Good point taken by Vodafone.

Keep the mask as it is and use the implementation from GERAN

E///: also agree to clarify this in the TR. Does not mean that this does not work for 43dm (we can have more power); no where in the spec it is mentioned that this the case.

mask should not be dependent in the power.

Support the proposal from telecom Italia.

Vodafone: would like to get feedback from vendors.

Would like to make sure that when it come to field deployment there will be no problem

NSN: agree with E/// on the comment but within certain limit. We can probably have more power but not too much power.

Need more discussion

ALU: GERAN agreement to keeping the mask should be viable. Other solution is to know what level power the operators wants and then may be increase the absolute level.

Status: Noted

| R4-100080 | Discussion | Correction of additional spurious emission requirement for BC2 | Nokia Siemens Networks |
| --- | --- | --- | --- |

Comments:

E///: good way forward. Propose to endorse the CR.

Status: Revised in 100242

R4-100242	Correction of additional spurious emission requirement for BC2 (CR 1 to 37.104 Rel-9) (Nokia Siemens Networks)

Status: Technically endosed

| R4-100081 | Discussion | Correction of Transmitter intermodulation | Nokia Siemens Networks |
| --- | --- | --- | --- |

Comments:

E///:

Regarding Transmit Intermodulation requirement: not sure is the more stringent requirement and would like to keep it as it is (keep both)

Status: Notes

| R4-100120 | Approval | TP for TS 37.141 clause 6.7; Transmitter intermodulation | Ericsson |
| --- | --- | --- | --- |

Status: Noted

| R4-100118 | Approval | TP for TS 37.141 clause 6.6.2; Operating band unwanted emissions | Ericsson |
| --- | --- | --- | --- |

Status: Noted

| R4-100119 | Approval | TP for TS 37.141 clause 6.6.4; Adjacent Channel Leakage power Ratio (ACLR) | Ericsson |
| --- | --- | --- | --- |

Status: Noted

### 2.5.3	Receiver characteristics

| R4-100015 | Discussion | MSR Rx test configurations | Nokia Siemens Networks |
| --- | --- | --- | --- |

Comments:

ALU: agree with configuration but:

Maximum RF BW is not the most stringent for Rx side

We may need some additional test to cover Cases where used BW is lower than maximum BW.

NSN: agree that it may be additional ones. We should agree in the principle of test configurations and we can add scenarios later.

Status: Noted

| R4-100111 | Approval | RX requirements test configurations | Ericsson |
| --- | --- | --- | --- |

Comments:

NSN:

Narrow band blocking . we should take into account the multi carrier MSR.

E///: yes should be done.

Status: Noted

Way forward: (RX )make a summary of open issue so that people are aware of.

| R4-100100 | Approval | TP for TS 37.141, clause 7.8 MSR Receiver in-channel selectivity | Ericsson |
| --- | --- | --- | --- |

Comments:

NSN: general comment on the Rx: as for Tx, we need to first finalise the test configuration and then agree on the TPs.

Status: Noted

| R4-100101 | Approval | TP for TS 37.141, clause 7.7- MSR Receiver intermodulation | Ericsson |
| --- | --- | --- | --- |

Comments:

Tables 7.7.5.1-1 and 7.7.5.2-1 referenced subclauses for PRefesens are false.

Status: Noted

| R4-100102 | Approval | TP for TS 37.141, clause 7.6 MSR Receiver spurious emissions | Ericsson |
| --- | --- | --- | --- |

Status: Noted

| R4-100103 | Approval | TP for TS 37.141, clause 7.5 MSR Receiver out-of-band blocking | Ericsson |
| --- | --- | --- | --- |

Status: Noted

| R4-100104 | Approval | TP for TS 37.141, clause 7.4 MSR Receiver in-band selectivity and blocking | Ericsson |
| --- | --- | --- | --- |

Status: Noted

### 2.5.4	Others

| R4-100062 | Discussion | Considerations of BC3 test configuration | CATT |
| --- | --- | --- | --- |

Comments:

E///: good thing to bring the TDD case.

Status: Noted

## Dual-Cell HSUPA [RANimp-DC_HSUPA] <R1>

| R4-100216 | LS in | LS on MAC agreements for DC-HSUPA | TSG RAN WG2 |
| --- | --- | --- | --- |

Status: Noted

| R4-100013 | Discussion | Consideration on E-TFC selection for DC-HSUPA | Huawei Technologies Co., Ltd. |
| --- | --- | --- | --- |

Comments:

Status:  Noted

| R4-100172 | Discussion | 25.133 TP E-TFC selection in UE for DC-HSUPA | Qualcomm Incorporated |
| --- | --- | --- | --- |

Status: Revised in 208

| R4-100208 | Discussion | 25.133 TP E-TFC selection in UE for DC-HSUPA | Qualcomm Incorporated |
| --- | --- | --- | --- |

Comments:

InterDigital: Interdig have a different approach from qualcomm’s one. The Right approach will be debated in RAN2.

Qualcomm: Our RAN4 is on line with our Qualcomm’s RAN2 proposal.

E///: slight concerns: should prioritize the retransmission

If it up to the implementation, then how the network will know what is the MPR.

Qualcomm: in the proposed proposal,. the retransmission are prioritized.

In the single carrier there is no MPR mandated.

Interdigital: if we specify a single value of MPR we will face a problem of Complexity.

Status: Noted

| R4-100079 | Approval | ETFC Restriction for DC-HSUPA | Nokia, Nokia Siemens Networks, Interdigital |
| --- | --- | --- | --- |

Status: Revised in 226

R4-100226	ETFC Restriction for DC-HSUPA (Nokia, Nokia Siemens Networks, Interdigital, Huawei)

Comments:

Qualcomm: was surprised to see Huawei co-sourcing the contribution as according to Qualcomm’s understanding, the contribution suggests a fixed MPR value while Huawei’s position is to not supporting this.

Huawei: co-sourced this contribution means we accept the content, but we need still to clarify few things.

InterDigital: can not agree on Qualcomm’s proposal as this is Pushing ran2 decision to ran4

Status: Noted

| R4-100171 | Discussion | TX-RX frequency separation for DC-HSUPA | Qualcomm Incorporated |
| --- | --- | --- | --- |

Comments:

E///: come back to this issue in the next meeting.

Status: Noted

| R4-100173 | Discussion | Independent configuration of maximum UL Tx power in DC-HSUPA | Qualcomm Incorporated |
| --- | --- | --- | --- |

Comments:

E///: concern about the introduction of this parameter at this late stage. We didn’t perform any system study to introduce this parameter.

We should concentrate on other issue that are not closed in WI.

Desactivation: there are other ways for handling it.

Nokia: ask why Qualcomm is proposing to introduce this signalling while Qualcomm refuses to agree on REFSENS requirements whereas is it similar.

Status: Noted

| R4-100044 | Discussion | In-band blocking DC-HSDPA requirement due to DC-HSUPA | Samsung |
| --- | --- | --- | --- |

Status: Noted

| R4-100070 | Discussion | DC-HSUPA blocking and intermodulation measurements | Nokia |
| --- | --- | --- | --- |

Comments:

This could be a good indicator but in final requirements simulations we can not use this as basis.

Value for measurement and simulations are different from both Qualcomm’s measurement and simulation values. Asks Nokia to check as there might be an error there.

Nokia: agree but felt that it could be good to provide this as indicator.

Status: Noted

| R4-100170 | Discussion | Receiver RF requirements for DC-HSUPA | Qualcomm Incorporated |
| --- | --- | --- | --- |

Comments:

E///:

- Taken into account the insertion loss when calculate the input power at the receiver?

- Formula in figure 1: not sure if 2/3 is correct. Is it used as it is in simulations or was it corrected?

- (band noise) What assumption on the duplexer and on the ACLR Rx channel is used ?

- Why green curve is higher then the red one ?

- Insertion loss need to be included in final simulation

- Used the number in the figure. But will double-check if there is really

- Didn’t assume any ACLR or duplexer. These are measurement results.

- 3dB factor: the reason could the I or Q measurement. ( factor of two,. But need to double-check.

( concentrate on the methodology.

Status: Noted

| R4-100121 | Discussion | DC-HSUPA related receiver requirements | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

Comments:

Qualcomm:

- Narrow band blocking: two configuration (Band II, IV, V, X or B in the third column and III, VIII, XII, XIII, XIV in the forth column) are presented. Is this assume the left (Band II, IV, V, X) one or the right one (Band III, VIII, XII, XIII, XIV).

- insertion loss is properly assumed. For the blocker should we also assume the insertion loss ?

E///: - used band 2. but need to double check.

- yes but will double check

Samsung: What type of noise used

E///: assumed white noise

Vodafone: Should focus on the evaluation if there is a real issue in the deployment. No need to go into the details

E///: last meeting the agreement is that we would specify the receiver requirements so you need to go into the detail.

E///: Draft CR is available 243.

Status: Noted

R4-100243	CR on Introduction of DC-HSUPA related receiver requirements (CR 695 to 25.101 Rel-9) (ST Ericsson)

Comment:

Nokia: seems to be a good way. Supports the proposal.

Qualcomm: want to clarify that the intention is to introduce intermod and inband blocking and not define a refsens.

We need to see the final outcome for the different band (blocking and intermod) as some band may need relaxation some bands may not. could be difficult to use one reference table and one offset for all bands.

This is one way to present it but can be other ways depending on the outcome of the study. Qualcomm will present some thing.

Vodafone: need more study.

Introduction of Refpow: have concerns about this as for Vodafone it is the same as refsens

E///: there is no intention to specify refsens.

Should come to an agreement in the next meeting as the WI has been delayed because of this

Nokia: propose to use this as a framework.

Qualcomm: will try to provide another proposal. So that to have two options to choose.

Status: Noted

R4-100249	Text Proposal of Rx core requirements for DC-HSUPA (Qualcomm Incorporated)

Comment:

Error in table XXX, 10.3 instead of XX

Vodafone: what is the level of blockers applied compared to single carrier case.

Qualcomm: in general requirements will be relaxed compared to single carrier but the level of relaxation will be hopefully decided  next meeting

Status: Noted

## 2.7	Enhanced Dual-Layer transmission for LTE [LTEimp-eDL] <R1>

| R4-100047 | Discussion | Considerations on dual-layer beamforming | Nokia |
| --- | --- | --- | --- |

Comments:

ST-E///: We need to keep the definitions on the latest spec to avoid confusion.

Status: noted

| R4-100063 | Discussion | Further considerations on Dual-layer BF performance requirements | CATT |
| --- | --- | --- | --- |

Comments:

Status: noted

| R4-100088 | Discussion | Framework for dual-layer beamforming | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

Comments:

Status: noted

| R4-100136 | Discussion | Simulation Framework for LTE Rel-9 Enhanced DL Transmission | Motorola |
| --- | --- | --- | --- |

Status: Noted

| R4-100157 | Discussion | Consideration on dual-layer beamforming performance requirement | Huawei |
| --- | --- | --- | --- |

Status: Noted

| R4-100179 | Approval | Framework for DL-BF demodulation requirements | CMCC |
| --- | --- | --- | --- |

Status: revised in R4-100248

| R4-100202 | Discussion | Some considerations on dual-layer beamforming testing | NEC |
| --- | --- | --- | --- |

Status: Noted

R4-100248	Framework for DL-BF demodulation requirements (CMCC)

Comments:

E///: good progress made in this issue however rank one is still under discussion. Strong concern from some companies.

Status: Email approval

## 2.8	MBMS support in LTE [MBMS_LTE] <R2>

| R4-100158 | Discussion | Test reference value for LTE MBMS | Huawei |
| --- | --- | --- | --- |

Status: Noted

| R4-100159 | Discussion | LTE MBMS simulation results for alignment (FDD) | Huawei |
| --- | --- | --- | --- |

Status: Revised in 223

R4-100223	LTE MBMS simulation results for alignment (FDD) (Huawei)

Status: Noted

| R4-100160 | Discussion | LTE MBMS simulation results for alignment (TDD) | Huawei |
| --- | --- | --- | --- |

Status: Noted

| R4-100161 | Discussion | LTE MBMS simulation results with impairments | Huawei |
| --- | --- | --- | --- |

Status: Noted

| R4-100180 | Discussion | Ideal simulation results for LTE MBMS | CMCC |
| --- | --- | --- | --- |

Status: Noted

| R4-100164 | Discussion | Summary of PMCH alignment results | Huawei |
| --- | --- | --- | --- |

Comments:

Encourage more input from the interested companies in order to set the requirements.

Status: Noted

| R4-100165 | Discussion | Summary of PMCH simulation results with impairments | Huawei |
| --- | --- | --- | --- |

Comments:

Same comment as 164

Status: Noted

| R4-100203 | Discussion | Further considerations for eMBMS | NEC |
| --- | --- | --- | --- |

Comments:

Huawei: Different view on EVM:

- Concerns on having conformance test for EVM for PMCH

- RAN4 normal procedure to derive requirements is to run Simulation on PMCH to derive the corresponding requirements

NEC:

- No PMCH conformance test is proposed.

- No signal quality difference is expected so we can adopt the requirements from PDSCH

Status: Noted

| R4-100162 | CR | Rel-9 | 36.101 CR: Editorial corrections on LTE MBMS reference measurement channels | Huawei | 36.101 |
| --- | --- | --- | --- | --- | --- |

Comments:

Status: technically endorsed

| R4-100163 | Approval | Minutes from LTE MBMS demodulation ad hoc | Huawei |
| --- | --- | --- | --- |

Comments:

Status: withdrawn

| R4-100038 | Discussion | MBSFN simulation results | Samsung |
| --- | --- | --- | --- |

Status: Withdrawn

| R4-100064 | Discussion | Ideal simulation results for LTE MBMS demodulation requirements | CATT |
| --- | --- | --- | --- |

Comments:

Status: Withdrawn

## Positioning Support for LTE [LCS_LTE] <R2>

| R4-100067 | CR | Rel-9 | AOA and TA measurement report mappings | CATT, Ericsson, ST-Ericsson | 36.133 |
| --- | --- | --- | --- | --- | --- |

Comments:

Status: Technically endorsed

| R4-100097 | Approval | Remaining issues on assistance data for OTDOA positioning window size | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

Comments:

Nokia: should think about practical considerations: e.g. max signal level UE can hear, Difference level between the two cells,…etc

Status: Noted

| R4-100098 | Approval | Link simulation results on OTDOA RSTD accuracy | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

Comments:

Nokia: how do you force the Algo (in Annex 1) to work in practice with difference in loading, Muting, …

E///: fading and all other thing are captured in the correlation computed.

Motorola: is muting is subframe based?

E///: muting is not used in the contribution. No need of using muting in synchronous case.

Motorola: Still if you do not need muting for synchronous case. The network may have implemented muting that the UE is not aware of.

Status: Noted

| R4-100130 | Discussion | Impact of window size on positioning performance | Qualcomm Incorporated |
| --- | --- | --- | --- |

Comments:

Document is saved on .docx (office 2007) format.

Nokia: again (as for E/// contribution) some practical physical considerations.

DO you assume a false alarm threshold ?

Qualcomm: 1% false ALARM

Status: Noted

| R4-100167 | Discussion | System-level simulation results for OTDOA positioning | Huawei |
| --- | --- | --- | --- |

Comments:

Motorola: concerns about deriving the threshold based on the SNR (due to SNR estimation accuracy). In practice may have problem to use this compared to the use of Signal level.

Status: Noted

R4-100230	Remaining issues on assistance data for OTDOA positioning  maximum range for estimated timing difference (Ericsson, ST-Ericsson)

Comment:

Huawei: The value of the time offset is not always positive: serving cell may be behind the other cell. Thus we still need signalling.

Nokia: Same as for previous contributions, we need to look into the practical limitations.

Status: Noted

R4-100231	Draft LS response on assistance information for OTDOA positioning support for LTE  remaining issues (Ericsson, ST-Ericsson)

Comment:

E///: Discussion on RAN2 to freeze these parameters by March. It is better if the LS is receive before next meeting

Nokia: some parts of the LS are agreeable and some other we need more discussion.

Status: revised to 252

R4-100252	Draft LS response on assistance information for OTDOA positioning support for LTE  remaining issues (Ericsson, ST-Ericsson)

Comments:

13 bits cover 90Km, should we consider 14Km to cover the 100Km ?

Nokia: 90 should be sufficient on the offline discussion assumption

E///: do not see any reason to go above.

Status: email approval.

| R4-100004 | Approval | 3GPP TS 36.171 V0.1.0 (2010-01) | Alcatel-Lucent |
| --- | --- | --- | --- |

Comments:

Few issues raised by Nokia and E///: (1) RRC state in 100004 and 100005 removed one and kept in the other. (2) Editorial UTRA parameters/abbreviation are still used as it is copied from different spec: We should use the E-UTRA ones.

ALU: Need a TP to make changes. We can not change any think now as this was approved last meeting

Status: in principle agreed

| R4-100005 | Approval | Text proposal on A-GNSS performance requirements for LTE | Alcatel-Lucent, Qualcomm Europe, Spirent Communica |
| --- | --- | --- | --- |

Comments:

Nokia: Why RRC state is removed from section 4.5 ? would like it to be kept.

ALU: reason for removal of this section is for alignment with GERAN spec.

Thales: confirm that in the GERAN there is no such section.

( Section to be kept. To be revised to capture this.

Status: revised in R4-100245

R4-100245	Text proposal on A-GNSS performance requirements for LTE (Alcatel-Lucent, Qualcomm Europe, Spirent Communica)

Status: in principle agreed.

| R4-100006 | Approval | Text proposal for Annex A of TS 36.171 | Alcatel-Lucent, Qualcomm Europe, Spirent Communica |
| --- | --- | --- | --- |

Status: in principle agreed.

| R4-100007 | Approval | Text proposal for Annex B of TS 36.171 | Alcatel-Lucent, Qualcomm Europe, Spirent Communica |
| --- | --- | --- | --- |

Comments:

Nokia: add section on the frequency error.

Thales: is ok to add this.

Status: to be revised to in R4-100246

R4-100246	Text proposal for Annex B of TS 36.171 (Alcatel-Lucent, Qualcomm Europe, Spirent Communica)

Status: in principle agreed.

| R4-100008 | Approval | Text proposal for Annex C of TS 36.171 | Alcatel-Lucent, Qualcomm Europe, Spirent Communica |
| --- | --- | --- | --- |

Status: in principle agreed.

| R4-100009 | Approval | Text proposal for Annex D of TS 36.171 | Alcatel-Lucent, Qualcomm Europe, Spirent Communica |
| --- | --- | --- | --- |

Status: in principle agreed.

| R4-100010 | Approval | Text proposal for Annex E of TS 36.171 | Alcatel-Lucent, Qualcomm Europe, Spirent Communica |
| --- | --- | --- | --- |

Status: in principle agreed.

| R4-100011 | Approval | Text proposal for Annex F of TS 36.171 | Alcatel-Lucent, Qualcomm Europe, Spirent Communica |
| --- | --- | --- | --- |

Status: in principle agreed.

| R4-100082 | Discussion | Discussion on RSTD STD requirements | Nokia |
| --- | --- | --- | --- |

Comments:

Motorola: agrees however raises that there is no studies showing quality measure is necessary or how useful this is.

E///: agree with Motorola comment.

( matter of time: This requires system analysis to see the benefits.

Status: Noted

| R4-100084 | Discussion | System level evaluation of the RSTD accuracy | Nokia |
| --- | --- | --- | --- |

Status: Noted

| R4-100166 | Discussion | On the framework of LTE positioning | Huawei |
| --- | --- | --- | --- |

Status: Noted

| R4-100168 | Discussion | Link-level simulation results for RSTD requirement | Huawei |
| --- | --- | --- | --- |

Comments:

Nokia: need alignment on to which value false alarm threshold are set.

Status: Noted

| R4-100169 | Discussion | Simulation results for UE Rx_Tx time difference measurement | Huawei |
| --- | --- | --- | --- |

Status: Noted

| R4-100065 | Discussion | Simulation results of UE Rx-Tx time difference measurement | CATT |
| --- | --- | --- | --- |

Comments:

E///: sampling rate use? (in order to compare to other contributions.)

CATT: 5 samples for 200ms

Huawei, Nokia: need to discuss implementation margin further.

Status: Noted

| R4-100092 | Discussion | Simulation Results for UE Rx - Tx Time Difference Measurement | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

Comments:

Nokia: agree with E/// on taking into account these imperfections,. Tx noise into the Rx bands, etc, in the implementation margin.

E///: in order to move forward. Suggestion to have lower geometry level than -3dB.

( needs further discussion.

Status: Noted

| R4-100131 | Discussion | Link level positioning simulation results | Qualcomm Incorporated |
| --- | --- | --- | --- |

Comments:

E///: - absolute error values should shown. Miss alignment in the assumptions. there is a miss-interpretation of SINR vs. SNR.

- Results from E/// and Huawei are aligned. In Qualcomm’s, the difference error is too large.

Nokia: if there is a difference in sampling weights in the Tx and Rx, this will have impacts. Would like to have this accounted in E///, Huawei and Qualcomm’s contributions

Qualcomm: - agree there are different assumption and may be the more important one is that Qualcomm used only one subframe accumulation: no accumulation.

- Difference between sampling in Rx and Tx was not considered.

Status: Noted

R4-100221	Considerations for Link-level Evaluations for RSTD Accuracy (Motorola)

Comments:

E///:  - one reuse for PRS ?

- muting is not needed for synchronous and still support this.

- -35dB considered, detection begin to be different from 0 at -20dB or even more. you will not detect any think at this level.

Motorola:

- reuse one assumed.

- does not agree that the detection is zero at -35dB.

- Regarding muting,. Agree that this will not be used in synchronous but UE has no information on this so the UE still have to assume there might be muting.

Disagreement of the two companies on the effect of reuse factor.

Status: Noted

| R4-100093 | Discussion | UE Rx - Tx Time Difference Measurement Report Mapping | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

Status: Noted

| R4-100066 | Approval | Mapping of UE RxTx time difference measurement | CATT |
| --- | --- | --- | --- |

Status: Noted

| R4-100094 | Discussion | RSTD Measurement Report Mapping | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

Comments:

Nokia: still need some alignment.

Status: Noted

| R4-100095 | LS out | Draft LS on Report Mapping of UE Measurements for Positioning | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

Comments:

Status: revised to 251

R4-100251	Draft LS on Report Mapping of UE Measurements for Positioning (Ericsson, ST-Ericsson)

Comments:

Status: Email approval

| R4-100083 | Discussion | Link simulation results for RSTD accuracy | Nokia |
| --- | --- | --- | --- |

Status: withdrawn

| R4-100096 | Approval | Remaining issues on assistance data for OTDOA positioning maximum range for estimated timing difference | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

Status: Withdrawn

| R4-100099 | LS out | Draft LS response on assistance information for OTDOA positioning support for LTE remaining issues | Ericsson, ST-Ericsson |
| --- | --- | --- | --- |

Status: Withdrawn

## 2.10	Close of the second session Meeting	(No later than Friday 5 p.m.)

Meeting closed on Friday at 16h36

# Phrases of the Week:

# Annex A	:	List of Documents

| Agenda | Tdoc | Type | Release | 'Title' | Source | 'Decision' |
| --- | --- | --- | --- | --- | --- | --- |
| 1.1 | R4-100001 | Approval |  | Proposed agenda | Chair | Approved |
| 2.2.1 | R4-100002 | Approval |  | Text Proposal on Home eNodeB Transmit Power Conformance Testing for Adjacent Channel Protection | Alcatel-Lucent | in principle agreed |
| 2.2.1 | R4-100003 | Discussion |  | Simulation results for ACK/NACK multiplexed to PUSCH over EVA5 | Alcatel-Lucent | Noted |
| 2.9 | R4-100004 | Approval |  | 3GPP TS 36.171 V0.1.0 (2010-01) | Alcatel-Lucent | in principle agreed |
| 2.9 | R4-100005 | Approval |  | Text proposal on A-GNSS performance requirements for LTE | Alcatel-Lucent, Qualcomm Europe, Spirent Communica | Revised in 245 |
| 2.9 | R4-100006 | Approval |  | Text proposal for Annex A of TS 36.171 | Alcatel-Lucent, Qualcomm Europe, Spirent Communica | in principle agreed |
| 2.9 | R4-100007 | Approval |  | Text proposal for Annex B of TS 36.171 | Alcatel-Lucent, Qualcomm Europe, Spirent Communica | Revised in 246 |
| 2.9 | R4-100008 | Approval |  | Text proposal for Annex C of TS 36.171 | Alcatel-Lucent, Qualcomm Europe, Spirent Communica | in principle agreed |
| 2.9 | R4-100009 | Approval |  | Text proposal for Annex D of TS 36.171 | Alcatel-Lucent, Qualcomm Europe, Spirent Communica | in principle agreed |
| 2.9 | R4-100010 | Approval |  | Text proposal for Annex E of TS 36.171 | Alcatel-Lucent, Qualcomm Europe, Spirent Communica | in principle agreed |
| 2.9 | R4-100011 | Approval |  | Text proposal for Annex F of TS 36.171 | Alcatel-Lucent, Qualcomm Europe, Spirent Communica | in principle agreed |
| 1.3 | R4-100012 | Approval |  | Bandwidth Aggregation Scenarios | US Cellular, Alcatel-Lucent, Huawei | Noted |
| 2.6 | R4-100013 | Discussion |  | Consideration on E-TFC selection for DC-HSUPA | Huawei Technologies Co., Ltd. | Noted |
| 1.4.3.3 | R4-100014 | Approval |  | TP for LTE-A RAN4 feasibility studies TR 36.815: Subclause 5.4.3 Receiver characteristics | Nokia Siemens Networks | in principle agreed |
| 2.5.3 | R4-100015 | Discussion |  | MSR Rx test configurations | Nokia Siemens Networks | Noted |
| 1.3.1 | R4-100016 | Discussion |  | LTE-Advanced carrier aggregation aspects for Rel-10 | TeliaSonera | Noted |
| 2.2.2 | R4-100017 | Approval |  | Text Proposal for 36.9xx: HeNB Measurements | NEC, picoChip Designs, Kyocera | in principle agreed |
| 2.2.2 | R4-100018 | Approval |  | Text Proposal for 36.9xx: HeNB Adaptive Frequency Selection | NEC | in principle agreed |
| 2.2.2 | R4-100019 | Approval |  | HeNB Power Control Based on HUE Measurement | NEC | in principle agreed |
| 2.2.2 | R4-100020 | Approval |  | Revision on Information Exchange Option 2 of TR36.921 | Kyocera, picoChip Designs, Qualcomm Incorporated, Institute for Information Industry (III), Coiler Corporation, NEC | in principle agreed |
| 1.4.4 | R4-100021 | Approval |  | TP for TR 36.815: RRM aspect | Nokia Siemens Networks, Nokia | Noted |
| 1.2 | R4-100022 | Approval |  | Work plan for the "Carrier Aggregation for LTE" WI in RAN4 | Nokia Siemens Networks, Nokia | in principle agreed |
| 1.4.3 | R4-100023 | Discussion |  | Expected changes to TS 36.104 due to CA WI | Nokia Siemens Networks | Noted |
| 2.5.1 | R4-100024 | Approval |  | TP for TS37.141: Applicability of requirements | Nokia Siemens Networks | Noted |
| 2.5.1 | R4-100025 | Approval |  | TP for TS37.141: Manufacturers declarations of regional and optional requirements | Nokia Siemens Networks | Noted |
| 2.5.1 | R4-100026 | Approval |  | TP for TS37.141: Format and interpretation of tests | Nokia Siemens Networks | in principle agreed |
| 2.5.1 | R4-100027 | Approval |  | TP for TS37.141: Regional requirements | Nokia Siemens Networks | Noted |
| 2.5.1 | R4-100028 | Approval |  | TP for TS37.141: Selection of configurations for testing | Nokia Siemens Networks | in principle agreed |
| 2.5.1 | R4-100029 | Approval |  | TP for TS37.141: General test conditions and declarations | Nokia Siemens Networks | Noted |
| 2.5.1 | R4-100030 | Discussion |  | MSR corrections in TS 37.104 | Nokia Siemens Networks | Noted |
|  | R4-100031 | Discussion |  |  |  | Withdrawn |
|  | R4-100032 | Discussion |  |  |  | Withdrawn |
| 2.5 | R4-100033 | LS in |  | LS on European Harmonised Standard for MSR Base Stations (TFES-09-121r1 Source: ETSI MSGTFES, To: TSG RAN WG4,TSG GERAN WG1, Cc: TSG RAN,ETSI ERM) | ETSI MSGTFES | Noted |
| 2.2.2 | R4-100034 | Approval |  | Simulation results of interference mitigation schemes and text proposal for TR 36.921 | ETRI | in principle agreed |
| 2.3 | R4-100035 | Discussion |  | HeNB inbound mobility simulation results | Samsung | Revised in 233 |
| 2.3 | R4-100036 | Discussion |  | Consideration on the HeNB inbound mobility simulation assumptions | Samsung | Noted |
| 2.3 | R4-100037 | Discussion |  | Consideration on the response to RAN2 LS on CSG mobility requirements | Samsung | Noted |
| 2.8 | R4-100038 | Discussion |  | MBSFN simulation results | Samsung | Withdrawn |
| 1.3.1 | R4-100039 | Discussion |  | Downlink simulation results for coexistence between LTE-A and LTE | Samsung | Withdrawn |
| 2.2.1 | R4-100040 | Discussion |  | Handling of missed HeNB performance requirements | Samsung | Revised in 227 |
| 2.2.1 | R4-100041 | CR | Rel9 | Corrections on HeNB performance requirements | Samsung | Revised in 228 |
| 2.2.1 | R4-100042 | CR | Rel9 | Corrections on HeNB performance requirements | Samsung | Revised in 229 |
| 1.4.1 | R4-100043 | Discussion |  | Effective antenna gain proposal in TR35.942 | Samsung | Noted |
| 2.6 | R4-100044 | Discussion |  | In-band blocking DC-HSDPA requirement due to DC-HSUPA | Samsung | Noted |
| 1.3.1 | R4-100045 | Discussion |  | UE to UE coexistence study for Carrier aggregation | Samsung | Noted |
| 1.3.1 | R4-100046 | Discussion |  | ACIR modelling for Uplink LTE-A co-existence simulation | Samsung | Revised in 201 |
| 2.7 | R4-100047 | Discussion |  | Considerations on dual-layer beamforming | Nokia | Noted |
| 2.2.2 | R4-100048 | Approval |  | Text Proposal for TR 36.921: Interference control for LTE Rel-9 HeNB cells | Nokia Siemens Networks, Nokia | Revised in 204 |
| 2.2.3 | R4-100049 | Approval |  | Text Proposal for TR 36.922: TDD HeNB Synchronization using Network Listening | Nokia Siemens Networks, Nokia, Qualcomm Europe | in principle agreed |
| 2.2.3 | R4-100050 | Discussion |  | Further consideration on LTE TDD HeNB synchronization use case and extra signaling | Nokia Siemens Networks, Nokia | Noted |
| 2.2.2 | R4-100051 | Discussion |  | Victim UE Aware Downlink Interference Management | picoChip Designs | Revised in 193 |
| 2.2.2 | R4-100052 | Approval |  | Text Proposal for TR36.921: Victim UE Aware Interference Management | picoChip Designs | Revised in 194 |
| 1.3.1 | R4-100053 | Discussion |  | Analysis of UL Carrier Aggregation | CATT | Noted |
| 2.2.1 | R4-100054 | CR | Rel-9 | Corrections of operating band unwanted emissions for Home BS | CATT | Technically endorsed |
| 2.4 | R4-100055 | CR | Rel-9 | Corrections of operating band unwanted emissions for Local Area BS | CATT | Revised in 238 |
| 2.4 | R4-100056 | CR | Rel-9 | Spurious emissions requirement for Local Area BS | CATT | Revised in 239 |
| 2.4 | R4-100057 | CR | Rel-9 | Dynamic range requirement for Local Area BS | CATT | Technically endorsed |
| 2.4 | R4-100058 | CR | Rel-9 | In-channel selectivity for Local Area BS | CATT | Technically endorsed |
| 2.4 | R4-100059 | CR | Rel-9 | ACS and narrow band blocking for Local Area BS | CATT | Technically endorsed |
| 2.4 | R4-100060 | CR | Rel-9 | Receiver intermodulation for Local Area BS | CATT | Technically endorsed |
| 2.4 | R4-100061 | CR | Rel-9 | Performance requirement for Local Area BS | CATT | Technically endorsed |
| 2.5.4 | R4-100062 | Discussion |  | Considerations of BC3 test configuration | CATT | Noted |
| 2.7 | R4-100063 | Discussion |  | Further considerations on Dual-layer BF performance requirements | CATT | Noted |
| 2.8 | R4-100064 | Discussion |  | Ideal simulation results for LTE MBMS demodulation requirements | CATT | Withdrawn |
| 2.9 | R4-100065 | Discussion |  | Simulation results of UE Rx-Tx time difference measurement | CATT | Noted |
| 2.9 | R4-100066 | Approval |  | Mapping of UE RxTx time difference measurement | CATT | Noted |
| 2.9 | R4-100067 | CR | Rel-9 | AOA and TA measurement report mappings | CATT, Ericsson, ST-Ericsson | Technically endorsed |
| 1.3.1 | R4-100068 | Discussion |  | Considerations of UE architectures for Carrier aggregation | Nokia | Noted |
| 1.3.1 | R4-100069 | Discussion |  | Considerations of UE categories for Carrier aggregation | Nokia | Noted |
| 2.6 | R4-100070 | Discussion |  | DC-HSUPA blocking and intermodulation measurements | Nokia | Noted |
| 1.4.3.1 | R4-100071 | Approval |  | TP for LTE-A RAN4 feasibility studies TR 36.815: Subclause 5.4.1 General | Nokia Siemens Networks | in principle agreed |
| 1.4.3.1 | R4-100072 | Approval |  | TP for LTE-A RAN4 feasibility studies TR 36.815: Subclause 5.4.4 Implementation feasibility of carrier aggregation scenarios | Nokia Siemens Networks | Noted |
| 1.4.3.2 | R4-100073 | Approval |  | TP for LTE-A RAN4 feasibility studies TR 36.815: Subclause 5.4.2.1 General | Nokia Siemens Networks | in principle agreed |
| 1.4.3.2 | R4-100074 | Approval |  | TP for LTE-A RAN4 feasibility studies TR 36.815: Subclause 5.4.2.2 Base Station output power | Nokia Siemens Networks | in principle agreed |
| 1.4.3.2 | R4-100075 | Approval |  | TP for LTE-A RAN4 feasibility studies TR 36.815: Subclause 5.4.2.3 Transmitted signal quality | Nokia Siemens Networks | in principle agreed |
| 1.4.3.2 | R4-100076 | Approval |  | TP for LTE-A RAN4 feasibility studies TR 36.815: Subclause 5.4.2.4 Unwanted emissions | Nokia Siemens Networks | in principle agreed |
| 2.5.2 | R4-100077 | Discussion |  | MSR Tx test configurations | Nokia Siemens Networks | Noted |
| 2.3 | R4-100078 | Discussion |  | Performance requirements for UTRA inbound handover | Nokia, Nokia Siemens Networks | Noted |
| 2.6 | R4-100079 | Approval |  | ETFC Restriction for DC-HSUPA | Nokia, Nokia Siemens Networks, Interdigital | Revised in 226 |
| 2.5.2 | R4-100080 | Discussion |  | Correction of additional spurious emission requirement for BC2 | Nokia Siemens Networks | Revised in 242 |
| 2.5.2 | R4-100081 | Discussion |  | Correction of Transmitter intermodulation | Nokia Siemens Networks | Noted |
| 2.9 | R4-100082 | Discussion |  | Discussion on RSTD STD requirements | Nokia | Noted |
| 2.9 | R4-100083 | Discussion |  | Link simulation results for RSTD accuracy | Nokia | Withdrawn |
| 2.9 | R4-100084 | Discussion |  | System level evaluation of the RSTD accuracy | Nokia | Noted |
| 1.4.4 | R4-100085 | Discussion |  | Mobility measurements and carrier aggregation | Nokia, Nokia Siemens Networks | Noted |
| 1.3.1 | R4-100086 | Discussion |  | Some considerations on Rel-10 Carrier Aggregation Deployment Scenarios | Verizon | Noted |
| 2 | R4-100087 | Information |  | Reference sensitivity and MSD | Ericsson, ST-Ericsson | Not Handled |
| 2.7 | R4-100088 | Discussion |  | Framework for dual-layer beamforming | Ericsson, ST-Ericsson | Noted |
| 1.3.1 | R4-100089 | Discussion |  | Inter-band carrier aggregation scenarios | Ericsson, ST-Ericsson | Noted |
| 1.4.2.1 | R4-100090 | Discussion |  | Contiguous carrier aggregation: impact on UE radio requirements | Ericsson, ST-Ericsson | Noted |
| 1.4.4 | R4-100091 | Discussion |  | Mobility Measurements in Carrier Aggregation Scenarios | Ericsson, ST-Ericsson | Noted |
| 2.9 | R4-100092 | Discussion |  | Simulation Results for UE Rx - Tx Time Difference Measurement | Ericsson, ST-Ericsson | Noted |
| 2.9 | R4-100093 | Discussion |  | UE Rx - Tx Time Difference Measurement Report Mapping | Ericsson, ST-Ericsson | Noted |
| 2.9 | R4-100094 | Discussion |  | RSTD Measurement Report Mapping | Ericsson, ST-Ericsson | Noted |
| 2.9 | R4-100095 | LS out |  | Draft LS on Report Mapping of UE Measurements for Positioning | Ericsson, ST-Ericsson | Revised in 251 |
| 2.9 | R4-100096 | Approval |  | Remaining issues on assistance data for OTDOA positioning maximum range for estimated timing difference | Ericsson, ST-Ericsson | Withdrawn |
| 2.9 | R4-100097 | Approval |  | Remaining issues on assistance data for OTDOA positioning window size | Ericsson, ST-Ericsson | Noted |
| 2.9 | R4-100098 | Approval |  | Link simulation results on OTDOA RSTD accuracy | Ericsson, ST-Ericsson | Noted |
| 2.9 | R4-100099 | LS out |  | Draft LS response on assistance information for OTDOA positioning support for LTE remaining issues | Ericsson, ST-Ericsson | Withdrawn |
| 2.5.3 | R4-100100 | Approval |  | TP for TS 37.141, clause 7.8 MSR Receiver in-channel selectivity | Ericsson | Noted |
| 2.5.3 | R4-100101 | Approval |  | TP for TS 37.141, clause 7.7- MSR Receiver intermodulation | Ericsson | Noted |
| 2.5.3 | R4-100102 | Approval |  | TP for TS 37.141, clause 7.6 MSR Receiver spurious emissions | Ericsson | Noted |
| 2.5.3 | R4-100103 | Approval |  | TP for TS 37.141, clause 7.5 MSR Receiver out-of-band blocking | Ericsson | Noted |
| 2.5.3 | R4-100104 | Approval |  | TP for TS 37.141, clause 7.4 MSR Receiver in-band selectivity and blocking | Ericsson | Noted |
| 1.4.3 | R4-100105 | Discussion |  | Contiguous carrier aggregation: Overview of impact on BS radio requirements | Ericsson, ST-Ericsson | Noted |
| 1.4.3 | R4-100106 | Discussion |  | Contiguous carrier aggregation: Overview of impact on BS demodulation requirements | Ericsson, ST-Ericsson | Noted |
| 1.4.3 | R4-100107 | Discussion |  | Inter-band carrier aggregation across different bands; feasibility of using RBs per CC as per rel-8 | Ericsson, ST-Ericsson | Noted |
| 2.5.1 | R4-100108 | Discussion |  | Test configurations overview | Ericsson | Noted |
| 2.5.1 | R4-100109 | Approval |  | Test configurations further details | Ericsson | Noted |
| 2.5.2 | R4-100110 | Approval |  | TX requirements test configurations | Ericsson | Noted |
| 2.5.3 | R4-100111 | Approval |  | RX requirements test configurations | Ericsson | Noted |
| 1.3.1 | R4-100112 | Discussion |  | Implementation issues for combining multiple carriers | Ericsson, ST- Ericsson | Noted |
| 1.4.3.2 | R4-100113 | Discussion |  | Co-existence issues for contiguous carrier aggregation | Ericsson, ST- Ericsson | Noted |
| 2.5.1 | R4-100114 | Approval |  | TP for TS 37.141 clause 2,3 and 4. | Ericsson | Revised in 241 |
| 2.5.1 | R4-100115 | Approval |  | TP for TS 37.141 clause 5; Applicability of requirements | Ericsson | Noted |
| 2.5.2 | R4-100116 | Approval |  | TP for TS 37.141 clause 6.2; Base station output power | Ericsson | Noted |
| 2.5.2 | R4-100117 | Approval |  | TP for TS 37.141 clause 6.6.1; Transmitter spurious emissions | Ericsson | Noted |
| 2.5.2 | R4-100118 | Approval |  | TP for TS 37.141 clause 6.6.2; Operating band unwanted emissions | Ericsson | Noted |
| 2.5.2 | R4-100119 | Approval |  | TP for TS 37.141 clause 6.6.4; Adjacent Channel Leakage power Ratio (ACLR) | Ericsson | Noted |
| 2.5.2 | R4-100120 | Approval |  | TP for TS 37.141 clause 6.7; Transmitter intermodulation | Ericsson | Noted |
| 2.6 | R4-100121 | Discussion |  | DC-HSUPA related receiver requirements | Ericsson, ST-Ericsson | Noted |
| 1.4.3.1 | R4-100122 | Discussion | Rel-10 | Practical design considerations for LTE-Advanced power amplifiers | Motorola, Inc. | Noted |
| - | R4-100123 | Information |  | 2GHz S-band Overview | TerreStar & DBSD | Not Handled |
| 1.4.4 | R4-100124 | LS out |  | Draft Reply LS on MC Measurements | Qualcomm Incorporated | Noted |
| 1.4.4 | R4-100125 | Discussion |  | Discussion on MC Measurements | Qualcomm Incorporated | Noted |
| 1.2 | R4-100126 | Approval |  | Organization of Relay RAN4 Specs | Qualcomm Incorporated | Noted |
| 1.2 | R4-100127 | Approval |  | Text Proposal on Relay Requirements | Qualcomm Incorporated | Noted |
| 2.2.1 | R4-100128 | Approval |  | TP Correction to Resource Partitioning | Qualcomm Incorporated | Revised in 232 |
| 2.2.1 | R4-100129 | Discussion |  | Discussion on victim UE aware interference management | Qualcomm Incorporated | Noted |
| 2.9 | R4-100130 | Discussion |  | Impact of window size on positioning performance | Qualcomm Incorporated | Noted |
| 2.9 | R4-100131 | Discussion |  | Link level positioning simulation results | Qualcomm Incorporated | Noted |
| 2.3 | R4-100132 | Discussion |  | In-bound mobility simulation results | Qualcomm Incorporated | Noted |
| 2.3 | R4-100133 | Discussion |  | In-bound mobility minimum performance requirements | Qualcomm Incorporated | Noted |
| 1.3.1 | R4-100134 | Discussion |  | Coexistence between LTE-Advanced and LTE in DL: ITU-R Base Coverage Urban and Microcellular deployment scenarios | Qualcomm Incorporated | Noted |
| 1.3.1 | R4-100135 | Discussion |  | Coexistence between LTE-Advanced and LTE in DL: ITU-R Base Coverage Urban and Microcellular deployment scenarios | Qualcomm Incorporated | Noted |
| 2.7 | R4-100136 | Discussion |  | Simulation Framework for LTE Rel-9 Enhanced DL Transmission | Motorola | Noted |
| 1.3.1 | R4-100137 | Discussion |  | Carrier Spacing and Placement for Contiguous Carrier Aggregation | Huawei | Withdrawn |
| 1.3.1 | R4-100138 | Discussion |  | Spectrum Shaping for Multiple carrier OFDM | Huawei | Noted |
| 1.3.2 | R4-100139 | Approval |  | Further consideration on LTE-A coexistence study | Huawei | Noted |
| 1.4.1 | R4-100140 | Discussion |  | LTE-A carrier aggregation inter-modulation analysis in certain scenarios | Huawei | Noted |
| 1.4.2.3 | R4-100141 | Discussion |  | Initial work on UE sensitivity in LTE-A | Huawei | Noted |
| 1.4.2.3 | R4-100142 | Discussion |  | MIMO impact on MSD in LTE-A | Huawei | Noted |
| 1.4.3.3 | R4-100143 | Discussion |  | Consideration on LTE-A BS dynamic range | Huawei | Noted |
| 1.4.3.2 | R4-100144 | Approval |  | TP Unwanted emission requirement for LTE-A BS | Huawei | Noted |
| 1.4.3.2 | R4-100145 | Discussion |  | Impact of cross carrier frequency/time error | Huawei | Noted |
| 1.4.3.2 | R4-100146 | Discussion |  | Cross carrier interferences introduced by phase noise | Huawei | Noted |
| 1.4.3.3 | R4-100147 | Discussion |  | Reference sensitivity level for LTE-Advanced BS | Huawei | Noted |
| 1.4.4 | R4-100148 | Discussion |  | Considerations on mobility measurements for Carrier aggregation | Huawei | Noted |
| 1.4.4 | R4-100149 | LS out |  | Reply LS on mobility measurements for carrier aggregation | Huawei | Noted |
| 2.4 | R4-100150 | CR | Rel-9 | E-UTRA BS classification | Huawei | Technically endorsed |
| 2.4 | R4-100151 | CR | Rel-9 | Maximum output power for Pico NodeB | Huawei | Technically endorsed |
| 2.4 | R4-100152 | CR | Rel-9 | Frequency error requirement for Pico NodeB | Huawei | Technically endorsed |
| 2.4 | R4-100153 | CR | Rel-9 | Reference sensitivity level requirement for Pico NodeB | Huawei | Technically endorsed |
| 2.4 | R4-100154 | CR | Rel-9 | Blocking requirement for Pico NodeB | Huawei | Revised in 224 |
| 2.4 | R4-100155 | CR | Rel-9 | ACLR requirement for Pico NodeB | Huawei | Technically endorsed |
| 2.4 | R4-100156 | CR | Rel-9 | Operating band unwanted emissions requirement for Pico NodeB | Huawei | Technically endorsed |
| 2.7 | R4-100157 | Discussion |  | Consideration on dual-layer beamforming performance requirement | Huawei | Noted |
| 2.8 | R4-100158 | Discussion |  | Test reference value for LTE MBMS | Huawei | Noted |
| 2.8 | R4-100159 | Discussion |  | LTE MBMS simulation results for alignment (FDD) | Huawei | Revised in 223 |
| 2.8 | R4-100160 | Discussion |  | LTE MBMS simulation results for alignment (TDD) | Huawei | Noted |
| 2.8 | R4-100161 | Discussion |  | LTE MBMS simulation results with impairments | Huawei | Noted |
| 2.8 | R4-100162 | CR | Rel-9 | 36.101 CR: Editorial corrections on LTE MBMS reference measurement channels | Huawei | Technically endorsed |
| 2.8 | R4-100163 | Approval |  | Minutes from LTE MBMS demodulation ad hoc | Huawei | Withdrawn |
| 2.8 | R4-100164 | Discussion |  | Summary of PMCH alignment results | Huawei | Noted |
| 2.8 | R4-100165 | Discussion |  | Summary of PMCH simulation results with impairments | Huawei | Noted |
| 2.9 | R4-100166 | Discussion |  | On the framework of LTE positioning | Huawei | Noted |
| 2.9 | R4-100167 | Discussion |  | System-level simulation results for OTDOA positioning | Huawei | Noted |
| 2.9 | R4-100168 | Discussion |  | Link-level simulation results for RSTD requirement | Huawei | Noted |
| 2.9 | R4-100169 | Discussion |  | Simulation results for UE Rx_Tx time difference measurement | Huawei | Noted |
| 2.6 | R4-100170 | Discussion |  | Receiver RF requirements for DC-HSUPA | Qualcomm Incorporated | Noted |
| 2.6 | R4-100171 | Discussion |  | TX-RX frequency separation for DC-HSUPA | Qualcomm Incorporated | Noted |
| 2.6 | R4-100172 | Discussion |  | 25.133 TP E-TFC selection in UE for DC-HSUPA | Qualcomm Incorporated | Revised in 208 |
| 2.6 | R4-100173 | Discussion |  | Independent configuration of maximum UL Tx power in DC-HSUPA | Qualcomm Incorporated | Noted |
| 2.3 | R4-100174 | Discussion |  | Simulation assumptions for HNB inbound mobility | Qualcomm Incorporated | Revised in 209 |
| 2.2.1 | R4-100175 | CR | Rel-9 | Dynamic range requirement for Home eNodeB | CMCC, CATT | Revised in 200 |
| 2.2.3 | R4-100176 | Approval |  | LTE TDD Home eNodeB RF requirements TR36.922 v1.1.0 | CMCC | in principle agreed |
| 2.2.3 | R4-100177 | Approval |  | Text proposal on LTE TDD HeNB synchronization requirement | CMCC, NSN, | in principle agreed |
| 2.2.3 | R4-100178 | Approval |  | Text proposal on LTE TDD HeNB interference control | CMCC | in principle agreed |
| 2.7 | R4-100179 | Approval |  | Framework for DL-BF demodulation requirements | CMCC | Revised in 248 |
| 2.8 | R4-100180 | Discussion |  | Ideal simulation results for LTE MBMS | CMCC | Noted |
| 1.3.1 | R4-100181 | Approval |  | Prioritization of carrier aggregation scenarios | Qualcomm Incorporated | Noted |
| 2.2.3 | R4-100182 | Discussion |  | Conversion of UTC Time to Frame Start Timing | Qualcomm Incorporated | Noted |
| 1.3.1 | R4-100183 | Discussion |  | LTE-A coexistence simulation result for scenario #1 | LG Electronics | Noted |
| 1.3.1 | R4-100184 | Discussion |  | LTE-A deployment scenario for CA, Enhanced DL and UL antenna transmission | Motorola | Noted |
| 1.4.2.1 | R4-100185 | Discussion |  | LTE-A Tx Architecture | Motorola | Noted |
| 2.5.2 | R4-100186 | Discussion |  | Tx test configurations for MSR test specification | Huawei | Noted |
| 2.2.2 | R4-100187 | Discussion |  | Victim UE transmission detection at the HeNB | picoChip Designs | Revised in 195 |
| 1.4.1 | R4-100188 | Discussion |  | Simulation assumptions for LTE-A co-existence study | NTT DOCOMO | Noted |
| 1.4.2.1 | R4-100189 | Discussion |  | Analysis on LTE-A UE RF requirements | NTT DOCOMO | Noted |
| - | R4-100190 | Information |  | 3GPP: L-Band Overview | Skyterra | Revised in 196 |
| 2.2.1 | R4-100191 | CR | Rel-9 | Operating band unwanted emissions requirement for Home eNodeB | CMCC, CATT | Technically endorsed |
| 1.4.4 | R4-100192 | Discussion |  | Carrier aggregation deployment scenarios for RRM | NTT DOCOMO | Noted |
| 2.2.2 | R4-100193 | Discussion |  | Victim UE Aware Downlink Interference Management | picoChip Designs, Kyocera | Noted |
| 2.2.2 | R4-100194 | Approval |  | Text Proposal for TR36.921: Victim UE Aware Interference Management | picoChip Designs, Kyocera | Noted |
| 2.2.2 | R4-100195 | Discussion |  | Victim UE transmission detection at the HeNB | picoChip Designs, Kyocera | Noted |
| - | R4-100196 | Information |  | 3GPP: L-Band Overview | Skyterra | Revised in 210 |
| 2.2.1 | R4-100197 | Approval |  | Text proposal for TR 36.9xx: Reducing interference from CSG cells by dynamically changing their CSG IDs | Motorola | in principle agreed |
| 1.4.2.1 | R4-100198 | Discussion |  | LTE-A TDD UE Performance | Vodafone | Withdrawn |
| 2.5.2 | R4-100199 | Discussion |  | Operating Band Unwanted emission mask (UEM) for Band Category 2 | Vodafone | Noted |
| 2.2.1 | R4-100200 | CR | Rel-9 | Dynamic range requirement for Home eNodeB | CMCC, CATT | Technically endorsed |
| 1.3.1 | R4-100201 | Discussion |  | ACIR modelling for Uplink LTE-A co-existence simulation | Samsung | Withdrawn |
| 2.7 | R4-100202 | Discussion |  | Some considerations on dual-layer beamforming testing | NEC | Noted |
| 2.8 | R4-100203 | Discussion |  | Further considerations for eMBMS | NEC | Noted |
| 2.2.2 | R4-100204 | Approval |  | Text Proposal for TR 36.921: Interference control for LTE Rel-9 HeNB cells | Nokia Siemens Networks, Nokia | Revised in 235 |
| 2.2.3 | R4-100205 | Approval |  | Text Proposal for TR 36.922: Interference control for LTE Rel-9 HeNB cells | Nokia Siemens Networks, Nokia, Panasonic | Revised in 234 |
| 2.3 | R4-100206 | Discussion |  | Discussions on HeNB inbound mobility performance requirements | NTT DOCOMO | Noted |
| 1.4.1 | R4-100207 | Discussion |  | Release 10 UE PUCCH/PUSCH configuration | Motorola | Noted |
| 2.6 | R4-100208 | Discussion |  | 25.133 TP E-TFC selection in UE for DC-HSUPA | Qualcomm Incorporated | Noted |
| 2.3 | R4-100209 | Discussion |  | Simulation assumptions for HNB inbound mobility | Qualcomm Incorporated | Noted |
| - | R4-100210 | Information |  | 3GPP: L-Band Overview | Skyterra | Not Handled |
| 2.5 | R4-100211 | LS in |  | Reply to LS Response on support of non-contiguous frequency bands for MSR BS (GP-092415 Source: TSG GERAN WG1, To: TSG RAN WG4, Cc: TSG RAN,TSG GERAN) | TSG GERAN WG1 | Noted |
| 2.5 | R4-100212 | LS in |  | Reply LS to “LS on Status of the MSR Work Item” (GP-092416 Source: TSG GERAN WG1, To: TSG RAN,TSG RAN WG4, Cc: ETSI MSG,ETSI MSGTFES) | TSG GERAN WG1 | Noted |
| 2.5 | R4-100213 | LS in |  | LTE Base Station mask options (Liaison statement to 3GPP on LTE BS mask options Source: ECC SE PT 42, To: TSG RAN, Cc: TSG RAN4, ETSI MSG TFES) | ECC SE PT 42 | Noted |
| 2.3 | R4-100214 | LS in |  | LS on CSG mobility performance (R2-097463 Source: TSG RAN WG2, To: TSG RAN WG4, Cc: ) | TSG RAN WG2 | Noted |
| 1.3.1 | R4-100215 | LS in |  | Response LS on carrier aggregation (R2-097497 Source: TSG RAN WG2, To: TSG RAN WG1,TSG RAN WG4, Cc: ) | TSG RAN WG2 | Noted |
| 2.6 | R4-100216 | LS in |  | LS on MAC agreements for DC-HSUPA (R2-097539 Source: TSG RAN WG2, To: TSG RAN WG4, Cc: TSG RAN WG1) | TSG RAN WG2 | Noted |
| 2.3.3 | R4-100217 | LS in |  | LS on providing backhaul signalling in support of time and frequency synchronization using network listening (RP-091447 Source: TSG RAN, To: TSG RAN WG3,TSG RAN WG4, Cc: TSG RAN WG2) | TSG RAN | Noted |
| 2.3.3 | R4-100218 | LS in |  | e:Response LS on the support for time and frequency synchronisation for TDD HeNB (S5-094183 Source: TSG SA WG5, To: TSG RAN WG4, Cc: None) | TSG SA WG5 | Noted |
| 2.5 | R4-100219 | LS in |  | LS on European Harmonised Standard for MSR Base Stations (TFES-09-121r1 Source: ETSI MSGTFES, To: TSG RAN WG4,TSG GERAN WG1, Cc: TSG RAN,ETSI ERM) | ETSI MSGTFES | Withdrawn |
| 1.3.1 | R4-100220 | Approval |  | LTE-A deployment scenarios | NTT DOCOMO, Deutche Telekom, TeliaSonera, US Cellu | in principle agreed |
| 2.9 | R4-100221 | Discussion |  | Considerations for Link-level Evaluations for RSTD Accuracy | Motorola | Noted |
| 2.9 | R4-100222 | Discussion |  | Link-level Simulation Results for RSTD Accuracy | Motorola | Withdrawn |
| 2.8 | R4-100223 | Discussion |  | LTE MBMS simulation results for alignment (FDD) | Huawei | Noted |
| 2.4 | R4-100224 | CR | Rel-9 | Blocking requirement for Pico NodeB | Huawei | Revised in 240 |
| 2.4 | R4-100225 | CR | Rel-9 | Editorial correction in TS36.104 for Pico NodeB | Huawei | Revised in 237 |
| 2.6 | R4-100226 | Approval |  | ETFC Restriction for DC-HSUPA | Nokia, Nokia Siemens Networks, Interdigital, Huawei | Noted |
| 2.2.1 | R4-100227 | Discussion |  | Handling of missed HeNB performance requirements | Samsung | Noted |
| 2.2.1 | R4-100228 | CR | Rel9 | Corrections on HeNB performance requirements | Samsung | Noted |
| 2.2.1 | R4-100229 | CR | Rel9 | Corrections on HeNB performance requirements | Samsung | Noted |
| 2.9 | R4-100230 | Approval |  | Remaining issues on assistance data for OTDOA positioning maximum range for estimated timing difference | Ericsson, ST-Ericsson | Noted |
| 2.9 | R4-100231 | LS out |  | Draft LS response on assistance information for OTDOA positioning support for LTE remaining issues | Ericsson, ST-Ericsson | Revised in 252 |
| 2.2.2 | R4-100232 | Approval |  | TP Correction to Resource Partitioning | Qualcomm Incorporated | in principle agreed |
| 2.3 | R4-100233 | Discussion |  | HeNB inbound mobility simulation results | Samsung | Noted |
| 2.2.3 | R4-100234 | Approval |  | Text Proposal for TR 36.922: Interference control for LTE Rel-9 HeNB cells | Nokia Siemens Networks, Nokia, Panasonic | in principle agreed |
| 2.2.2 | R4-100235 | Approval |  | Text Proposal for TR 36.921: Interference control for LTE Rel-9 HeNB cells | Nokia Siemens Networks, Nokia | in principle agreed |
| 2.4 | R4-100236 | CR | Rel-9 | Editorial correction in TS36.104 for Pico NodeB | Huawei | Withdrawn |
| 2.4 | R4-100237 | CR | Rel-9 | Editorial correction in TS36.104 for Pico NodeB | Huawei | Technically endorsed |
| 2.4 | R4-100238 | CR | Rel-9 | Corrections of operating band unwanted emissions for Local Area BS | CATT | Technically endorsed |
| 2.4 | R4-100239 | CR | Rel-9 | Spurious emissions requirement for Local Area BS | CATT | Technically endorsed |
| 2.4 | R4-100240 | CR | Rel-9 | Blocking requirement for Pico NodeB | Huawei | Technically endorsed |
| 2.5.1 | R4-100241 | Approval |  | TP for TS 37.141 clause 2,3 and 4. | Ericsson | in principle agreed |
| 2.5.2 | R4-100242 | CR | Rel-9 | Correction of additional spurious emission requirement for BC2 | Nokia Siemens Networks | Technically endorsed |
| 2.6 | R4-100243 | CR | Rel-9 | CR on Introduction of DC-HSUPA related receiver requirements | ST Ericsson | Noted |
| 2.3 | R4-100244 | Approval |  | Way forward on HeNB inbound mobility requirements | NTT DOCOMO, Samsung | in principle agreed |
| 2.9 | R4-100245 | Approval |  | Text proposal on A-GNSS performance requirements for LTE | Alcatel-Lucent, Qualcomm Europe, Spirent Communica | in principle agreed |
| 2.9 | R4-100246 | Approval |  | Text proposal for Annex B of TS 36.171 | Alcatel-Lucent, Qualcomm Europe, Spirent Communica | in principle agreed |
| 1.3.1 | R4-100247 | LS out |  | Draft reply LS on mobility measurements for carrier aggregation | Nokia | in principle agreed |
| 2.7 | R4-100248 | Approval |  | Framework for DL-BF demodulation requirements | CMCC | Email approval |
| 2.6 | R4-100249 | Information |  | Text Proposal of Rx core requirements for DC-HSUPA | Qualcomm Incorporated | Noted |
| 2.2.1 | R4-100250 | Approval |  | Simulation assumptions for additional performance requirements of E-UTRA LA and Home BS class | NTT DOCOMO, Nokia Siemens Networks, Alcatel-Lucent | in principle agreed |
| 2.9 | R4-100251 | LS out |  | Draft LS on Report Mapping of UE Measurements for Positioning | Ericsson, ST-Ericsson | Email approval |
| 2.9 | R4-100252 | LS out |  | Draft LS response on assistance information for OTDOA positioning support for LTE remaining issues | Ericsson, ST-Ericsson | Email approval |

Annex B:	List of Endorsed Change Requests

| Agenda | Tdoc | Release | 'Title' | Source | Spec | CR | R | Cat |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 2.2.1 | R4-100054 | Rel-9 | Corrections of operating band unwanted emissions for Home BS | CATT | 36.104 | 144 |  | F |
| 2.4 | R4-100057 | Rel-9 | Dynamic range requirement for Local Area BS | CATT | 36.141 | 148 |  | B |
| 2.4 | R4-100058 | Rel-9 | In-channel selectivity for Local Area BS | CATT | 36.141 | 149 |  | B |
| 2.4 | R4-100059 | Rel-9 | ACS and narrow band blocking for Local Area BS | CATT | 36.141 | 150 |  | B |
| 2.4 | R4-100060 | Rel-9 | Receiver intermodulation for Local Area BS | CATT | 36.141 | 151 |  | B |
| 2.4 | R4-100061 | Rel-9 | Performance requirement for Local Area BS | CATT | 36.141 | 152 |  | B |
| 2.9 | R4-100067 | Rel-9 | AOA and TA measurement report mappings | CATT, Ericsson, ST-Ericsson | 36.133 | 393 |  | B |
| 2.4 | R4-100150 | Rel-9 | E-UTRA BS classification | Huawei | 36.141 | 153 |  | B |
| 2.4 | R4-100151 | Rel-9 | Maximum output power for Pico NodeB | Huawei | 36.141 | 154 |  | B |
| 2.4 | R4-100152 | Rel-9 | Frequency error requirement for Pico NodeB | Huawei | 36.141 | 155 |  | B |
| 2.4 | R4-100153 | Rel-9 | Reference sensitivity level requirement for Pico NodeB | Huawei | 36.141 | 156 |  | B |
| 2.4 | R4-100155 | Rel-9 | ACLR requirement for Pico NodeB | Huawei | 36.141 | 158 |  | B |
| 2.4 | R4-100156 | Rel-9 | Operating band unwanted emissions requirement for Pico NodeB | Huawei | 36.141 | 159 |  | B |
| 2.8 | R4-100162 | Rel-9 | 36.101 CR: Editorial corrections on LTE MBMS reference measurement channels | Huawei | 36.101 | 445 |  | F |
| 2.2.1 | R4-100191 | Rel-9 | Operating band unwanted emissions requirement for Home eNodeB | CMCC, CATT | 36.141 | 161 |  | F |
| 2.2.1 | R4-100200 | Rel-9 | Dynamic range requirement for Home eNodeB | CMCC, CATT | 36.141 | 160r1 | 1 | F |
| 2.4 | R4-100237 | Rel-9 | Editorial correction in TS36.104 for Pico NodeB | Huawei | 36.104 | 146r1 | 1 | F |
| 2.4 | R4-100238 | Rel-9 | Corrections of operating band unwanted emissions for Local Area BS | CATT | 36.104 | 145r1 | 1 | F |
| 2.4 | R4-100239 | Rel-9 | Spurious emissions requirement for Local Area BS | CATT | 36.141 | 147r1 | 1 | B |
| 2.4 | R4-100240 | Rel-9 | Blocking requirement for Pico NodeB | Huawei | 36.141 | 157r2 | 2 | B |
| 2.5.2 | R4-100242 | Rel-9 | Correction of additional spurious emission requirement for BC2 | Nokia Siemens Networks | 37.104 | 1 |  | F |

Annex C:	List of documents discussed via reflector

| Agenda | Tdoc | Type | 'Title' | Source | 'Decision' |
| --- | --- | --- | --- | --- | --- |
| 2.7 | R4-100248 | Approval | Framework for DL-BF demodulation requirements | CMCC | Email approval |
| 2.9 | R4-100251 | LS out | Draft LS on Report Mapping of UE Measurements for Positioning | Ericsson, ST-Ericsson | Email approval |
| 2.9 | R4-100252 | LS out | Draft LS response on assistance information for OTDOA positioning support for LTE remaining issues | Ericsson, ST-Ericsson | Email approval |

# Annex D:	List of non treated documents

| Agenda | Tdoc | Type | 'Title' | Source |
| --- | --- | --- | --- | --- |
| 2 | R4-100087 | Information | Reference sensitivity and MSD | Ericsson, ST-Ericsson |
| - | R4-100123 | Information | 2GHz S-band Overview | TerreStar & DBSD |
| - | R4-100210 | Information | 3GPP: L-Band Overview | Skyterra |

# Annex E:	List of agreed outgoing Liaison Statements

# Annex F:	List of ingoing Liaison Statements

| Agenda | Tdoc | 'Title' | Source | 'Decision' |
| --- | --- | --- | --- | --- |
| 2.5 | R4-100033 | LS on European Harmonised Standard for MSR Base Stations (TFES-09-121r1 Source: ETSI MSGTFES, To: TSG RAN WG4,TSG GERAN WG1, Cc: TSG RAN,ETSI ERM) | ETSI MSGTFES | Noted |
| 2.5 | R4-100211 | Reply to LS Response on support of non-contiguous frequency bands for MSR BS (GP-092415 Source: TSG GERAN WG1, To: TSG RAN WG4, Cc: TSG RAN,TSG GERAN) | TSG GERAN WG1 | Noted |
| 2.5 | R4-100212 | Reply LS to “LS on Status of the MSR Work Item” (GP-092416 Source: TSG GERAN WG1, To: TSG RAN,TSG RAN WG4, Cc: ETSI MSG,ETSI MSGTFES) | TSG GERAN WG1 | Noted |
| 2.5 | R4-100213 | LTE Base Station mask options (Liaison statement to 3GPP on LTE BS mask options Source: ECC SE PT 42, To: TSG RAN, Cc: TSG RAN4, ETSI MSG TFES) | ECC SE PT 42 | Noted |
| 2.3 | R4-100214 | LS on CSG mobility performance (R2-097463 Source: TSG RAN WG2, To: TSG RAN WG4, Cc: ) | TSG RAN WG2 | Noted |
| 1.3.1 | R4-100215 | Response LS on carrier aggregation (R2-097497 Source: TSG RAN WG2, To: TSG RAN WG1,TSG RAN WG4, Cc: ) | TSG RAN WG2 | Noted |
| 2.6 | R4-100216 | LS on MAC agreements for DC-HSUPA (R2-097539 Source: TSG RAN WG2, To: TSG RAN WG4, Cc: TSG RAN WG1) | TSG RAN WG2 | Noted |
| 2.3.3 | R4-100217 | LS on providing backhaul signalling in support of time and frequency synchronization using network listening (RP-091447 Source: TSG RAN, To: TSG RAN WG3,TSG RAN WG4, Cc: TSG RAN WG2) | TSG RAN | Noted |
| 2.3.3 | R4-100218 | e:Response LS on the support for time and frequency synchronisation for TDD HeNB (S5-094183 Source: TSG SA WG5, To: TSG RAN WG4, Cc: None) | TSG SA WG5 | Noted |

# Annex G:	Registered Attendees