## Slide 1
3GPP TSG-RAN WG4 Meeting #73 UE RF AH
Oulu, Finland, 13 – 16 Jan, 2015
Agenda item: 4.1.2, 4.2.2
Source: KDDI
Document for: Approval
Title: Proposals on Class A2 framework
R4-73AH-0031

## Slide 2: Summary
KDDI would like to propose framework for Class A2 combination in this contribution.
One of our key proposals here is that:
  Discussion whether to include HTF* or not should be concluded within 6 months. (* Harmonic Trap Filter)
Motivation why we propose above will be explained later.
R4-73AH-0031

## Slide 3: Background
Framework for following classes have been developed so far;
  Class A1: DTIB/DRIB = 0.3/0 dB, respectively.
  Class A2: NONE.
  Class A3: DTIB/DRIB = 0.5/0 dB, respectively
  Class A4: NONE.
  Class A5: DTIB/DRIB = 0.3 (0.5)/0 dB, respectively.
Lack of framework for Class A2 leads one of reasons for huge RAN4 workload.
R4-73AH-0031

## Slide 4: Review of CA_1A-28A work
One of typical Class A2 combinations is CA_1A-28A.
When we take a look back of this WI, one can understand that RAN4 had done HTF discussion for one year (= six RAN4 meetings)!
Calendar Year | 2013 4Q | 2014 1Q | 2014 2Q | 2014 3Q | 2014 4Q | 2015 1Q
CA_1A-28A |  |  |  |  |  | 
RAN4 Meeting |  |  |  |  |  | 
★
R4#70
★
R4#72
★ ★
bis R4#73
How long have we discussed?
 One Year = Six RAN4 meetings!
★ ★
bis R4#71
★ ★
AH R4#74
Figure 1: How long have we discussed CA_1A-28A
R4-73AH-0031

## Slide 5: Detail Review of CA_1A-28A work
R4#70: HTF inclusion proposed but NOT agreed.
R4#70-bis: Proposal w/o HTF was made. HTF inclusion between DUP and PA were also proposed.
R4#71: HTF inclusion discussed. Another big impact was B28 utilization in EU.
R4#72: HTF inclusion discussed. Tighter values for DTIB/DRIB (=0.3/0.2 dB) were agreed.
R4#72-bis: HTF inclusion still discussed.
R4#73: HTF inclusion still discussed and agreed.
R4-73AH-0031

## Slide 6: Outcome of CA_1A-28A discussion
It would be agreeable that DTIB/DRIB of HTF should be 0.3/0.2 dB, respectively.
It is also agreeable that HTF insertion between DUP and PA should be avoided.
Some operators consider multiple type of UE implementations should be allowed in RAN4 specifications but some operators NOT. And most of vendors don’t prefer multiple type of UE implementation.
Unclear future never provides conclusion. The safest approach was chosen after all despite of long discussion.
 Same discussion might be repeated in the future!
R4-73AH-0031

## Slide 7: Proposals/Conclusions
Proposal 1: If HTF inclusion is agreed, values for DTIB/DRIB shall be 0.3/0.2 dB, respectively.
Proposal 2: If HTF inclusion is agreed, it shall be after DUP (NOT between DUP and PA).
Proposal 3: Discussion on HTF inclusion should be for a maximum of six month (three RAN4 meetings). When no consensus, the safest approach shall be taken (= inclusion of HTF shall be agreed).
Proposal 4: Even if six months is hard to agree, deadline should be set from the beginning of RAN4 work. No longer than one 3GPP release. This can satisfy operator demands for commercial service.
R4-73AH-0031

## Slide 8: Complements
If deadline is not set, operators/vendors who would like to launch commercial service/devices might suffer. Off course, commercial perspective is not the most important aspect but it should pay attention to (otherwise political war might happen which everyone would like to avoid).
R4-73AH-0031