## Slide 1: WF on BS output power accuracy value for NR
NTT DOCOMO, INC.
3GPP TSG-RAN WG4 NR AH Meeting
Spokane, Washington, USA, 17 - 19 January, 2017
R4-1700265
Agenda item: 3.6.3
Document for: Approval

## Slide 2: Introduction
In RAN4#81 meeting, it was agreed as follows:
  OTA BS output power accuracy requirement is specified as EIRP in the last meeting [1].
  general concept (vender declares the range of directions to meet EIRP accuracy requirement) can be reused AAS one.
It is needed to discuss how to decide output power accuracy value for NR BS
[1] R4-1610923, “Way forward on BS RF requirements for NR”, Nokia, RAN4#81, November 2016

## Slide 3: Way forward
Regarding below 6GHz,
  If conducted requirement is specified:
    Accuracy value should be 2.0dB (same as non-AAS)
  If OTA requirement is specified:
    Accuracy value should be 2.2dB (same as AAS)
Regarding above 6GHz,
  If conducted requirement is specified:
    RAN4 needs to discuss how to decide the accuracy value. Interested companies encourage to present the method to decide the value in RAN4#82 meeting.
  If OTA requirement is specified:
    RAN4 needs to discuss how to decide the accuracy value. Interested companies encourage to present whether the same EIRP accuracy equation with AAS (shown in the next slide) can be reused or not in RAN4#82 meeting. If not, accuracy modeling method would be also provided.
Note that it is open issue whether conducted only, OTA only or both conducted/OTA for below 6GHz and above 6GHz. This issue will be discussed separately with accuracy value issue.

## Slide 4: Information(AAS EIRP accuracy equation)