3GPP TSG-RAN WG 5 Meeting #61	(R5-134452

# San Francisco, U.S.A. 11th – 15th Nov 2013

| CR-Form-v10 |
| --- |
| CHANGE REQUEST |
| ( | 36.521-1 | CR | CRNum | ( rev | - | ( Current version: | 11.2.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Update applicability table for LTE B14 public safety high power UE test cases |
| --- | --- |
| Source to WG: ( | Motorola Solutions |
| Source to TSG: ( | R5 |
| Work item code: ( | LTE_B14_PSBB_HPUE-UEConTest |  | Date: ( | 2013-09-20 |
| Category: ( | F |  | Release: ( | Rel-11 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) |
| Reason for change: ( | The Applicability of B14 HPUE test cases are currently for UE of Rel-11 and forward , The HPUE can be tested in a earlier release as long as the RF tests cases specified iin Rel-11 are used for any additional HPUE RF test cases. Note there is not impact on other test specifications as the HPUE changes are limited to the RF domain and do not impact other specifications |
| Summary of change: ( | Added note on those HPUE test cases that they can be executed for an earlier release UE |
| Consequences if ( not approved: | There is need to deploy the feature in the market now particular as a HPUE will be needed for intial or start of deployement and this would allow testing for a earlier release |
| Clauses affected: ( | 4.1 |
|  | Y | N |  |  |
| Other specs ( |  | x | Other core specifications ( | TS/TR ... CR ... |
| affected: |  | x | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | x | O&M Specifications | TS/TR ... CR ... |
| Other comments: ( |  |

<Start of modified section>

## 4.1	RF conformance test cases

Table 4.1-1: Applicability of RF conformance test cases, ref. TS 36.521-1 [1]

| Clause | Title | Release | Applicability | Additional Information |
| --- | --- | --- | --- | --- |
|  |  |  | Condition | Comments |  |
| Transmitter Characteristics |
| 6.2.2 | UE Maximum Output Power | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.2.2_1 | UE Maximum Output Power for HPUE | Rel-11 | C39 | UE supporting E-UTRA Power Class 1 This TC can be executed with a Rel-8 UE | FDD |
|  |  |  |  |  | TDD |
| 6.2.2A.1 | UE Maximum Output Power for CA (intra-band contiguous DL CA and UL CA) | Rel-10 | C19 | UE supporting E-UTRA and intra-band contiguous DL CA and UL CA | FDD |
|  |  |  |  |  | TDD |
| 6.2.2B | UE Maximum Output Power for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.2.3 | Maximum Power Reduction (MPR) | Rel-8 | N/A | UE supporting E-UTRA, The minimum requirement tested in 6.2.3 is covered by test case 6.6.2.3. | FDD |
|  |  |  |  |  | TDD |
| 6.2.3_1 | Maximum Power Reduction (MPR) for HPUE | Rel-11 | N/A | UE supporting E-UTRA Power Class 1 .The minimum requirement tested in 6.2.3_1 is covered by test case 6.6.2.3_1. This TC can be executed with a Rel-8 UE | FDD |
|  |  |  |  |  | TDD |
| 6.2.3A.1 | Maximum Power Reduction (MPR) for CA (intra-band contiguous DL CA and UL CA) | Rel-10 | N/A | UE supporting E-UTRA and intra-band contiguous DL CA and UL CA. The minimum requirement tested in 6.2.3A.1 is covered by test case 6.6.2.3A.1 | FDD |
|  |  |  |  |  | TDD |
| 6.2.3B | Maximum Power Reduction (MPR) for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.2.4 | Additional Maximum Power Reduction (A-MPR) | Rel-8 | N/A | UE supporting E-UTRA. The minimum requirement tested in 6.2.4 is covered by test case 6.6.2.2 or 6.6.3.3 according to the supported NS value. | FDD |
|  |  |  |  |  | TDD |
| 6.2.4_1 | Additional Maximum Power Reduction (A-MPR) for HPUE | Rel-11 | N/A | UE supporting E-UTRA Power Class 1.The minimum requirement tested in 6.2.4_1 is covered by test case 6.6.2.2 or 6.6.3.3 according to the supported NS value. This TC can be executed with a Rel-8 UE | FDD |
|  |  |  |  |  | TDD |
| 6.2.4A.1 | Additional Maximum Power Reduction (A-MPR) for CA (intra-band contiguous DL CA and UL CA) | Rel-10 | N/A | UE supporting E-UTRA and intra-band contiguous DL CA and UL CA. The minimum requirement tested in 6.2.4A.1 is covered by test case 6.6.2.2A.1 or 6.6.3.3A.1 according to the supported NS value. | FDD |
|  |  |  |  |  | TDD |
| 6.2.4B | Additional Maximum Power Reduction (A-MPR) for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.2.5 | Configured UE transmitted Output Power | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.2.5_1 | Configured UE transmitted Output Power for HPUE | Rel-11 | C39 | UE supporting E-UTRA Power Class 1 This TC can be executed with a Rel-8 UE | FDD |
|  |  |  |  |  | TDD |
| 6.2.5A.1 | Configured UE transmitted Output Power for CA (intra-band contiguous DL CA and UL CA) | Rel-10 | C19 | UE supporting E-UTRA and intra-band contiguous DL CA and UL CA | FDD |
|  |  |  |  |  | TDD |
| 6.2.5A.2 | Configured UE transmitted Output Power for CA (inter-band DL CA without UL CA) | Rel-10 | C21 | UE supporting E-UTRA and inter-band DL CA but no UL CA | FDD |
|  |  |  |  |  | TDD |
| 6.2.5B | Configured transmitted power for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.3.1 | Void |  |  |  |  |
| 6.3.2 | Minimum Output Power | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.3.2A.1 | Minimum Output Power for CA (intra-band contiguous DL CA and UL CA) | Rel-10 | C19 | UE supporting E-UTRA and intra-band contiguous DL CA and UL CA | FDD |
|  |  |  |  |  | TDD |
| 6.3.2B | Minimum Output Power for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.3.3 | Transmit OFF Power | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.3.3A.1 | Transmit OFF Power for CA (intra-band contiguous DL CA and UL CA) | Rel-10 | C19 | UE supporting E-UTRA and intra-band contiguous DL CA and UL CA | FDD |
|  |  |  |  |  | TDD |
| 6.3.3B | UE Transmit OFF power for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.3.4.1 | General ON/OFF time mask | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.3.4.2.1 | PRACH time mask | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.3.4.2.2 | SRS time mask | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.3.4A.1.1 | General ON/OFF time mask for CA (intra-band contiguous DL CA and UL CA) | Rel-10 | C19 | UE supporting E-UTRA and intra-band contiguous DL CA and UL CA | FDD |
|  |  |  |  |  | TDD |
| 6.3.4B | ON/OFF time mask for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.3.5.1 | Power Control Absolute Power Tolerance | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.3.5.2 | Power Control Relative Power Tolerance | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.3.5.3 | Aggregate Power Control Tolerance | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.3.5A.1.1 | Power Control Absolute Power Tolerance for CA (intra-band contiguous DL CA and UL CA) | Rel-10 | C19 | UE supporting E-UTRA and intra-band contiguous DL CA and UL CA | FDD |
|  |  |  |  |  | TDD |
| 6.3.5A.2.1 | Power Control Relative Power Tolerance for CA (intra-band contiguous DL CA and UL CA) | Rel-10 | C19 | UE supporting E-UTRA and intra-band contiguous DL CA and UL CA | FDD |
|  |  |  |  |  | TDD |
| 6.3.5A.3.1 | Aggregate Power Control Tolerance for CA (intra-band contiguous DL CA and UL CA) | Rel-10 | C19 | UE supporting E-UTRA and intra-band contiguous DL CA and UL CA | FDD |
|  |  |  |  |  | TDD |
| 6.3.5B.1 | Power Control Absolute power tolerance for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.3.5B.2 | Power Control Relative power tolerance for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.3.5B.3 | Aggregate power control tolerance for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.5.1 | Frequency Error | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.5.1A.1 | Frequency Error for CA (intra-band contiguous DL CA and UL CA) | Rel-10 | C19 | UE supporting E-UTRA and intra-band contiguous DL CA and UL CA | FDD |
|  |  |  |  |  | TDD |
| 6.5.1B | Frequency Error for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.5.2.1 | Error Vector Magnitude (EVM) | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.5.2.1A | PUSCH-EVM with exclusion period | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.5.2.2 | Carrier leakage | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.5.2.3 | In-band emissions for non allocated RB | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.5.2.4 | EVM equalizer spectrum flatness | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.5.2A.1.1 | Error Vector Magnitude (EVM) for CA (intra-band contiguous DL CA and UL CA) | Rel-10 | C19 | UE supporting E-UTRA and intra-band contiguous DL CA and UL CA | FDD |
|  |  |  |  |  | TDD |
| 6.5.2A.2.1 | Carrier leakage for CA (intra-band contiguous DL CA and UL CA) | Rel-10 | C19 | UE supporting E-UTRA and intra-band contiguous DL CA and UL CA | FDD |
|  |  |  |  |  | TDD |
| 6.5.2A.3.1 | In-band emissions for non allocated RB for CA (intra-band contiguous DL CA and UL CA) | Rel-10 | C19 | UE supporting E-UTRA and intra-band contiguous DL CA and UL CA | FDD |
|  |  |  |  |  | TDD |
| 6.5.2B.1 | Error Vector Magnitude for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.5.2B.2 | Carrier leakage for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.5.2B.3 | In-band emissions for non allocated RB for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.5.2B.4 | EVM equalizer spectrum flatness for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.6.1 | Occupied bandwidth | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.6.1A.1 | Occupied bandwidth for CA (intra-band contiguous DL CA and UL CA) | Rel-10 | C19 | UE supporting E-UTRA and intra-band contiguous DL CA and UL CA | FDD |
|  |  |  |  |  | TDD |
| 6.6.1B | Occupied bandwidth for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.6.2.1 | Spectrum Emission Mask | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.6.2.1A.1 | Spectrum Emission Mask for CA (intra-band contiguous DL CA and UL CA) | Rel-10 | C19 | UE supporting E-UTRA and intra-band contiguous DL CA and UL CA | FDD |
|  |  |  |  |  | TDD |
| 6.6.2.1B | Spectrum Emission Mask for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.6.2.2 | Additional Spectrum Emission Mask | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.6.2.2B | Additional Spectrum Emission Mask for UL-MIMO | Rel-10 | C07 | UE supporting E-UTRA and UL_MIMO | FDD |
|  |  |  |  |  | TDD |
| 6.6.2.3 | Adjacent Channel Leakage power Ratio | Rel-8 | R | UE supporting E-UTRA | FDD |
|  |  |  |  |  | TDD |
| 6.6.2.3_1 | Adjacent Channel Leakage power Ratio for HPUE | Rel-11 | C39 | UE supporting E-UTRA Power Class 1 This TC can be executed with a Rel-8 UE | FDD |
|  |  |  |  |  | TDD |

<End of modified section>

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark appropriate boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Office® 2003 applications. Prefered format is ISO standard yyyy-MM-dd.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected and the CRs which are linked. This is particularly important where the affected specs belong to a different working group than that which will agree the present CR.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.