3GPP TSG-RAN WG 5 Meeting #61	(R5-134451

# San Francisco, U.S.A. 11th – 15th Nov 2013

| CR-Form-v10 |
| --- |
| CHANGE REQUEST |
| ( | 36.521-1 | CR | CRNum | ( rev | - | ( Current version: | 11.2.0 | ( |
| For HELP on using this form look at the pop-up text over the ( symbols. Comprehensive instructions on how to use this form can be found at http://www.3gpp.org/Change-Requests. |

| Proposed change affects: ( | UICC apps( |  | ME |  | Radio Access Network |  | Core Network |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |

| Title: ( | Modify Applicability for LTE B14 public safety high power UE test cases |
| --- | --- |
| Source to WG: ( | Motorola Solutions |
| Source to TSG: ( | R5 |
| Work item code: ( | LTE_B14_PSBB_HPUE-UEConTest |  | Date: ( | 2013-09-20 |
| Category: ( | F |  | Release: ( | Rel-11 |
|  | Use one of the following categories: F (correction) A (mirror corresponding to a change in an earlier release) B (addition of feature), C (functional modification of feature) D (editorial modification) Detailed explanations of the above categories can be found in 3GPP TR 21.900. | Use one of the following releases: Rel-4 (Release 4) Rel-5 (Release 5) Rel-6 (Release 6) Rel-7 (Release 7) Rel-8 (Release 8) Rel-9 (Release 9) Rel-10 (Release 10) Rel-11 (Release 11) Rel-12 (Release 12) |
| Reason for change: ( | The Applicability of B14 HPUE test cases are currently for UE of Rel-11 and forward , The HPUE can be tested in a earlier release as long as the RF tests cases specified iin Rel-11 are used for any additional HPUE RF test cases. Note there is not impact on other test specifications as the HPUE changes are limited to the RF domain and do not impact other specifications |
| Summary of change: ( | Added note on those HPUE test cases that they can be executed for an earlier release UE |
| Consequences if ( not approved: | There is need to deploy the feature in the market now particular as a HPUE will be needed for intial or start of deployement and this would allow testing for a earlier release |
| Clauses affected: ( | 6.2.2_1,6.2.3_1,6.2.4_1,6.2.5_1,6.3.5_1,6.6.2.3_1 |
|  | Y | N |  |  |
| Other specs ( |  | x | Other core specifications ( | TS/TR ... CR ... |
| affected: |  | x | Test specifications | TS/TR ... CR ... |
| (show related CRs) |  | x | O&M Specifications | TS/TR ... CR ... |
| Other comments: ( |  |

<Start of modified section>

### 6.2.2_1	Maximum Output Power for HPUE

#### 6.2.2_1.2	Test applicability

This test applies to all types of E-UTRA UE Power Class 1 release 11 and forward. This test can be executed with a release 8/9/10 Power Class 1 UE.

<End of modified section>

<Start of modified section>

### 6.2.3_1	Maximum Power Reduction (MPR) for HPUE

#### 6.2.3_1.2	Test applicability

The requirements of this test apply in test cases 6.6.2.3_1 Adjacent Channel Leakage power Ratio for HPUE to all types of E-UTRA Power Class 1 UE release 11 and forward. This test can be executed with a release 8/9/10 Power Class 1 UE.

<End of modified section>

<Start of modified section>

### 6.2.4_1	Additional Maximum Power Reduction (A-MPR) for HPUE

#### 6.2.4_1.2	Test applicability

The requirements of this test apply in test case 6.6.2.2 Additional Spectrum Emission Mask for network signalled values NS_06, to all types of E-UTRA Power Class 1 UE release 11 and forward. This test can be executed with a release 8/9/10 Power Class 1 UE.

<End of modified section>

<Start of modified section>

### 6.2.5_1	Configured UE transmitted Output Power for HPUE

#### 6.2.5_1.2	Test applicability

This test applies to all types of E-UTRA power Class 1 UE release 11 and forward. This test can be executed with a release 8/9/10 Power Class 1 UE.

<End of modified section>

<Start of modified section>

#### 6.3.5_1.1	Power Control Absolute power tolerance for HPUE

##### 6.3.5_1.1.2	Test applicability

This test applies to all types of E-UTRA Power Class 1 UE release 11 and forward. This test can be executed with a release 8/9/10 Power Class 1 UE.

<End of modified section>

<Start of modified section>

#### 6.3.5_1.2	Power Control Relative power tolerance for HPUE

##### 6.3.5_1.2.2	Test applicability

This test applies to all types of E-UTRA Power Class 1 UE release 11 and forward. This test can be executed with a release 8/9/10 Power Class 1 UE.

<End of modified section>

<Start of modified section>

#### 6.3.5_1.3	Aggregate power control tolerance for HPUE

##### 6.3.5_1.3.2	Test applicability

This test applies to all types of E-UTRA Power Class 1 UE release 11 and forward. This test can be executed with a release 8/9/10 Power Class 1 UE.

<End of modified section>

<Start of modified section>

#### 6.6.2.3_1	Adjacent Channel Leakage power Ratio for HPUE

##### 6.6.2.3_1.2	Test applicability

This test case applies to all types of E-UTRA Power Class 1 UE release 11 and forward. This test can be executed with a release 8/9/10 Power Class 1 UE.

<End of modified section>

<Start of modified section>

# Comments

Document numbers are allocated by the Working Group Secretary.   Use the format of document number specified by the 3GPP Working Procedures.

Enter the specification number in this box. For example, 04.08 or 31.102. Do not prefix the number with anything . i.e. do not use "TS", "GSM" or "3GPP" etc.

Enter the CR number here. This number is allocated by the 3GPP support team.  It consists of at least four digits, padded with leading zeros if necessary.

Enter the revision number of the CR here. If it is the first version, use a "-".

Enter the version of the specification here. This number is the version of the specification to which the CR was written and (normally) to which it will be applied if it is approved. Make sure that the latest version of the specification (of the relevant release) is used when creating the CR. If unsure what the latest version is, go to  http://www.3gpp.org/specs/specs.htm.

For help on how to fill out a field, place the mouse pointer over the special symbol closest to the field in question.

Mark appropriate boxes with an X.

SIM / USIM / ISIM applications.

Enter a concise description of the subject matter of the CR. It should be no longer than one line, but if this is not possible, do not enter hard new-line characters.  Do not use redundant information such as "Change Request number xxx to 3GPP TS xx.xxx".

One or more organizations (3GPP Individual Members) which drafted the CR and are presenting it to the Working Group.

For CRs agreed at Working Group level, the identity of the WG.  Use the format "xn" where 
	x = "C" for TSG CT, "R" for TSG RAN, "S" for TSG SA, "G" for TSG GERAN; 
	n = digit identifying the Working Group; for CRs drafted during the TSG meeting itself, use "P". 
Examples: "C4", "R5", "G3new", "SP".

Enter the acronym for the work item which is applicable to the change. This field is mandatory for category F, A, B & C CRs for Release 4 and later. A list of work item acronyms can be found in the 3GPP work plan. See 
http://www.3gpp.org/ftp/Specs/html-info/WI-List.htm .

Enter the date on which the CR was last revised.  Format to be interpretable by English version of MS Office® 2003 applications. Prefered format is ISO standard yyyy-MM-dd.

Enter a single letter corresponding to the most appropriate category listed. For more detailed help on interpreting these categories, see Technical Report 21.900 "TSG working methods".

Enter a single release code from the list below.

Enter text which explains why the change is necessary.

Enter text which describes the most important components of the change. i.e. How the change is made.

Enter here the consequences if this CR were to be rejected. It is mandatory to complete this section only if the CR is of category "F" (i.e. correction), though it may well be useful for other categories.

Enter the number of each clause which contains changes.   Be as specific as possible (ie list each subclause, not just the umbrella clause).

Tick "yes" box if any other specifications are affected by this change.  Else tick "no".  You MUST fill in one or the other.

List here the specifications which are affected and the CRs which are linked. This is particularly important where the affected specs belong to a different working group than that which will agree the present CR.

Enter any other information which may be needed by the group being requested to approve the CR. This could include special conditions for it's approval which are not listed anywhere else above.