## Slide 1: MTC cat 0 RRM Test Tolerance analysis strategy
RAN5 #70, Malta
R5-160879

## Slide 2: Overview of test cases
In the following slides the RRM test cases for MTC cat 0 are presented and discussed according to their type and clause.
For some clauses (5, 6, 7) we present suggestions on coming Test Tolerance analysis and for some (8) we raise questions on how to handle the test tolerances.
The aim with the presentation is to agree (partly per clause or fully) on a way forward for the coming Test Tolerance work needed to complete the Work Item.
This document captures the agreed way forward based on R5-160609, the agreements are written in red text below.

## Slide 3: MTC Handover test cases, TS36.521-3, clause 5
There are three MTC cat-0 handover test cases, 5.1.10, 5.1.11 and 5.1.12. All have the same dB values as the legacy intra freq FDD/TDD test cases 5.1.1, 5.1.2 (and 5.1.12) and all test cases are in AWGN.
Since the dB values are identical we suggest to apply the same Test Tolerance and hence no new analysis is needed.
Suggestion endorsed.

## Slide 4: MTC RRC Connection control test cases, TS36.521-3, clause 6
There are three MTC cat-0 RRC Connection Control test cases, 6.1.6, 6.1.7 and 6.1.8. All have the same dB values as the legacy intra freq FDD/TDD test cases 6.1.1, 6.1.3 (and 6.1.5) and all test cases are in AWGN.
Since the dB values are identical we suggest to apply the same Test Tolerance and hence no new analysis is needed.
Suggestion endorsed.

## Slide 5: MTC RLM test cases, TS36.521-3, clause 7
There are 12 MTC cat-0 RLM test cases, 7.3.26 - 7.3.37.
Non of the dB values are similar to any legacy test cases hence these test cases needs separate Test Tolerance analyses.
Suggestion endorsed, new test tolerance analysis needed.

## Slide 6: MTC RRM Measurement test cases, TS36.521-3, clause 8
There are 14 MTC cat-0 RRM Measurement test cases, 8.1.11 - 8.1.22 and 8.2.7, 8.2.8. The test cases have identical dB values and fading condition as the corresponding “legacy” test cases. Test cases are synchronous/asynchronous and with/without DRX. E.g. 8.1.11 same as 8.1.1(“legacy”)
Question: Is it possible to reuse existing test tolerances?
Not possible to reuse since absolute RSRP accuracy is worse for Cat-0 UEs, new TT analysis needed.

## Slide 7: MTC RRM RSRP/RSRQ accuracy test cases, TS36.521-3, clause 9
There are 9 MTC cat-0 RRM RSRP/RSRQ accuracy test cases, 9.1.41.1/2 – 9.1.43.1/2 (RSRP) and 9.2.42 – 9.2.44 (RSRQ)
The test cases does NOT have identical dB (only sub tests1 and 3 are identical) values as the corresponding “legacy” test cases.
However 9.1.41 – 9.1.43 have identical values as has 9.2.42 – 9.2.44.
Question: Is it possible to make one analysis per group, RSRP and RSRQ respectively?
Make absolute and relative tests into one test case (as in 36.133 and as done for the corresponding 3DL CA cases), one TT analysis to be done per group of test cases.