## Slide 1: NR FR2 TT Way Forward
3GPP TSG-RAN WG5 Meeting #81
Spokane, USA, 12th – 16th November 2018
R5-188058
Telecom Italia, Orange, Vodafone, CMCC, China Unicom, Qualcomm, AT&T, Ericsson, NTT DoCoMo, Verizon, Dish, Intel, Apple

## Slide 2: Background
At RAN5 5G-AH#3 New FR2 MU values for IFF method introduced in R5-186344
At RAN5#81 the following contribution regarding TT are presented:
  R5-186888: proposing TT = 0 and highlight Network coverage impact
  R5-187576: defining upper bound for TTs (TT = 2.1 dB)
  R5-187568: proposing basically TT = 0.65xMU
  R5-187235: proposing basically TT = 0.82xMU

## Slide 3: TT NR FR2 Agreement
Except the FFS and empty items, the proposed FR2 TT Values are included in the spreadsheet file, based on the following assumption:
TTs shall be defined case by case
TT = 0.65 * MU (the upper bound of MU value used for TT calculation is 5.5 dB, 0.65 upper bound TT/MU ratio)
  Applies to following Test Cases:
    Min Peak EIRP
    Max TRP
    Reference Sensitivity
TT = 0.50 * MU (the upper bound of MU value used for TT calculation is 0.01ppm , 0.5 upper bound TT/MU ratio)
  Applies to following Test Cases:
    Frequency error
TT = MU for ACLR and SEM it will be updated when the related MU will be finalized
since TT have dependency from MU, no TT value can be defined if the corresponding MU is not finalized (business as usual).
TT values may decrease based on the experience on the field and when all parties will have more confidence in device performance
The TT values and the method to derive the TT defined until RAN5#85 (November 2019) for execution in any possible certification. At RAN5#85 the TT values shall be re-evaluated
  Required actions are specified in editor’s note in Annex F (next slide)

## Slide 4: Agreed Editor’s note to TS 38.521-2 TT Annex F
The TT values defined in this section are valid only until RAN5#85 (November 2019)
RAN5 expects to have the following actions performed by RAN5#85 in efforts to improve the TT values
  For updated TT evaluation only, MU analysis taking into the account the data sheet from commercially available test systems or any additional experimental data to justify the values
  UE vendors’ have supplied further input on TT based on the performance of the existing mmWave UE against the RF test cases
  At least one statistical analysis has been done on possibilities to improve test confidence level
  Measurement results & evaluation of network performance / commercially available devices has been provided