## Slide 1: Multi PDU Session and IMS in SA Option-2 Athens, Greece, RAN5#82
Feb 25, 2019
R5-191665

## Slide 2: Background
A 5GS UE can initiate –
  IMS PDU session only
  Internet PDU session only
  IMS and Internet both (in any order)
  Extra PDU sessions in addition to above
In EUTRA the PDN was part of the “Attach” process and hence it was predictable which PDN was being used by UE, and in which order, as such based on what UE behavior was, the assignment of EPS Bearer ID and DRB id and QFI flows was made
In 5GS, after REGISTRATION complete, UE can trigger any PDU session and the behavior is dynamic and the assignment of corresponding QFI flow, DRB id and QFI\QRI
RRC_IDLE and some key generic procedure like PDU session establishment SHALL account for handling of multi PDU session and the behavior in 5GS preamble shall be made “dynamic” rather than “static”
RF TC doesn’t want to involve IMS signaling during RF tests

## Slide 3: Issues\Solutions & Observation
Issue#1
UE Usage Setting (TS 24.501) --> Indicate to support voice (support any – Voice or Data), Spec reference below, including this IE means UE is configured to support IMS voice
8.2.6.14 UE's usage setting
This IE shall be included if the UE is configured to support IMS voice.
àRAN5 may have to consider the case where this is included and not-included (as well as Account for all devices - No IMS, IMS, Data (or rather voice or no-voice)) but most likely VoPS indication in Registration Accept SHALL be 1.
This is addressed in Registration Accept as VOPS = 1
Definitions for parameters | Per | M | FDDTDD DIFF | FR1 FR2 DIFF
voiceOverEUTRA-5GC Indicates whether the UE supports IMS voice over E-UTRA via 5GC. | UE | No | No | No
voiceOverNR Indicates whether the UE supports IMS voice over NR. It is mandated to the IMS voice capable UE in NR otherwise optional. | UE | No | No | Yes
Observation#1
UE Capability
VoNR - voice over MCG bearer in UE Capability Message
Also capability for FR1, FR2 defined in RAN2 (38.331)
Inter-rat capability for eLTE
No capability for IMS voice for EPS fallback
  Per 38.306 -4.2.13 IMS Parameters
This is addressed by introduction of new PICS for 5G UE support of IMS

## Slide 4: Issues\Solutions & Observation
Issue#2
Order of IMS PDU or Internet in RRC IDLE and other generic procedure–
  Handle IMS, Internet and combination in any order along with both IMS and Internet requested in parallel
  Scale the solution in case more PDU sessions are requested
Possible Solution –
Identify the PDU session, Transaction ID of IMS PDU session, assign it the IMS values (QFI flow, DRB, QoS)
Complete the assignment of PDU session and in parallel handle Internet PDU session
This if the UE only request any order of number of PDU sessions, those can be handled
Have a set table for IMS and Internet PDU assignment which can be mapped once those PDU session are identified.
PICS/PIXIT for UE to declare no. of PDU session supported
One such solution is proposed in R5-191283
Issue#3
RRC_IDLE call flow will depend how the UE sets FoR bit.
RRC Release might be part of the RRC_IDLE procedure, This is not handled in current solution.

## Slide 5: Issues\Solutions & Observation
Observation#2
Test loopback Mode –
Same solution which we had in EN-DC should be fine.
Issue#4
Once common procedure for Issue#2 is agreed, for IMS Registration – Only minor changes needed (For ex)
  24.229 - Re-use it for NR, RAT will use "NR" in PANI header.
  PANI Header - Cell Network Identifier, 5G Cell is 36 bit compared to 28 bit for LTE. Several other places where the RAT setting are needed.
  34.229 can be updated to add 5G RAT and Cell Identity wherever needed in Annexes for Rel-15 5G NR
  MO, MT and EPS Fallback related changes may be required
5.3.2 Close UE test loop
Same as TS 36.509 [6], subclause 5.4.2 with the following exceptions:
- where E-UTRA is mentioned the same applies for NR;
- the NB-IoT mode is out of the scope of the present specification
- where different UE test loop modes are mentioned only those applicable to 5GS should be taken into account (see subclause 5.3.4 for the applicable 5GS UE test loop modes).
- where EPS bearers are mentioned the same applies for 5GS QoS flows; and

## Slide 6: Summary of Multi PDU Session handling
US Usage setting (voice, data, none) is handled
UE Voice Capability may not have impact on RRC_IDLE or RRC_CONNECTED procedures. New PICS will handle UE support of IMS voice for case when VoNR is not supported.
Handling of multi PDU (various requirements) are all handled by dynamic procedure.
Test loopback Modes do not need any change at this time
FoR bit handling is not accounted in preambles
IMS reg procedures and session establishment procedures needs to be updated

## Slide 7: Requirements for RF
Above may have worked for “combined attach” for LTE OR UE’s may not have even configured IMS PDN at all. Since PDN is part of the attach process, the test is run with essentially 1 PDN (non-IMS)
“Activate Test Mode” enables the suppressing of user plane data for 1 PDU (non-IMS).
RF Test Requirement related to signaling –
  Do not allow IMS PDU session or signaling related to IMS PDU session
  Do not allow any data activity from any other PDU session (ex- Internet)
  The outcome of the test is not dependent on no. of PDU session configured.
Handling of above Requirement in LTE
In LTE, RF tests indicated no VOPS allowed based on the pc_Disable_E-UTRA_NOIMSVoIP

## Slide 8: Requirements for RF – 5GC
Same requirements as LTE (Slide-7) are required for 5GC as well. However the solution of NW indicating no VOPS will not work, allowing VOPS for IMS UE’s might also not work, based on below –
  a typical 5G UE, will set the UE Usage setting to “voice centric” as it will support some form of IMS voice (From TS 24.501 cl 4.3.1 and cl 8.2.6.14)
  If we set VOPS=0, from NW side, then as per TS 24.501 cl 4.3.2, we are creating the condition when “IMS voice is not available over 3GPP access”, as such, the outcome of this situation will be – “the UE may disable the N1 mode capability for 3GPP access”.
  If we set VOPS=1 and if IMS PDU is allowed and the “Activate Test Mode” is ON. IMS Reg from UE will be suppresses in this case. However, given the long test duration of RF tests, it is likely that the timer associated with attempting successfully IMS Reg will expire thus again resulting in “IMS voice is not available over 3GPP access” and the outcome - “the UE may disable the N1 mode capability for 3GPP access”. TS 24.501 cl 4.3.2
Thus, the cleanest way to execute RF tests for 5GC capable UE’s will be to not even configure IMS and set some additional “appropriate setting” as such UE stays on NR

## Slide 9: Proposal for executing RF tests – 5GC
Proposal -1
UE’s to be configured with 1 PDU session (non-IMS) with “appropriate settings” to ensure that UE stays on NR after running RRC_CONNECTED or RRC_IDLE procedures from TS 38.508-1, 5GC NR preambles can handle any UE configuration and such this UE type (for ex – 1 internet PDU only), will be handled gracefully.
Some more details on “appropriate setting” could be –
  UE Usage Setting – set to “Data Centric”
  Disable IMS in UE
  Allow\Configure Internet PDU or any other non-IMS PDU session only
  NW will set VOPS indication in REGISTRATION ACCEPT as “1”. As such signaling preambles will have no issues and this will be ignored by UE (Proposal-1).
  Possibly, also ensure SMS settings will not cause unexpected domain selection.
Proposal -2
Test Mode Shall be ON (i.e Activate Test Mode) for all RF tests, this will ensure that user data signaling is suppressed. For ex – if Internet PDU is established, then all the data coming from various applications (for ex – smartphones mobile data)

## Slide 10: Way Forward for Proposal 1,2
Proposal -1
Insert a note to RF_RRC_CONNECTED procedure in TS 38.508-1, “UE’s to be configured with 1 PDU session (non-IMS) with “appropriate settings” to ensure that UE stays on NR after above procedure” OR insert same note in RF Spec (?)
Proposal -2
Specify in RF Test Spec for each TC that Test Mode Shall be ON (i.e Activate Test Mode)