## Slide 1: WF on Noise Impact on RF Measurements for FR2
Keysight Technologies, Anritsu, Rohde & Schwarz
3GPP TSG-RAN5 Meeting #82 R5-192663 Athens, Greece, 25 Feb - 1 Mar 2019

## Slide 2: Background
  RAN5 have been discussing feasibility of RF core requirements for several meetings already.
  Whether a relaxation on test requirements is required to make the test feasible or a tradeoff on MU is needed is being analyzed in a case-by-case base by TE vendors.
  The impact on MU is related to the systematic error due to Influence of noise in each measurement.
  In RAN5#82, 2 papers were presented [1], [2]
  During RAN5#82 off-line discussions, the influence of noise for EIRP spherical coverage was discussed.

## Slide 3: RAN5#82 discussions
Several aspects were discussed regarding influence of noise MU factor:
How the influence of noise for EIRP spherical coverage should be calculated
Influence of noise floor reduction for given use cases
Whether testing Tx off power with relaxation or not testing it due to high relaxation needed
Assumptions for ACLR influence of noise analysis

## Slide 4: EIRP spherical coverage- Calculation of influence of noise
Values provided by TE vendors so far were related to the SNR inferred at the EIRP spherical coverage limit for a given band.
Above approach could be improved if the influence of noise is taken into account for each measurement included in the spherical coverage test and then the appropriate analysis is done according to the statistics used to calculate the EIRP spherical coverage instead of considering only the SNR at the EIRP spherical coverage limit
  There is a dependency with UE CDF curve as the influence of noise will be higher on low EIRP values than in high EIRP ones.
  Some assumptions are needed from UE vendors if simulations are needed based on this improved approach

## Slide 5: Influence of noise floor reduction for given use cases
TE design requires a low noise amplifier (LNA) to allow the measurement of low EIRP/TRP values.
Current core requirements define a max EIRP for a PC3 device of 43 dBm.
Depending on TE design, there is a risk that LNA gets into compression mode if UL max EIRP is above a given level (X), what causes the MU increase significantly.
Once the final influence of noise is calculated, if influence of noise is too high, several options should be considered:
  Additionally split influence of noise per channel bandwidth value
  Additionally split influence of noise per UL max EIRP value. Three options are currently under study on how to consider this max EIRP split:
    Option 1: Limit max EIRP value to X in test requirements
    Option 2: Require a manufacturer declaration on max EIRP
    Option 3: Perform a pre-test to double check LNA is not saturated
      Issue: this pre-test would be also affected by MU

## Slide 6: Tx off power testing
According to [1] and [2], different results have been obtained for SNR for TX off power.
Two options have been proposed:
  Option 1: Test Tx OFF power with relaxation
  Option 2: Not to test Tx Off power
 |  | Anritsu R5-191794 |  |  |  | R&S R5-192125 |  |  | 
Test case | Applicable Frequency Range[GHz] | UL signal level [dBm] | Estimated SNR for total component [dB] | Proposed ΔSNR | Proposed relaxation of test requirement | UL signal level [dBm] | Estimated SNR for total component [dB] | ΔSNR | Proposed relaxation of test requirement
Off power | 23.45 GHz ≤ f ≤ 32.125 GHz | -35dBm/ChBW | -18 | 0.41 | 28.0 - DChBW | -35dBm/ChBW | -30.9 | 30.9 | do not test
 | 32.125 GHz < f ≤ 40.8 GHz |  | -26.1 | 0.41 | 36.1 - DChBW |  | -34.7 | 34.7 | do not test

## Slide 7: Assumptions on ACLR influence of noise
ACLR requirement
Wanted channel TRP
Adjacent channel TRP
TRP power
Frequency
Assumption for min TRP power value on wanted channel shall be:
  min EIRP – 16 dB (UE antenna (8x2) directivity)
Assumption for min TRP power value on adjacent channel shall be:
  min EIRP – 16 dB (UE antenna (8x2) directivity) – ACLR requirement

## Slide 8: Agreement and Proposal
Test case | Applicable Frequency Range[GHz] | Assumed UL signal level [dBm] | Maximum EIRP EIRPmax | ΔSNR[dB] (ChBW=400MHz) | Relaxation of test requirement [dB]
MOP (Min Peak EIRP, PC3) | 23.45GHz ≤ f ≤ 32.125 GHz | 20.7dBm/ChBW (22.4 – 1.7) | EIRPmax ≤ 43 dBm | 0.1 | 0.0
 | 32.125 GHz ≤ f ≤ 40.8 GHz | 18.9dBm/ChBW (20.6 – 1.7) | EIRPmax ≤ 43 dBm | 0.3 | 0.0
MOP (TRP, PC3) | 23.45GHz ≤ f ≤ 32.125 GHz | 23dBm/ChBW | [33] dBm < EIRPmax ≤ 43 dBm | TBD | TBD
 |  |  | EIRPmax ≤ [33] dBm | 0.1 | 0.0
 | 32.125 GHz ≤ f ≤ 40.8 GHz | 23dBm/ChBW | [33] dBm < EIRPmax ≤ 43 dBm | TBD | TBD
 |  |  | EIRPmax ≤ [33] dBm | 0.3 | 0.0
∆SNR[dB] =
SNRtotal [dB] = <UL signal level>[dBm] – <Noise per single polarization>[dBm/400MHz] – 3 + ∆ChBW
∆ChBW =
ΔSNR and Relaxation of test requirement in Table 1 is proposed to be applicable for
PC3
Channel Bandwidth ≤ 400MHz
DUT size ≤ 15 cm and DUT size ≤ 30 cm
Table 1 : ΔSNR and Relaxation of test requirement
Proposal 1: For PC3 UE, no test requirement limit relaxation for MOP (Min peak EIRP)
Proposal 2: For PC3 UE, Influence of noise in MOP-min EIRP=
  0.1 dB for 23.45 GHz ≤ f ≤ 32.125 GHz (for CBW ≤ 400 MHz and max EIRP≤43 dBm)
  0.3 dB for 32.125 GHz ≤ f ≤ 40.8 GHz (for CBW ≤ 400 MHz and max EIRP≤43 dBm)
Proposal 3: For PC3 UE, Influence of noise in MOP-TRP=
  0.1 dB for 23.45 GHz ≤ f ≤ 32.125 GHz (for CBW ≤ 400 MHz )
  0.3 dB for 32.125 GHz ≤ f ≤ 40.8 GHz (for CBW ≤ 400 MHz )
  only for max EIRP ≤ [33] dBm
Notes: Type equation here.
"Type equation here."

## Slide 9: Assumptions agreement
Use slide 7 as power level assumptions for ACLR influence of noise analysis

## Slide 10: WF on noise impact and test feasibility
  Maximum Output Power (EIRP spherical coverage):
    UE vendors to provide an acceptable assumption for the CDF curve by RAN5#5-5G-NR Adhoc
    TE vendors to provide simulations on influence of noise for EIRP spherical coverage based on above assumption by RAN5#83
    Consider split on channel BW and max EIRP to keep the influence of noise acceptable for some cases
  Complete analysis of other P1 and P2 test cases by RAN5#5-5G-NR Adhoc
  Industry input requested on:
    Slide 5 Option 1: Acceptable limit for max EIRP in test requirements (X)
    Slide 5 Option 2: Require a manufacturer declaration on max EIRP
    Slide 6: Whether to test transmit OFF Power with relaxation or not to test.

## Slide 11: References
[1] | R5-191794, “SNR estimation update for FR2 priority 1 and 2 TRx TCs”, Anritsu, 3GPP TSG-RAN5 Meeting#82, Athens, Feb 2019
[2] | R5-192125, “On the SNR for FR2 TRx test cases”, Rohde & Schwarz, 3GPP TSG-RAN5 Meeting#82, Athens, Feb 2019