## Slide 1: NR FR2 WF on MB relaxation
Apple, Inc.
3GPP TSG-RAN WG5 Meeting #83 R5-194122
Reno, USA, 13th May 2019 - 17th May 2019
Agenda Item : 5.3.5.17
Document for : Discussion and Endorsement

## Slide 2: Agreements / Assumptions
Based on RAN4 LS (R5-192901), RAN5 applies MB relaxation into conformance test with following assumptions except for verdict for certification / validation.
  MB relaxation value for each FR2 band are based on “UE declaration”.
  “Verdict per band”, which is same approach as legacy LTE.
Time plan
  Pre meeting discussions : 1) Proposed approach to remaining issues, 2) Raise additional issues
  [RAN5#83] (May-2019): CR implementation to reflect agreements in this WF, Completion target of MB relaxation except for MU, TT
Process of UE declaration (Definition of verdict is TBD.)
  UE manufacturers declare each MB relaxation value to satisfy core requirement.
  Test houses, labs implement declared value into TE by manual since there is no capability for this relaxation.
  TE concludes verdict considering implemented declared value.

## Slide 3: Remaining issues [1/3]
UE declaration
  1-1 How to declare MB relaxation value
    Option 1 TS 38.522
    Option 2 TS 38.508-2.
    1-2 Whether declared value can be updated
    Option 1 : UE declared value shall not be updated.
    Option 2 : UE declared value can be modified during UE development period.
  Definition of Verdict
    Whether testing all FR2 bands at the same time with same TE is required?
MU, TT, SNR estimation
  3-1 Whether MUMB = MUSB for each TC.
  3-2 Whether TTMB = TTSB for each TC.
  3-3 Whether SNR estimation is required for MB TCs (or estimation of SB can be resued to MB TCs)
Impact on certification bodies
  After completion of RAN5 work, we will send LS to certification bodies (e.g. GCF CAG, PTCRB).

## Slide 4: Remaining issues [2/3]
Spe structure
4-1 Test applicability for each TC (TC without MB relaxation and TC with MB relaxation)
4-2 Test procedure for MB should be updated. Whether following points to be captured in the procedure.
1) Process of UE declaration
2) Process of implementing declared value into TE
3) Other
4-3 Description of test requirement
How to apply MB relaxation into test requirement. (e.g. 22.4 – TT – MB)?
4-4 TCs, Annex F (TS 38.521-2), TCs (TS 38.521-3), and applicability spec (TS 38.522) should be updated accordingly.
4-5 Whether additional TCs for MB relaxation are required except for TCs captured in the latest WP - MOP (EIRP, TRP, SC), MPR, A-MPR, configured output power, [ACLR?]…
TE Implementation
5-1 Whether should discuss this topic in RAN5 (or this topic should be TE implementation matter.)
5-2 Necessity to capture supporting FR2 bands and declared relaxation value for all FR2 bands.
[E.g.] UE supports 3 FR2 bands (n257, n260, n261), and conduct n257 testing.
TC : MOP (Spherical Coverage, MB FR2 bands)
Verdict : PASS (Band n257)
Declared relaxation value : 0.3 dB (n257), 0.1 dB (n260), 1.0dB (n261)
Certification/Validation
6-1 After completion of RAN5 work, it is required to send LS to certification bodies (e.g. GCF CAG, PTCRB).

## Slide 5: Spec structure
TCs of transmit power to be divided as below based on the latest WP of TS 38.521-2.
  Contents of TRP (6.2.1.1) and TRP (6.2_1.1.1) are completely same since there is no MB relaxation.
    6.2.1.1 : UE maximum output power - EIRP and TRP
    6.2.1.2 : UE maximum output power - Spherical coverage
    6.2.2 : UE maximum output power reduction
    6.2.3 : UE maximum output power with additional requirements
    6.2.4 : Configured transmitted power
    6.2_1.1.1 : UE maximum output power - EIRP and TRP with multi-band relaxation
    6.2_1.1.2 : UE maximum output power - Spherical coverage with multi-band relaxation
    6.2_1.2 : UE maximum output power reduction with multi-band relaxation
    6.2_1.3 : UE maximum output power with additional requirements with multi-band relaxation
    6.2_1.4 : Configured transmitted power with multi-band relaxation