## Slide 1: Discussion on handling of HP-UE requirements in FR1
Huawei, HiSilicon, CMCC
3GPP TSG-RAN5 Meeting #86-e R5-200395
Electronic Meeting, 17 - 28 Feb 2020

## Slide 2: Background for power class related requirements
Test cases with power class specific requirements – impacted by power class directly
  MOP, MPR, A-MPR, ACLR, Configured output power
Test cases with common requirements, ran at Pumax –impacted by power class indirectly
  Relative power control, Frequency Error, EVM, OBW, SEM, SE, SE-co-existence, A-SE, Transmit intermodulation
PC2 dropping back to PC3
  P-max <= 23dBm
  Percentage of uplink symbols > maxUplinkDutyCycle or 50% (NOTE 1)
NOTE 1: maxUplinkDutyCycle is UE capability which ranges from 60%~100%

## Slide 3
Proposal 1: All the mentioned test cases shall be tested firstly based on the UE’s power class capability.
  PC3 UE shall be verified based on 23dBm MOP; PC2 UE shall be verified based on 26dBm MOP
  Test configurations and default parameters shall ensure above requirement
    Default P-max is ‘Not present’ (Defined in 38.508-1)
    For PC2, the percentage of uplink symbols is less than 50% according to RMC. (Ensured by RMC definition)

## Slide 4
Proposal 2: For test cases with PC specific requirements, PC2 UEs shall also be verified with PC3 requirements; For test cases with common requirements, PC2 UEs don’t need additional PC3 testing.
  For the test cases MOP, MPR, A-MPR, configured output power and ACLR, the PC3 requirements are different from PC2. In order to make sure PC2 UE is conformant when it drops back to PC3, the additional test points shall be added.
  In test procedure, it shall be explicitly required that PC2 UE verifies PC3 requirement.
  Adding parameter exception to ensure PC2 UE drops back to PC3
    P-max = 23dBm

## Slide 5
Proposal 3: For test cases with PC specific requirements, define a separate test case for PC2 UEs with a suffix of ‘_1’.
  In LTE there are different test cases for PC3 and PC2/PC1 requirements.
  From GCF’s point of view, it would be more convenient to organize the WI with separate test cases for UEs of different power classes.
  From lab’s point of view, it would be more clear to know for each power class which test procedures, messages and requirements shall be considered.
  New test cases would be as below:
    6.2.1_1 UE maximum output power for HPUE
    6.2.2_1 UE maximum output power reduction for HPUE
    6.2.3_1 UE additional maximum output power reduction for HPUE
    6.2.4_1 Configured transmitted power for HPUE
    6.5.2.4.1_1 NR ACLR for HPUE
  New test cases will only take care of 26dBm requirements and only apply to PC2 UE.
  ‘Old’ test cases will cover 23dBm requirement and apply to PC3 and PC2 UE.

## Slide 6
Proposal 4: Power class 2 is also defined for UL-MIMO. The same principle shall apply for relevant UL-MIMO testing.
Proposal 5: PC1 requirements is already introduced in R16. The same principle shall apply for PC1 testing.

## Slide 7
Proposal 1: All the mentioned test cases shall be tested firstly based on the UE’s power class capability.
Proposal 2: For test cases with PC specific requirements, PC2 UEs shall also be verified with PC3 requirements; For test cases with common requirements, PC2 UEs don’t need additional PC3 testing.
Proposal 3: For test cases with PC specific requirements, define a separate test case for PC2 UEs with a suffix of ‘_1’.
Proposal 4: Power class 2 is also defined for UL-MIMO. The same principle shall apply for relevant UL-MIMO testing.
Proposal 5: PC1 requirements is already introduced in R16. The same principle shall apply for PC1 testing.
Summary